TAQOZ Quick Reference

for Parallax P2

Interpreter

The console interpreter looks for words and numbers delimited by whitespace. Everything is interpreted as a word or a number. Numbers are pushed onto the stack. Words are looked up and compiled or acted upon immediately. Names of words are limited to 31 characters. All words can be used interpretively including IF BEGIN DO LOOP etc

Data and the stack

The data stack (S:) is directly accessible and has 32 32-bit cells for holding numerical values. Functions get their arguments from the stack and leave their results there as well. There is also a return address stack (R:) that can be used for temporary storage or preferably the aux data stack.

Notation

n, n1, n2, n3	Single-cell integers (16-bit).
u, u1, u2	Unsigned integers (16-bit).
x, x1, x2, x3	Single-cell item (16-bit).

c	Character value (8-bit).
d ud	Double-cell signed and unsigned (32-bit).
t ut	Triple-cell signed and unsigned (48-bit).
q uq	Quad-cell signed and unsigned (64-bit).

f	Boolean	ag: 0 is false, -1 is true.
flt flt1 flt3	Floating-point value (32-bit).

PIC24-30-33 only, with build option.
addr, addr1, addr2	16-bit addresses.
a-addr	cell-aligned address.
c-addr	character or byte address.

Numbers and values

Leave integer two onto the stack. ( -- 2 )
#255Leave decimal 255 onto the stack. ( -- 255 )
%11Leave integer three onto the stack. ( -- 3 )
$10Leave integer sixteen onto the stack. ( -- 16 )

Leave double number on the stack. ( -- 23 0 ) decimal Set number format to base 10. ( -- )
hexSet number format to hexadecimal. ( -- )
binSet number format to binary. ( -- )

s>dSign extend single to double number. ( n -- d ) Since double numbers have the most signi cant bits in the cell above the least signi cant bits, you can just drop the top cell to recover the single number, provided that the value is not too large to t in a single cell.

d>qExtend double to quad-cell number. ( d -- q ) Requires qmath.h to be loaded. PIC18, PIC24-30-33.

Displaying data

Display a number. ( n -- )

Display u unsigned. ( u -- )

u.r	Display u with	eld width n, 0 < n < 256. ( u n -- )

Display double number. ( d -- )

ud.	Display unsigned double number. ( ud -- )

.s	Display stack content (nondestructively).

.st	Emit status string for base, current data section, and display the stack contents. ( -- )

Display content at address. ( addr -- ) PIC24-30-33 dump Display memory from address, for u bytes. ( addr u -- )

Stack manipulation

dup	Duplicate top item. ( x -- x x )

?dup	Duplicate top item if nonzero. ( x -- 0 | x x )

swap	Swap top two items. ( x1 x2 -- x2 x1 )

over	Copy second item to top. ( x1 x2 -- x1 x2 x1 )

drop	Discard top item. ( x -- )

nip	Remove x1 from the stack. ( x1 x2 -- x2 )

rot Rotate top three items. ( x1 x2 x3 -- x2 x3 x1 ) tuck Insert x2 below x1 in the stack. ( x1 x2 -- x2 x1 x2 ) pick Duplicate the u-th item on top.

( xu ... x0 u -- xu ... x0 xu )

2dup	Duplicate top double-cell item. ( d -- d d )

2swap	Swap top two double-cell items. ( d1 d2 -- d2 d1 )

2over	Copy second double item to top. ( d1 d2 -- d1 d2 d1 )

2drop	Discard top double-cell item. ( d -- )

>r	Send to return stack. S:( n -- ) R:( -- n )

r>	Take from return stack. S:( -- n ) R:( n -- )

r@	Copy top item of return stack. S:( -- n ) R:( n -- n )

rdrop	Discard top item of return stack. S:( -- ) R:( n -- )

sp@	Leave data stack pointer. ( -- addr )

sp!	Set the data stack pointer to address. ( addr -- )

Operators

Arithmetic with single-cell numbers

Some of these words require core.txt and math.txt.
Add. ( n1 n2 -- n1+n2 ) sum

Subtract. ( n1 n2 -- n1-n2 ) di erence
*Multiply. ( n1 n2 -- n1*n2 ) product
/Divide. ( n1 n2 -- n1/n2 ) quotient

mod Divide. ( n1 n2 -- n.rem ) remainder /mod Divide. ( n1 n2 -- n.rem n.quot )

u/ Unsigned 16/16 to 16-bit division. ( u1 u2 -- u2/u1 ) u/mod Unsigned division. ( u1 u2 -- u.rem u.quot )

16-bit/16-bit to 16-bit

1Leave one. ( -- 1 )

1+ Add one. ( n -- n1 )

1- Subtract one. ( n -- n1 )

2+ Add two. ( n -- n1 )

2- Subtract 2 from n. ( n -- n1 )

2* Multiply by 2; Shift left by one bit. ( u -- u1 ) 2/ Divide by 2; Shift right by one bit. ( u -- u1 )

*/	Scale. ( n1 n2 n3 -- n1*n2/n3 )

Uses 32-bit intermediate result.

*/mod	Scale with remainder. ( n1 n2 n3 -- n.rem n.quot ) Uses 32-bit intermediate result.

u*/mod	Unsigned Scale u1*u2/u3 ( u1 u2 u3 -- u.rem u.quot ) Uses 32-bit intermediate result.

abs	Absolute value. ( n -- u )

negate	Negate n. ( n -- -n )

?negate	Negate n1 if n2 is negative. ( n1 n2 -- n3 )

min	Leave minimum. ( n1 n2 -- n )

max	Leave maximum. ( n1 n2 -- n )

umin	Unsigned minimum. ( u1 u2 -- u )

umax	Unsigned maximum. ( u1 u2 -- u )

Arithmetic with double-cell numbers

Some of these words require core.txt, math.txt and qmath.txt. d+ Add double numbers. ( d1 d2 -- d1+d2 ) d- Subtract double numbers. ( d1 d2 -- d1-d2 )

m+	Add single cell to double number. ( d1 n -- d2 )

m*	Signed 16*16 to 32-bit multiply. ( n n -- d )

d2*	Multiply by 2. ( d -- d )

d2/	Divide by 2. ( d -- d )

um*	Unsigned 16x16 to 32 bit multiply. ( u1 u2 -- ud )

ud*	Unsigned 32x16 to 32-bit multiply. ( ud u -- ud )

um/mod	Unsigned division. ( ud u1 -- u.rem u.quot )

32-bit/16-bit to 16-bit

ud/mod	Unsigned division. ( ud u1 -- u.rem ud.quot ) 32-bit/16-bit to 32-bit

fm/mod	Floored division. ( d n -- n.rem n.quot )

sm/rem	Symmetric division. ( d n -- n.rem n.quot )

32-bit/16-bit to 16-bit.

m*/	Scale with triple intermediate result. d2 = d1*n1/n2 ( d1 n1 n2 -- d2 )

um*/	Scale with triple intermediate result. ud2 = ud1*u1/u2 ( ud1 u1 u2 -- ud2)

dabs	Absolute value. ( d -- ud )

dnegate	Negate double number. ( d -- -d )

?dnegate	Negate d if n is negative. ( d n -- -d )

Arithmetic with triple- and quad-numbers

For PIC18, these words require core.txt, math.txt and qmath.txt.

q+	Add a quad to a quad. ( q1 q2 -- q3 )

For PIC24-30-33.

qm+	Add double to a quad. ( q1 d -- q2 )

For PIC18 and PIC24-30-33.

uq*	Unsigned 32x32 to 64-bit multiply. ( ud ud -- uq ) For PIC18 and PIC24-30-33.

ut*	Unsigned 32x16 to 48-bit multiply. ( ud u -- ut )

ut/	Divide triple by single. ( ut u -- ud )

uq/mod	Divide quad by double. ( uq ud -- ud-rem ud-quot )
Relational
Leave true if x1 x2 are equal. ( x1 x2 -- f )

<>	Leave true if x1 x2 are not equal. ( x1 x2 -- f )

Leave true if n1 less than n2. ( n1 n2 -- f )

Leave true if n1 greater than n2. ( n1 n2 -- f )

0=Leave true if n is zero. ( n -- f ) Inverts logical value.
0<Leave true if n is negative. ( n -- f )

within Leave true if xl <= x < xh. ( x xl xh -- f )

u< Leave true if u1 < u2. ( u1 u2 -- f ) u> Leave true if u1 > u2. ( u1 u2 -- f )

d= Leave true if d1 d2 are equal. ( d1 d2 -- f ) d0= Leave true if d is zero. ( d -- f )

d0< Leave true if d is negative. ( d -- f ) d< Leave true if d1 < d2. ( d1 d2 -- f ) d> Leave true if d1 > d2. ( d1 d2 -- f )

Bitwise
invert	Ones complement. ( x -- x )

dinvert	Invert double number. ( du -- du )

and	Bitwise and. ( x1 x2 -- x )

or	Bitwise or. ( x1 x2 -- x )

xor	Bitwise exclusive-or. ( x -- x )

lshift	Left shift by u bits. ( x1 u -- x2 )

rshift	Right shift by u bits. ( x1 u -- x2 )
AVR8 Memory map

All operations are restricted to 64kB byte address space that is divided into:
$0000 { (RAMSIZE-1)	SRAM

RAMSIZE { (RAMSIZE+EEPROMSIZE-1)	EEPROM

($ffff-FLASHSIZE+1) { $ffff	Flash

The SRAM space includes the IO-space and special function registers. The high memory mark for the Flash context is set by the combined size of the boot area and FF kernel.

Memory Context

ram	Set address context to SRAM. ( -- )

eeprom	Set address context to EEPROM. ( -- )

flash	Set address context to Flash. ( -- )
fl-	Disable writes to Flash, EEPROM. ( -- )

fl+	Enable writes to Flash, EEPROM, default. ( -- )

iflush	Flush the	ash write bu er. ( -- )

here	Leave the current data section dictionary

pointer. ( -- addr )

align	Align the current data section dictionary

pointer to cell boundary. ( -- )

hi	Leave the high limit of the current

data space. ( -- u )

The following come from bit.txt
bit1: name	De ne a word to set a bit. ( addr bit -- )

bit0: name	De ne a word to clear a bit. ( addr bit -- )

bit?: name	De ne a word to test a bit. ( addr bit -- )

When executed, name leaves a	ag. ( -- f )

The Dictionary

Dictionary management

marker -my-mark	Mark the dictionary and memory

allocation state with -my-mark.
-my-mark	Return to the dictionary and allotted-memory

state that existed before -my-mark was created.

find name	Find name in dictionary. ( -- n )

Leave 1 immediate, -1 normal, 0 not found.

forget name	Forget dictionary entries back to name.

empty	Reset all dictionary and allotted-memory

pointers. ( -- )

words	List words in dictionary. ( -- )

Memory

Typically, the microcontroller has three distinct memory contexts: Flash, EEPROM and SRAM. FlashForth uni es these memory spaces into a single 64kB address space.

PIC18 Memory map

The address ranges are:
$0000 { $ebff	Flash

$ec00 { $efff	EEPROM

$f000 { $ff5f	SRAM, general use

$ff60 { $ffff	SRAM, special function registers

The high memory mark for each context will depend on the particular device used. Using a PIC18F26K22 and the default values in p18f-main.cfg for the UART version of FF, a total of 423 bytes is dedicated to the FF system. The rest (3473 bytes) is free for application use. Also, the full 64kB of Flash memory is truncated to t within the range speci ed above.

PIC24 Memory map

A device with EEPROM will have its 64kB address space divided

into:	{ $07ff	SRAM, special function registers
$0000
$0800	{ ($0800+RAMSIZE-1)	SRAM, general use
($0800+RAMSIZE) { $fbff		Flash
$fc00 { $ffff		EEPROM

The high memory mark for the Flash context will depend on the device. Also, the full Flash memory of the device may not be accessible.

Accessing Memory

Store x to address. ( x a-addr -- )
@Fetch from address. ( a-addr -- x )

@+Fetch cell and increment address by cell size. ( a-addr1 -- a-addr2 x )

2! Store 2 cells to address. ( x1 x2 a-addr -- ) 2@ Fetch 2 cells from address. ( a-addr -- x1 x2 )

c! Store character to address. ( c addr -- ) c@ Fetch character from address. ( addr -- c ) c@+ Fetch char, increment address.

( addr1 -- addr2 c )

+! Add n to cell at address. ( n addr -- ) -@ Fetch from addr and decrement addr by 2.

( addr1 -- addr2 x )

cf! Store to Flash memory. ( dataL dataH addr -- ) PIC24-30-33 only.

cf@ Fetch from Flash memory. ( addr -- dataL dataH ) PIC24-30-33 only.

>a Write to the A register. ( x -- ) a> Read from the A register. ( -- x )

Accessing bits in RAM

mset	Set bits in	le register with mask c. ( c addr -- )

For PIC24-30-33, the mask is 16 bits.

mclr	Clear bits in	le register with mask c. ( c addr -- )

mtst	AND	le register byte with mask c. ( c addr -- x )

De ning constants and variables

constant name	De ne new constant. ( n -- )

2constant name	De ne double constant. ( x x -- )

name	Leave value on stack. ( -- n )

variable varname	De ne a variable in the current data

section. ( -- )

Use ram, eeprom or flash to set data section.

2variable name	De ne double variable. ( -- )

varname	Leave address on stack. ( -- addr )

value valname	De ne value. ( n -- )

to valname	Assign new value to valname. ( n -- )

valname	Leave value on stack. ( -- n )

user name	De ne a user variable at o set +n. ( +n -- )

Examples

ram	Set SRAM context for variables and

values. Be careful not to accidentally

de ne variables in EEPROM or Flash

memory. That memory wears quickly

with multiple writes.
$ff81 constant portb	De ne constant in Flash.
3 value xx	De ne value in SRAM.
variable yy	De ne variable in SRAM.
6 yy !	Store 6 in variable yy.
eeprom 5 value zz ram	De ne value in EEPROM.
xx yy zz portb yy @	Leaves 3 f172 5 ff81 6

warm	Warm restart clears SRAM data.
xx yy zz portb yy @	Leaves 0 f172 5 ff81 0
4 to xx	Sets new value.
xx yy zz portb yy @	Leaves 4 f172 5 ff81 0
hi here - u.	Prints the number of bytes free.
$ff8a constant latb	PortB latch for the PIC18.
$ff93 constant trisb	PortB direction-control register.
%00000010 trisb mclr	Sets RB1 as output.
latb 1 bit1: pb1-high	De nes a word to set RB1 high.
pb1-high	Sets RB1 high.

De ning compound data objects

create name	Create a word de nition and store

the current data section pointer.

does>	De ne the runtime action of a created word.

allot	Advance the current data section dictionary

pointer by u bytes. ( u -- )

Append x to the current data section. ( x -- )

c, Append c to the current data section. ( c -- ) ," xxx" Append a string at HERE. ( -- )
i,Append x to the ash data section. ( x -- )
ic,Append c to the ash data section. ( c -- )

cf, Compile xt into the ash dictionary. ( addr -- ) c>n Convert code eld addr to name eld addr.

( addr1 -- addr2 )

n>c Convert name eld addr to code eld addr. ( addr1 -- addr2 )

n>l Convert nfa to lfa. ( nfa -- lfa ) Not implemented; use 2- instead.

>bodyLeave the parameter eld address of the created word. ( xt -- a-addr )

:noname De ne headerless forth code. ( -- addr )

>xa Convert a Flash virtual address to a real executable address. PIC24-30-33, ATmega ( a-addr1 -- a-addr2 )

xa> Convert a real executable address to a Flash virtual address. PIC24-30-33, ATmega ( a-addr1 -- a-addr2 )

Array examples

: mk-byte-array		De ning word ( n -- )
	create allot	...to make byte array objects
	does> + ;	...as shown in FF user’s guide.
10	mk-byte-array my-bytes	Creates an array object
		my-bytes ( n -- addr ).
18	0 my-bytes c!	Sets an element
21	1 my-bytes c!	...and another.
255 2 my-bytes c!
2 my-bytes c@		Should leave 255.
: mk-cell-array		De ning word ( n -- )
	create cells allot	...to make cell array objects.
	does> swap cells + ;
5 mk-cell-array my-cells		Creates an array object
		my-cells ( n -- addr ).

3000 0 my-cells !		Sets an element
45000 1	my-cells !	...and another.
63000 2	my-cells !
1 my-cells @ .		Should print 45000

Memory operations

Some of these words come from core.txt.
cmove	Move u bytes from address-1 to address-2.

( addr1 addr2 u -- )

Copy proceeds from low addr to high address.

wmove	Move u cells from address-1 to address-2.

addr1 addr2 u -- ) PIC24-30-33 only
fillFill u bytes with c starting at address.

addr u c -- )
eraseFill u bytes with 0 starting at address.

addr u -- )

blanks Fill u bytes with spaces starting at address.

addr u -- )

cellsConvert cells to address units. ( u -- u )
charsConvert chars to address units. ( u -- u )
char+Add one to address. ( addr1 -- addr2 )

cell+ Add size of cell to address. ( addr1 -- addr2 ) aligned Align address to a cell boundary. ( addr -- a-addr )

Prede ned variables

base	Variable containing number base. ( -- a-addr )

irq	Interrupt vector (SRAM variable). ( -- a-addr ) Always disable user interrupts and clear

related interrupt enable bits before zeroing interrupt vector.

di false to irq ei

turnkey	Vector for user start-up word. ( -- a-addr ) EEPROM value mirrored in SRAM.

prompt	Deferred execution vector for the info displayed by quit. Default value is .st ( -- a-addr )

’emit	EMIT vector. Default is tx1 ( -- a-addr )

’key	KEY vector. Default is rx1 ( -- a-addr )

’key?	KEY? vector. Default is rx1? ( -- a-addr )

’source	Current input source. ( -- a-addr )

s0	Variable for start of data stack. ( -- a-addr )

r0	Bottom of return stack. ( -- a-addr )

rcnt	Number of saved return stack cells. ( -- a-addr )

tib	Address of the terminal input bu er. ( -- a-addr )

tiu	Terminal input bu er pointer. ( -- a-addr )

>in	Variable containing the o set, in characters,

from the start of tib to the current

parse area. ( -- a-addr )

pad	Address of the temporary area for strings. ( -- addr ) : pad tib ti# + ;

Each task has its own pad but has zero default size. If needed the user must allocate it separately with allot for each task.

dp	Leave the address of the current data section dictionary pointer. ( -- addr )

EEPROM variable mirrored in RAM.

dps	End address of dictionary pointers. ( -- d )

Absolute address of start of free Flash. Library and C code can be linked, starting at this address. PIC24, dsPIC33

hp	Hold pointer for formatted numeric output.

( -- a-addr )

up Variable holding a user pointer. ( -- addr ) latest Variable holding the address of the latest de ned word. ( -- a-addr )

float?	Interpreter defer for parsing	oating-point values.

’ >float is float? PIC24-30-33 only

ram		Example
create my-array	20 allot	...of creating an array,
my-array 20 $ff fill		... lling it with 1s, and
my-array 20 dump		...displaying its content.
create my-cell-array
100 , 340 ,	5 ,	Initialised cell array.
my-cell-array 2	cells + @	Should leave 5. ( -- x )
create my-byte-array
18 c, 21 c,	255 c,	Initialised byte array.
my-byte-array 2	chars + c@	Should leave 255. ( -- c )

Prede ned constants

cell	Size of one cell in characters. ( -- n )

true	Boolean true value. ( -- -1 )

false	Boolean false value. ( -- 0 )

bl	ASCII space. ( -- c )

Fcy	Leave the cpu instruction-cycle frequency in kHz. ( -- u )

ti#	Size of the terminal input bu er. ( -- u )

Floating-point for PIC24-30-33

These words require that FlashForth has been built with the .eq FLOATS, 1 option in the relevant processor con g le. >float Convert a string into a oat. ( c-addr u -- flt f )

Note that it works for decimal base only. Examples: 1e10 -1e10 1.234e10 -1.234e10

Print in decimal format. ( flt -- )
fe.Print in engineering format. ( flt -- )
fs.Print in scienti c format. ( flt -- )

fdrop	Discard top	oat item. ( flt -- )

fdup	Duplicate top	oat item. ( flt -- flt flt )

fover	Copy second	oat item to top.

( flt1 flt2 -- flt1 flt2 flt1 )

fswap Swap top two oat items. ( flt1 flt2 -- flt2 flt1 ) frot Rotate top three oat items.

( flt1 flt2 flt3 -- flt2 flt3 flt1 )

fnip Remove second top oat. ( flt1 flt2 -- flt2 ) ftuck Insert flt2 below flt1.

( flt1 flt2 -- flt2 flt1 flt2 )

nfswap	Swap	oat and single. ( flt n -- n flt )

fnswap	Swap	oat and single. ( n flt -- flt n )

nfover	Copy	oat item over single. ( flt n -- flt n flt )

fnover	Copy single over	oat item. ( n flt -- n flt n)

f@	Fetch	oat item to stack. ( addr -- flt )

f!	Store	oat item to address. ( flt addr -- )

fconstant name	De ne constant. ( flt -- )

fvariable name	De ne variable. ( -- )

fliteral		Compile in literal value. ( flt -- )
f0		Leave value 0.0 on stack. ( -- flt )
f1		Leave value 1.0 on stack. ( -- flt )
f10		Leave value 10.0 on stack. ( -- flt )
f0.5		Leave value 0.5 on stack. ( -- flt )
s>f	Convert single to oat. ( n -- flt )
d>f	Convert double to oat. ( d -- flt )
f>s	Convert oat to single. ( flt -- n )
f>d	Convert oat to double. ( flt -- d )
f0=	Leave true if flt equal to zero. ( flt -- f )
f0<	Leave true if flt less than zero. ( flt -- f )
f=	Leave true if oats are equal. ( flt1 flt2 -- f )
f<	Leave true if flt1 less than flt2. ( flt1 flt2 -- f )
f<=	eave true if flt1 less than or equal to flt2.
	( flt1 flt2 -- f )
f>	Leave true if flt1 greater than flt2.
	( flt1 flt2 -- f )
f>=	Leave true if flt1 greater than or equal to flt2.
	( flt1 flt2 -- f )
fnegate Negate oat value. ( flt -- -flt )
fabs		Leave absolute value. ( flt1 -- flt2 )
fround		Round to nearest integral value. ( flt1 -- flt2 )
fmin		Leave minimum. ( flt1 flt2 -- flt )
fmax		Leave maximum. ( flt1 flt2 -- flt )
f2*	Multiple by 2. ( flt -- flt*2)
f2/	Divide by 2. ( flt -- flt/2 )

The following functions call out to the Microchip math library. f+ Addition ( flt1 flt2 -- flt1+flt2 )
f-	Subtraction ( flt1 flt2 -- flt1-flt2 )

f*	Multiplication ( flt1 flt2 -- flt1*flt2 )

f/	Division ( flt1 flt2 -- flt1/flt2 )

fpow	Power. ( flt1 flt2 -- flt1**flt2)

fsin	Sine of flt in radians. ( flt -- sin(flt) )

fcos	Cosine of flt in radians. ( flt -- cos(flt) )

ftan	Tangent of flt in radians. ( flt -- tan(flt) )

fasin Arcine of flt, radians. ( flt -- asin(flt) ) facos Arccosine of flt, radians. ( flt -- acos(flt) ) fatan Arctangent of flt, radians. ( flt -- atan(flt) ) fatan2 Arctangent of flt1/flt2, radians.

flt1 flt2 -- atan(flt1/flt2) )

fsqrtSquare-root. ( flt -- sqrt(flt) )
fexpExponential. ( flt -- exp(flt) )

flog Natural logarithm. ( flt -- loge(flt) ) flog10 Logarithm, base 10. ( flt -- log10(flt) )

fcosh Hyperbolic cosine. ( flt -- cosh(flt) ) fsinh Hyperbolic sine. ( flt -- sinh(flt) ) ftanh Hyperbolic tangent. ( flt -- tanh(flt) )

The Compiler

De ning functions

Begin colon de nition. ( -- )
;End colon de nition. ( -- )
[Enter interpreter state. ( -- )

] Enter compilation state. ( -- ) state Compilation state. ( -- f )

State can only be changed with [ and ].

[i Enter Forth interrupt context. ( -- ) PIC18, PIC24-30-33

i] Enter compilation state. ( -- ) PIC18, PIC24-30-33

;i End an interrupt word. ( -- )

literalCompile value on stack at compile time. ( x -- ) At run time, leave value on stack. ( -- x )

2literal Compile double value on stack at compile time. ( x x -- )

At run time, leave value on stack. ( -- x x )

inline nameInline the following word. ( -- )

inlined	Mark the last compiled word as inlined. ( -- )

immediate	Mark latest de nition as immediate. ( -- )

immed?	Leave a nonzero value if addr contains

an immediate	ag. ( addr -- f )

in?	Leave a nonzero	ag if nfa has inline bit

set. ( nfa -- f )

postpone name	Postpone action of immediate word. ( -- )

see name	Show de nition. Load see.txt.

Comments

( comment text)	Inline comment.

\ comment text	Skip rest of line.

Examples of colon de nitions

square ( n -- n**2 )Example with stack comment.
dup * ;	...body of de nition.
: poke0	( -- )	Example of using PIC18 assembler.

[ $f8a 0 a, bsf, ] ;
Flow control

Structured	ow control

if xxx else yyy then	Conditional execution. ( f -- )

begin xxx again	In nite loop. ( -- )

begin xxx cond until	Loop until cond is true. ( -- )

begin xxx cond while	Loop while cond is true. ( -- )
repeatyyy is not executed on the last iteration.

for xxx next	Loop u times. ( u -- )

r@ gets the loop counter u-1 ... 0

endit	Sets loop counter to zero so that we leave

a for loop when next is encountered.

(--)

From doloop.txt, we get the ANSI loop constructs which iterate from initial up to, but not including, limit:
limit initial do words-to-repeat loop

limit initial do words-to-repeat value +loop

Leave the current loop index. ( -- n )

Innermost loop, for nested loops.

Leave the next-outer loop index. ( -- n ) leave Leave the do loop immediately. ( -- )
?doStarts a do loop which is not run if

the arguments are equal. ( limit initial -- )

Loop examples

decimal
: sumdo 0 100 0 do i + loop ;	sumdo leaves 4950
: sumfor 0 100 for r@ + next ;	sumfor leaves 4950

: print-twos 10 0 do i u. 2 +loop ;

Case example

From case.txt, we get words case, of, endof, default and endcase to de ne case constructs.
testcase

4 for r@

case

0 of ." zero " endof

1 of ." one " endof

2 of ." two " endof default ." default " endof

endcase

next

;

Unstructured	ow control

exit	Exit from a word. ( -- )

If exiting from within a for loop,

we must drop the loop count with rdrop.

abort	Reset stack pointer and execute quit. ( -- )

?abort	If	ag is false, print message

and abort. ( f addr u -- )

?abort?	If	ag is false, output ? and abort. ( f -- )
abort" xxx"	if	ag, type out last word executed,

followed by text xxx. ( f -- )

quit	Interpret from keyboard. ( -- )
warm	Make a warm start.

Reset reason will be displayed on restart.

S: Reset instruction

E: External reset pin

W: Watchdog reset

U: Return stack under ow

O: Return stack over ow

B: Brown out reset

P: Power on reset

M: Math error

A: Address error

Note that irq vector is cleared.

Vectored execution (Function pointers)

’ nameSearch for name and leave its

execution token (address). ( -- addr )

[’] name Search for name and compile

it’s execution token. ( -- )

execute	Execute word at address. ( addr -- ) The actual stack e ect will depend on the word executed.

@ex		Fetch vector from addr and execute.
		( addr -- )
defer vec-name		De ne a deferred execution vector. ( -- )
is vec-name		Store execution token in vec-name.
		( addr -- )
vec-name		Execute the word whose execution token
		is stored in vec-name’s data space.
int!	Store interrupt vector to table.
	( xt vector-no -- )
	PIC18: vector-no is dummy vector number (0)
	for high priority interrupts.
	PIC30: Alternate interrupt vector table in Flash.
	PIC33: Alternate interrupt vector table in RAM.
	PIC24H: Alternate interrupt vector table in RAM.
	PIC24F: Alternate interrupt vector table in RAM.
	PIC24FK: Alternate interrupt vector table in Flash.
	PIC24E: Main interrupt vector table in RAM.
	ATmega: Interrupt vector table in RAM.
int/	Restore the original vector to the interrupt vector
	table in ash. PIC30 PIC24FK ( vector-no -- )
ivt	Activate the normal interrupt vector table. ( -- )
	Not PIC24E, dsPIC33E.
aivt	Activate the alternate interrupt vector table. ( -- )

Interrupt example

ram variable icnt1	...from FF source.
: irq_forth	It’s a Forth colon de nition

[i	...in the Forth interrupt context.

icnt1 @ 1+

icnt1 !

]i

;i
’ irq_forth 0 int!Set the user interrupt vector.

: init	Alternatively, compile a word

[’] irq_forth 0 int! ...so that we can install the

;	...interrupt service function
’ init is turnkey	...at every warm start.

The P register

The P register can be used as a variable or as a pointer. It can be used in conjunction with for..next or at any other time.
!p	Store address to P(ointer) register. ( addr -- )

@p	Fetch the P register to the stack. ( -- addr )

!p>r	Push contents of P to return stack and

store new address to P. ( addr -- ) ( R: -- addr )

r>p	Pop from return stack to P register. ( R: addr -- )

p+	Increment P register by one. ( -- )

p2+	Add 2 to P register. ( -- )

p++	Add n to the p register. ( n -- )

p!	Store x to the location pointed to by the p register. ( x -- )

pc!	Store c to the location pointed to by the p register. ( c -- )

p@	Fetch the cell pointed to

by the p register. ( -- x )

pc@	Fetch the char pointed to

by the p register. ( -- c )

In a de nition, !p>r and r>p should always be used to allow proper nesting of words.

Characters

digit?	Convert char to a digit according to base.

( c -- n f )

>digit	Convert n to ascii character value. ( n -- c )

>pr	Convert a character to an ASCII value. ( c -- c )

Nongraphic characters converted to a dot.

char char	Parse a character and leave ASCII value. ( -- n )

For example: char A ( -- 65 )

[char] char	Compile inline ASCII character. ( -- )
place	Place string from a1 to a2

as a counted string. ( addr1 u addr2 -- )

n=	Compare strings in RAM(addr) and Flash(nfa).

Leave true if strings match, n < 16.

( addr nfa u -- f )

scan	Scan string until c is found.

c-addr must point to RAM and u < 255.

c-addr u c -- caddr1 u1 ) skip Skip chars until c not found.

c-addr must point to RAM and u < 255.

c-addr u c -- caddr1 u1 )

/string Trim string. ( addr u n -- addr+n u-n ) >number Convert string to a number.

( 0 0 addr1 u1 -- ud.l ud.h addr2 u2 ) number? Convert string to a number and ag.

( addr1 -- addr2 0 | n 1 | d.l d.h 2 ) Pre x: # decimal, $ hexadecimal, % binary.

sign?Get optional minus sign.

( addr1 n1 -- addr2 n2 flag )

typeType line to terminal, u < #256. ( addr u -- )

acceptGet line from the terminal. ( c-addr +n1 -- +n2 ) At most n1 characters are accepted, until the line is terminated with a carriage return.

sourceLeave address of input bu er and number of characters. ( -- c-addr u )

evaluate Interpret a string in SRAM. ( addr n -- ) interpret Interpret the bu er. ( c-addr u -- )
parseParse a word in TIB. ( c -- addr length )
wordParse a word in TIB and write length into TIB.

Leave the address of length byte on the stack.

( c -- c-addr )

Pictured numeric output

Formatted string representing an unigned double-precision integer is constructed in the end of tib.
<#	Begin conversion to formatted string. ( -- )

Convert 1 digit to formatted string. ( ud1 -- ud2 )

#sConvert remaining digits. ( ud1 -- ud2 ) Note that ud2 will be zero.

hold Append char to formatted string. ( c -- )

sign Add minus sign to formatted string, if n<0. ( n -- )

#>End conversion, leave address and count of formatted string. ( ud1 -- c-addr u )

For example, the following:

-1 34. <# # # #s rot sign #> type results in -034 ok

Autostart example

’ my-app is turnkey	Autostart my-app.
false is turnkey	Disable turnkey application.

Strings

Some of these words come from core.txt.
s"	text"	Compile string into	ash. ( -- )

At run time, leaves address and length.

( -- addr u )
."	text"	Compile string to print into	ash. ( -- )

Interaction with the operator

Interaction with the user is via a serial communications port, typically UART1. Settings are 38400 baud, 8N1, using Xon/Xo handshaking. Which particular serial port is selected is determined by the vectors ’emit, ’key and ’key?.

emit	Emit c to the serial port FIFO. ( c -- )

FIFO is 46 chars. Executes pause.

space	Emit one space character. ( -- )

spaces	Emit n space characters. ( n -- )

cr	Emit carriage-return, line-feed. ( -- )

key	Get a character from the serial port FIFO.

Execute pause until a character is available. ( -- c )

key?	Leave true if character is waiting

in the serial port FIFO. ( -- f )

Serial communication ports

tx0 Send a character via UART0 on ATmega. ( c -- ) rx0 Receive a character from UART0 on ATmega. ( -- c ) rx0? Leave true if the UART0 receive bu er

is not empty. ATmega ( -- f )
u0-	Disable	ow control for UART1 interface. ( -- )

u0+	Enable	ow control for UART1 interface, default. ( -- )

tx1	Send character to UART1. ( c -- )

Bu ered via an interrupt driven queue.

rx1	Receive a character from UART1. ( -- c )

Bu ered by an interrupt-driven queue. rx1? Leave true if the UART1 receive bu er

is not empty. ( -- f )
u1-	Disable	ow control for UART1 interface. ( -- )

u1+	Enable	ow control for UART1 interface, default. ( -- )

tx2	Send character to UART2. ( c -- )

PIC24-30-33

rx2	Receive a character from UART2. ( -- c )

PIC24-30-33

rx2?	Leave true if the UART1 receive bu er is not empty. PIC24-30-33 ( -- f )
u2-	Disable	ow control for UART2 interface. ( -- )

u2+	Enable	ow control for UART2 interface, default. ( -- )

txu	Send a character via the USB UART. ( c -- )

PIC18-USB

rxu	Receive a character from the USB UART. ( -- c ) PIC18-USB

rxu?	Leave true if the USB UART receive bu er

is not empty. PIC18-USB ( -- f )

Character queues on PIC24-30-33

cq: name	Create character queue. ( u -- )

cq0	Initialize or reset queue. ( queue-addr -- )

>cq?	Is there space available in queue. ( queue-addr -- f )

>cq	Put character into queue. ( c queue-addr -- )

cq>?	Number of characters in queue. ( queue-addr -- u )

cq>	Get character from queue. ( queue-addr -- c )

u1rxq	Leave UART1 RX queue address. ( -- queue-addr )

u1txq	Leave UART1 TX queue address. ( -- queue-addr )

u2rxq	Leave UART2 RX queue address. ( -- queue-addr )

u2txq	Leave UART2 TX queue address. ( -- queue-addr )

Other Hardware
cwd	Clear the WatchDog counter. ( -- )

PIC18, PIC24-30-33

ei	Enable interrupts. ( -- )

di	Disable interrupts. ( -- )

ms	Pause for +n milliseconds. ( +n -- )

ticks	System ticks, 0{	milliseconds. ( -- u )

Multitasking

Load the words for multitasking from task.txt. task: De ne a new task in ash memory space

( tibsize stacksize rstacksize addsize -- ) Use ram xxx allot to leave space for the PAD of the prevously de ned task.

The OPERATOR task does not use PAD.

tinit	Initialise a user area and link it

to the task loop. ( taskloop-addr task-addr -- )

Note that this may only be executed from

the operator task.

task	Leave the address of the task de nition table. ( -- addr )

run	Makes a task run by inserting it after operator

in the round-robin linked list. ( task-addr -- )

May only be executed from the operator task.

end	Remove a task from the task list. ( task-addr -- )

May only be executed from the operator task.

single	End all tasks except the operator task. ( -- )

Removes all tasks from the task list.

May only be executed from the operator task.

tasks	List all running tasks. ( -- )

pause	Switch to the next task in the round robin task list.

Idle in the operator task if allowed by all tasks. ( -- )

his	Access user variables of other task.

( task.addr vvar.addr -- addr )

load	Leave the CPU load on the stack. ( -- n )

Load is percentage of time that the CPU is busy.

Updated every 256 milliseconds.

load+	Enable the load LED on AVR8. ( -- )
load-	Disable the load LED on AVR8. ( -- )

busy	CPU idle mode not allowed. ( -- )

idle	CPU idle is allowed. ( -- )

operator	Leave the address of the operator task. ( -- addr )

ulink	Link to next task. ( -- addr )

Structured Assembler

To use many of the words listed in the following sections, load the text le asm.txt. The assembler for each processor family provides the same set of structured ow control words, however, the conditionals that go with these words are somewhat processor-speci c.

if, xxx else, yyy then,	Conditional execution. ( cc -- )

begin, xxx again,	Loop inde nitely. ( -- )

begin, xxx cc until,	Loop until condion is true. ( -- )
Assembler words for PIC18

In the stack-e ect notaion for the PIC18 family, f is a le register address, d is the result destination, a is the access bank modi er, and k is a literal value.

Conditions for structured	ow control
cc,	test carry ( -- cc )

nc,	test not carry ( -- cc )

mi,	test negative ( -- cc )

pl,	test not negative ( -- cc )

z,	test zero ( -- cc )

nz,	test not zero ( -- cc )

ov,	test over ow ( -- cc )

nov,	test not over ow ( -- cc )

not,	invert condition ( cc -- not-cc )

Destination and access modi ers w, Destination WREG ( -- 0 ) f, Destination le ( -- 1 )

a,	Access bank ( -- 0 )

b,	Use bank-select register ( -- 1 )

Byte-oriented	le register operations

addwf,	Add WREG and f. ( f d a -- )

addwfc,	Add WREG and carry bit to f. ( f d a -- )

andwf,	AND WREG with f. ( f d a -- )

clrf,	Clear f. ( f a -- )

comf,	Complement f. ( f d a -- )

cpfseq,	Compare f with WREG, skip if equal. ( f a -- )

cpfsgt,	Compare f with WREG, skip if greater than. ( f a -- )

cpfslt,	Compare f with WREG, skip if less than. ( f a -- )

decf,	Decrement f. ( f d a -- )

decfsz,	Decrement f, skip if zero. ( f d a -- )

dcfsnz,	Decrement f, skip if not zero. ( f d a -- )

incf,	Increment f. ( f d a -- )

incfsz,	Increment f, skip if zero. ( f d a -- )

infsnz,	Increment f, skip if not zero. ( f d a -- )

iorwf,	Inclusive OR WREG with f. ( f d a -- )

movf,	Move f. ( f d a -- )

movff,	Move fs to fd. ( fs fd -- )

movwf,	Move WREG to f. ( f a -- )

mulwf,	Multiply WREG with f. ( f a -- )

negf,	Negate f. ( f a -- )

rlcf,	Rotate left f, through carry. ( f d a -- )

rlncf,	Rotate left f, no carry. ( f d a -- )

rrcf,	Rotate right f, through carry. ( f d a -- )

rrncf,	Rotate right f, no carry. ( f d a -- )

setf,	Set f. ( f d a -- )

subfwb,	Subtract f from WREG, with borrow. ( f d a -- )

subwf,	Subtract WREG from f. ( f d a -- )

subwfb,	Subtract WREG from f, with borrow. ( f d a -- )

swapf,	Swap nibbles in f. ( f d a -- )

tstfsz,	Test f, skip if zero. ( f a -- )

xorwf,	Exclusive OR WREG with f. ( f d a -- )

Bit-oriented	le register operations

bcf,	Bit clear f. ( f b a -- )

bsf,	Bit set f. ( f b a -- )

btfsc,	Bit test f, skip if clear. ( f b a -- )

btfss,	Bit test f, skip if set. ( f b a -- )

btg,	Bit toggle f. ( f b a -- )

Literal operations

addlw,	Add literal and WREG. ( k -- )

andlw,	AND literal with WREG. ( k -- )

daw,	Decimal adjust packed BCD digits in WREG. ( -- )

iorlw,	Inclusive OR literal with WREG. ( k -- )

lfsr,	Move literal to FSRx. ( k f -- )

movlb,	Move literal to BSR. ( k -- )

movlw,	Move literal to WREG. ( k -- )

mullw,	Multiply literal with WREG. ( k -- )

sublw,	Subtract WREG from literal. ( k -- )

xorlw,	Exclusive OR literal with WREG. ( k -- )

Conditions for structured	ow control

z,	test zero ( -- cc )

nz,	test not zero ( -- cc )

not,	invert condition ( cc -- not-cc )

Low-level	ow control operations

bra,	Branch unconditionally. ( rel-addr -- )

rcall,	Call subroutine. ( rel-addr -- )

return,	Return from subroutine. ( -- )

retfie,	Return from interrupt enable. ( -- )

Bit-oriented operations

bclr,	Bit clear. ( bit ram-addr -- )

bset,	Bit set. ( bit ram-addr -- )

btst,	Bit test to z. ( bit ram-addr -- )

btsc,	Bit test, skip if clear. ( bit ram-addr -- )

btss,	Bit test, skip if set. ( bit ram-addr -- )

R0	--(	0 )	R16	--(	16 )
R1	( --	1 )	R17	( --	17 )
R2	( --	2 )	R18	( --	18 )
R3	( --	3 )	R19	( --	19 )
R4	( --	4 )	R20	( --	20 )
R5	( --	5 )	R21	( --	21 )
R6	( --	6 )	R22	( --	22 )
R7	( --	7 )	R23	( --	23 )
R8	( --	8 )	R24	( --	24 )
R9	( --	9 )	R25	( --	25 )
R10	( --	10 )	R26	( --	26 )
R11	( --	11 )	R27	( --	27 )
R12	( --	12 )	R28	( --	28 )
R13	( --	13 )	R29	( --	29 )
R14	( --	14 )	R30	( --	30 )
R15	( --	15 )	R31	( --	31 )

Data memory { program memory operations

tblrd*,	Table read. ( -- )

tblrd*+,	Table read with post-increment. ( -- )
tblrd*-,	Table read with post-decrement. ( -- )

tblrd+*,	Table read with pre-increment. ( -- )

tblwt*,	Table write. ( -- )

tblwt*+,	Table write with post-increment. ( -- )
tblwt*-,	Table write with post-decrement. ( -- )

tblwt+*,	Table write with pre-increment. ( -- )

Low-level	ow control operations

bra,	Branch unconditionally. ( rel-addr -- )

call,	Call subroutine. ( addr -- )

goto,	Go to address. ( addr -- )

pop,	Pop (discard) top of return stack. ( -- )

push,	Push address of next instruction to

top of return stack. ( -- )

rcall,	Relative call. ( rel-addr -- )

retfie,	Return from interrupt enable. ( -- )

retlw,	Return with literal in WREG. ( k -- )

return,	Return from subroutine. ( -- )

Other MCU control operations

clrwdt,	Clear watchdog timer. ( -- )

nop,	No operation. ( -- )

reset,	Software device reset. ( -- )

sleep,	Go into standby mode. ( -- )

Assembler words for PIC24-30-33

As stated in the wordsAll.txt, there is only a partial set of words for these families of microcontrollers.

Assembler words for AVR8

For the ATmega instructions, Rd denotes the destination (and source) register, Rr denotes the source register, Rw denotes a register-pair code, K denotes constant data, k is a constant address, b is a bit in the register, x,Y,Z are indirect address registers, A is an I/O location address, and q is a displacement (6-bit) for direct addressing.

Conditions for structured	ow control

cs,	carry set ( -- cc )

eq,	zero ( -- cc )

hs,	half carry set ( -- cc )

ie,	interrupt enabled ( -- cc )

lo,	lower ( -- cc )

lt,	less than ( -- cc )

mi,	negative ( -- cc )

ts,	T	ag set ( -- cc )

vs,	no over ow ( -- cc )

not,	invert condition ( cc -- not-cc )

Register constants

(--0) Z+ (--1) -Z (--2)

Y (--8) Y+ (--9) -Y (--10)

X (--12) X+ (--13) -X (--14)

XH:XL ( -- 01 ) YH:YL ( -- 02 ) ZH:ZL ( -- 03 )

Arithmetic and logic instructions

add,	Add without carry. ( Rd Rr -- )

adc,	Add with carry. ( Rd Rr -- )

adiw,	Add immediate to word. ( Rw K -- )

Rw = {XH:XL,YH:YL,ZH:ZL}

sub,	Subtract without carry. ( Rd Rr -- )

subi,	Subtract immediate. ( Rd K -- )

sbc,	Subtract with carry. ( Rd Rr -- )

sbci,	Subtract immediate with carry. ( Rd K -- )

sbiw,	Subtract immediate from word. ( Rw K -- )

Rw = {XH:XL,YH:YL,ZH:ZL}

and,	Logical AND. ( Rd Rr -- )

andi,	Logical AND with immediate. ( Rd K -- )

or,	Logical OR. ( Rd Rr -- )

ori,	Logical OR with immediate. ( Rd K -- )

eor,	Exclusive OR. ( Rd Rr -- )

com,	One’s complement. ( Rd -- )

neg,	Two’s complement. ( Rd -- )

sbr,	Set bit(s) in register. ( Rd K -- )

cbr,	Clear bit(s) in register. ( Rd K -- )

inc,	Increment. ( Rd -- )

dec,	Decrement. ( Rd -- )

tst,	Test for zero or minus. ( Rd -- )

clr,	Clear register. ( Rd -- )

ser,	Set register. ( Rd -- )

mul,	Multiply unsigned. ( Rd Rr -- )

muls,	Multiply signed. ( Rd Rr -- )

mulsu	Multiply signed with unsigned. ( Rd Rr -- )

fmul,	Fractional multiply unsigned. ( Rd Rr -- )

fmuls,	Fractional multiply signed. ( Rd Rr -- )

fmulsu,	Fractional multiply signed with unsigned. ( Rd Rr -- )

Branch instructions

rjmp,	Relative jump. ( k -- )

ijmp,	Indirect jump to (Z). ( -- )

eijmp,	Extended indirect jump to (Z). ( -- )

jmp,	Jump. ( k16 k6 -- )

k6 is zero for a 16-bit address.

rcall,	Relative call subroutine. ( k -- )

icall,	Indirect call to (Z). ( -- )

eicall,	Extended indirect call to (Z). ( -- )

call,	Call subroutine. ( k16 k6 -- )

k6 is zero for a 16-bit address.

ret,	Subroutine return. ( -- )

reti,	Interrupt return. ( -- )

cpse,	Compare, skip if equal. ( Rd Rr -- )

cp,	Compare. ( Rd Rr -- )

cpc,	Compare with carry. ( Rd Rr -- )

cpi,	Compare with immediate. ( Rd K -- )

sbrc,	Skip if bit in register cleared. ( Rr b -- )

sbrs,	Skip if bit in register set. ( Rr b -- )

sbic,	Skip if bit in I/O register cleared. ( A b -- )

sbis,	Skip if bit in I/O register set. ( A b -- )

Data transfer instructions

mov,	Copy register. ( Rd Rr -- )

movw,	Copy register pair. ( Rd Rr -- )

ldi,	Load immediate. ( Rd K -- )

lds,	Load direct from data space. ( Rd K -- )

ld,	Load indirect. ( Rd Rr -- )

Rr = {X,X+,-X,Y,Y+,-Y,Z,Z+,-Z}

ldd,	Load indirect with dosplacement. ( Rd Rr q -- ) Rr = {Y,Z}

sts,	Store direct to data space. ( k Rr -- )

st,	Store indirect. ( Rr Rd -- )

Rd = {X,X+,-X,Y,Y+,-Y,Z,Z+,-Z}

std,	Store indirect with displacement. ( Rr Rd q -- ) Rd={Y,Z}

in,	In from I/O location. ( Rd A -- )

out,	Out to I/O location. ( Rr A -- )

push,	Push register on stack. ( Rr -- )

pop,	Pop register from stack. ( Rd -- )

Bit and bit-test instructions

lsl,	Logical shift left. ( Rd -- )

lsr,	Logical shift right. ( Rd -- )

rol,	Rotate left through carry. ( Rd -- )

ror,	Rotate right through carry. ( Rd -- )

asr,	Arithmetic shift right. ( Rd -- )

swap,	Swap nibbles. ( Rd -- )

bset,	Flag set. ( s -- )

bclr,	Flag clear. ( s -- )

sbi,	Set bit in I/O register. ( A b -- )

cbi,	Clear bit in I/O register. ( A b -- )

bst,	Bit store from register to T. ( Rr b -- )

bld,	Bit load from T to register. ( Rd b -- )
sec,	Set carry. ( -- )

clc,	Clear carry. ( -- )

sen,	Set negative	ag. ( -- )

cln,	Clear negative	ag. ( -- )

sez,	Set zero	ag. ( -- )

clz	Clear zero	ag. ( -- )

sei,	Global interrupt enable. ( -- )

cli,	Global interrupt disable. ( -- )

ses,	Set signed test	ag. ( -- )

cls,	Clear signed test	ag. ( -- )

sev,	Set two’s complement over ow. ( -- )

clv,	Clear two-s complement over ow. ( -- )

set,	Set T in SREG. ( -- )

clt,	Clear T in SREG. ( -- )

seh,	Set half carry	ag in SREG. ( -- )

clh,	Clear half carry	ag in SREG. ( -- )

MCU control instructions
break,	Break. ( -- )

nop,	No operation. ( -- )

sleep,	Sleep. ( -- )

wdr,	Watchdog reset. ( -- )

Synchronous serial communication I2C communications as master

The following words are available as a common set of words for PIC18FXXK22, PIC24FV32KX30X and ATmega328P microcontrollers. Load them from a le with a name like i2c-base-XXXX.txt where XXXX is the speci c microcontroller.
i2c.init	Initializes I2C master mode, 100 kHz clock.
(--)

i2c.close	Shut down the peripheral module. ( -- )

i2c.ping?	Leaves true if the addressed slave device

acknowledges. ( 7-bit-addr -- f )

i2c.addr.write	Address slave device for writing.

Leave true if the slave acknowledged.

( 7-bit-addr -- f )

i2c.c!	Send byte and leave ack bit. ( c -- ack )

Note that the ack bit will be high

if the slave device did not acknowledge.
i2c-addr-read	Address slave device for reading.

Leave true if slave acknowledged.

7-bit-addr -- f )
i2c.c@.ackFetch a byte and ack for another.

	( -- c )
i2c.c@.nack	Fetch one last byte. ( -- c )
	(--)
Low level words.	Leave true if the I2C bus is idle. ( -- f )
i2c.idle?
i2c.start	Send start condition. ( -- )
i2c.rsen	Send restart condition. ( -- )
i2c.stop	Send stop condition. ( -- )
i2c.wait	Poll the I2C hardware until the operation
	has nished. ( -- )
i2c.bus.reset	Clock through bits so that slave devices
	are sure to release the bus. ( -- )

Alternate set I2C words for PIC18

Load these words from i2c_base.txt for a PIC18 microcontroller.

They make use of the structured assembler for the PIC18.
i2cinit	Initializes I2C master mode, 100 kHz clock. ( -- )
i2cws	Wake slave. Bit 0 is R/W bit. ( slave-addr -- )
The 7-bit I2C address is in bits 7-1.
i2c!	Write one byte to I2C bus and wait for ACK. ( c -- )
i2c@ak	Read one byte and continue. ( -- c )
i2c@nak	Read one last byte from the I2C bus. ( -- c )
i2c-addr1	Write 8-bit address to slave. ( addr slave-addr -- )
i2c-addr2	Write 16-bit address to slave ( addr slave-addr -- )

Lower-level words.
ssen	Assert start condition. ( -- )

srsen	Assert repeated start condition. ( -- )

spen	Generate a stop condition. ( -- )

srcen	Set receive enable. ( -- )

snoack	Send not-acknowledge. ( -- )

sack	Send acknowledge bit. ( -- )

sspbuf!	Write byte to SSPBUF and wait for

transmission. ( c -- )

SPI communications as master

The following words are available as a common set of words for PIC18FXXK22, PIC24FV32KX30X and ATmega328P microcontrollers. Load them from a le with a name like spiN-base-XXXX.txt where XXXX is the speci c microcontroller and N identi es the particular SPI module. Because SPI devices are so varied in their speci cation, you likely have to adjust the register settings in spi.init to suit your particular device.

spi.init	Initializes SPI master mode, 1 MHz clock.

(--)

spi.close	Shut down the peripheral module. ( -- )

spi.wait	Poll the SPI peripheral until the operation

has	nished. ( -- )

spi.cexch	Send byte c1, leave incoming byte c2 on stack.

c1 -- c2 )
spi.csendSend byte c. ( c -- )

spi.select Select the external device. ( -- ) spi.deselect Deselect the external device. ( -- )

This guide assembled by Peter Jacobs, School of Mechanical Engineering, The University of Queensland, February-2016 as Report 2016/02.

It is a remix of material from the following sources: FlashForth v5.0 source code and word list by Mikael Nordman http:// ashforth.sourceforge.net/
EK Conklin and ED Rather Forth Programmer’s Handbook 3rd Ed.
2007 FORTH, Inc.

L Brodie Starting Forth 2nd Ed., 1987 Prentice-Hall Software Series. Robert B. Reese Microprocessors from Assembly Language to C Using the PIC18Fxx2 Da Vinci Engineering Press, 2005.

Microchip 16-bit MCU and DSC Programmers Reference Manual Document DS70157F, 2011.
Atmel 8-bit AVR Insturction Set Document 08561-AVR-07/10.