UNOFFICIAL	P2X8C4M64P 8-Core Realtime Processor / Preliminary Shortform Data 2012082300

The P2X8C4M64P is the first member of the Parallax P2 family of realtime controllers containing 8 identical 32-bit processors called “cogs”, which connect to a common “hub”. The hub provides a shared RAM, a CORDIC math solver, and common system resources.
The architecture supports up to 64 smart I/O pins, each capable of many autonomous analog and digital functions such as UARTS, PWM, A/D, D/A etc.
COG x8 / 200MHz 32-bit CPU - (Overclocks to 360MHz) / Equal access to all I/O pins, plus four fast DAC output channels / 512 longs of dual-port register RAM for code and fast variables / 512 longs of dual-port lookup RAM for code, streamer lookup, and variables / Ability to execute code directly from register RAM, lookup RAM, and hub RAM / ~350 unique instructions for math, logic, timing, and control operations / 2-clock execution for all math and logic instructions, including 16 x 16 multiply / 6-clock custom-bytecode executor for interpreted languages / Stream hub RAM and/or lookup RAM to DACs and pins, also pins to hub RAM / Live colorspace conversion using a 3 x 3 matrix with 8-bit signed/unsigned coefficients / Pixel blending instructions for 8:8:8:8 data / 16 unique event trackers that can be polled and waited upon / 3 prioritized interrupts that trigger on selectable events / Hidden debug interrupt for single-stepping, breakpoint, and polling / HUB / 512kB of contiguous RAM in a 20-bit address space / 32-bits-per-clock sequential read/write for all cogs, simultaneously / readable and writable as bytes, words, or longs / last 16KB of RAM also appears at end of 1MB map and is write-protectable / 16 semaphore bits with atomic read-modify-write operations / 32-bit free-running counter, increments every clock / Mechanisms for starting, polling, and stopping cogs / 16KB boot ROM loads into last 16KB of hub RAM on boot-up / SPI Flash and SD boot loader for automatic startup / Serial loader for startup from host + Monitor + TAQOZ interactive interpreter / CORDIC SOLVER / 32-bit, pipelined CORDIC solver with scale-factor correction / 32 x 32 unsigned multiply and 64 / 32 unsigned divide / 64 → 32 square root / Rotate (X32,Y32) by Theta32 → (X32,Y32) / Convert between Polar (Rho32,Theta32) ↔ Cartesian (X32,Y32) / 32 → 5:27 unsigned-to-logarithm and 5:27 → 32 logarithm-to-unsigned / CORDIC operations can start every 1/2/4/8/16 clocks with results in 55 clocks / PRNG Pseudo Random Number Generator / High-quality PRNG (Xoroshiro128**) updates every clock, unique data per cog and pin / CLOCK - RCSLOW, RCFAST or EXT, XTAL --> PLL = ÷1..64 ; x1..1024 ; ÷2,4,6..30	SMART PIN (64 channels) / 8-bit, 120-ohm (3ns) and 1k-ohm DACs / 16-bit oversampling, noise, and high/low digital modes / Delta-sigma ADC with 5 ranges, 2 sources, and VIO/GIO calibration / Logic, Schmitt, pin-to-pin-comparator, and 8-bit-level-comparator input modes / 2/3/5/8-bit-unanimous input filtering with selectable sample rate / Incorporation of inputs from relative pins, -3 to +3 / Negative or positive local feedback, with or without clocking / Separate drive modes for high and low output: logic/1.5k/15k/150k/1mA/100uA/10uA/float / Programmable 32-bit clock output, transition output, NCO/duty output / Triangle/sawtooth/SMPS PWM output, 16-bit frame with 16-bit prescaler / Quadrature decoding with 32-bit counter, both position and velocity modes / 16 different 32-bit measurements involving one or two signals / USB full-speed and low-speed (via odd/even pin pairs) / Synchronous serial transmit and receive, 1 to 32 bits / Asynchronous serial transmit and receive, 1 to 32 bits, up to clock/3 (60Mbps) / BLOCK DIAGRAM and PINOUT

P2X8C4M64P PIN CONNECTIONS - TQFP100
PIN NAME NOTES * / 1 TEST connect to GND / 2 VDD CPU 1.8V 4 / 3 P0 SmartPin / 4 P1 SmartPin / 5 V0003 I/O 3.3V 5 / 6 P2 SmartPin / 7 P3 SmartPin / 8 VDD CPU 1.8V 4 / 9 P4 SmartPin / 10 P5 SmartPin / 11 V0407 I/O 3.3V 5 / 12 P6 SmartPin / 13 P7 SmartPin / 14 VDD CPU 1.8V 4 / 15 P8 SmartPin / 16 P9 SmartPin / 17 V0811 I/O 3.3V 5 / 18 P10 SmartPin / 19 P11 SmartPin / 20 VDD CPU 1.8V 4 / 21 P12 SmartPin / 22 P13 SmartPin / 23 V1215 I/O 3.3V 5 / 24 P14 SmartPin / 25 P15 SmartPin	PIN NAME NOTES * / 26 VDD CPU 1.8V 4 / 27 P16 SmartPin / 28 P17 SmartPin / 29 V1619 I/O 3.3V 5 / 30 P18 SmartPin / 31 P19 SmartPin / 32 VDD CPU 1.8V 4 / 33 P20 SmartPin / 34 P21 SmartPin / 35 V2023 I/O 3.3V 5 / 36 P22 SmartPin / 37 P23 SmartPin / 38 VDD CPU 1.8V 4 / 39 P24 SmartPin / 40 P25 SmartPin / 41 V2527 I/O 3.3V 5 / 42 P26 SmartPin / 43 P27 SmartPin / 44 VDD CPU 1.8V 4 / 45 P28 SmartPin / 46 P29 SmartPin / 47 V2831 I/O 3.3V 5 / 48 P30 SmartPin / 49 P31 SmartPin / 50 X0 Crystal out	PIN NAME NOTES * / 51 XI Crystal/Ext Clock In 7 / 52 VDD CPU 1.8V 4 / 53 P32 SmartPin / 54 P33 SmartPin / 55 V3225 I/O 3.3V 5 / 56 P34 SmartPin / 57 P35 SmartPin / 58 VDD CPU 1.8V 4 / 59 P36 SmartPin / 60 P37 SmartPin / 61 V3639 I/O 3.3V 5 / 62 P38 SmartPin / 63 P39 SmartPin / 64 VDD CPU 1.8V 4 / 65 P40 SmartPin / 66 P41 SmartPin / 67 V4043 I/O 3.3V 5 / 68 P42 SmartPin / 69 P43 SmartPin / 70 VDD CPU 1.8V 4 / 71 P44 SmartPin / 72 P45 SmartPin / 73 V4447 I/O 3.3V 5 / 74 P46 SmartPin / 75 P47 SmartPin	PIN NAME NOTES SPI SD SER * / 76 VDD CPU 1.8V 4 / 77 P48 SmartPin / 78 P49 SmartPin / 79 V4851 I/O 3.3V 5 / 80 P50 SmartPin / 81 P51 SmartPin / 82 VDD CPU 1.8V 4 / 83 P52 SmartPin / 84 P53 SmartPin / 85 V5255 I/O 3.3V 5 / 86 P54 SmartPin / 87 P55 SmartPin / 88 VDD CPU 1.8V 4 / 89 P56 SmartPin / 90 P57 SmartPin / 91 V5659 I/O 3.3V 5 / 92 P58 SmartPin DO DO / 93 P59 SmartPin DI DI 3 / 94 VDD CPU 1.8V 4 / 95 P60 SmartPin CK CS 2 / 96 P61 SmartPin CS CK 1 / 97 V6063 I/O 3.3V 5 / 98 P62 SmartPin TXD / 99 P63 SmartPin RXD / 100 RES RESET / PAD GND COMMON

NOTES: / *1 – Add pull-up for SPI Flash detection / *2 – Do not use ext pull-up – uses SD card’s internal pull-up for card detection / *3 – Pull-down disables all serial boot functions including monitor and TAQOZ. / *3 – Pull-up forces serial boot priority	*4 – Connect all VDD pins to 1.8V CPU supply / *5 – Connect all VIO pins to I/O supply voltage / *6 – 10 to 20MHz crystal input or external clock

P2X8C4M64P TQFP100 LD MECHANICAL
Symbol Description Min Typ mm Max / D1/E1 Body 14 BSC / D/E Tip-Tip 16 BSC / ePad Exposed GND Pad 10.3 / A2 Body Thickness 1.35 1.4 1.45 / A Height off PCB - - 1.6 / A1 PCB clearance 0.05 - 0.15 / e Lead spacing 0.5 BSC / b Lead Width 0.17 0.22 0.27 / L Foot Length 0.45 0.6 0.75

PHYSICAL PINOUT DIAGRAM
 LINKS
 P2 DOCUMENTATION
 INSTRUCTION SET & SAMPLES
 Parallax P2 Forum
 Spin2gui fastspin IDE
 TAQOZ
 SD BOOTER
 MONITOR

P2 TOOLS
Spin2 GUI with fastspin, p2asm, p2load / 00498 | ' '' recursive version / 00498 | ' PUB fiborec(n) / 00498 / 00498 | _Fiborec / 00498 618364FC | wrlong _Fiborec_N, ptra++ / 0049c 616364FC | wrlong Fiborec_tmp001_, ptra++ / 004a0 616564FC | wrlong Fiborec_tmp005_, ptra++ / 004a4 616764FC | wrlong Fiborec_tmp008_, ptra++ / 004a8 518200F6 | mov _Fiborec_N, arg1 / 004ac | ' return (n < 2) ? n : fiborec(n-1)+fiborec(n-2) / 004ac 02825CF2 | cmps _Fiborec_N, #2 wcz / 004b0 416200C6 | if_b mov Fiborec_tmp001_, _Fiborec_N / 004b4 280090CD | if_b jmp #@L__0012 / 004b8 41A200F6 | mov arg1, _Fiborec_N / 004bc 01A284F1 | sub arg1, #1 / 004c0 D4FFDFFD | calla #@_Fiborec / 004c4 2B6400F6 | mov Fiborec_tmp005_, result1 / 004c8 41A200F6 | mov arg1, _Fiborec_N / 004cc 02A284F1 | sub arg1, #2 / 004d0 C4FFDFFD | calla #@_Fiborec / 004d4 2B6600F6 | mov Fiborec_tmp008_, result1 / 004d8 326200F6 | mov Fiborec_tmp001_, Fiborec_tmp005_ / 004dc 336200F1 | add Fiborec_tmp001_, Fiborec_tmp008_ / 004e0 / 004e0 | L__0012 / 004e0 315600F6 | mov result1, Fiborec_tmp001_ / 004e4 5F6704FB | rdlong Fiborec_tmp008_, --ptra / 004e8 5F6504FB | rdlong Fiborec_tmp005_, --ptra / 004ec 5F6304FB | rdlong Fiborec_tmp001_, --ptra / 004f0 5F8304FB | rdlong _Fiborec_N, --ptra / 004f4 / 004f4 | _Fiborec_ret / 004f4 2E0064FD | reta	ROM TOOLS - TAQOZ / ---------------------------------------------------------------- / Parallax P2 .:.:--TAQOZ--:.:. V1.0--142 180530-0135 / ---------------------------------------------------------------- / TAQOZ# WORDS / DUP OVER SWAP ROT -ROT DROP 3RD 4TH 2DROP 3DROP NIP 2SWAP 2DUP ?DUP AND / ANDN OR XOR ROL ROR >> << SAR 2/ 2* 4/ 4* 8<< 16>> 8>> 9<< 9>> REV |< >| / >N >B >9 BITS NOT = <> 0= 0<> 0< < U< > U> <= => WITHIN DUPC@ C@ W@ @ C+! / C! C@++ W+! W! +! ! BIT! SET CLR SET? 1+ 1- 2+ 2- 4+ + - UM* * W* / U/ / U// // */ UM// C++ C-- W++ W-- ++ -- RND GETRND SQRT SETDACS ~ ~~ W~ W~~ / C~ C~~ L>S >W L>W W>B W>L B>W B>L MINS MAXS MIN MAX ABS -NEGATE ?NEGATE / NEGATE ON TRUE -1 FALSE OFF GOTO IF ELSE THEN BEGIN UNTIL AGAIN WHILE REPEAT / SWITCH CASE@ CASE= CASE> BREAK CASE ADO DO LOOP +LOOP FOR NEXT ?NEXT I / J LEAVE IC@ I+ BOUNDS H L T F R HIGH LOW FLOAT PIN@ WRPIN WXPIN WYPIN RDPIN / RQPIN AKPIN WAITPIN WRACK PIN @PIN ns PW PULSE PULSES HILO DUTY NCO HZ / KHZ MHZ MUTE BLINK PWM SAW BIT BAUD TXD RXD TXDAT WAITX WAITCNT REBOOT / RESET 0EXIT EXIT NOP CALL JUMP >R R> >L L> !SP DEPTH COG@ COG! LUT@ LUT! / COGID COGINIT COGSTOP NEWCOG COGATN POLLATN SETEDG POLLEDG KEY WKEY KEY! / CON NONE COM CONKEY CONEMIT SEROUT EMIT EMITS CRLF CR CLS SPACE SPACES / RAM DUMP: DUMP DUMPW DUMPL DUMPA DUMPAW QD QW DEBUG lsio COG LUT KB MB / M . PRINT .AS .AS" .DECL .DEC4 HOLD #> <# # #S <D> U. .DEC .BIN .H .B .BYTE / .W .WORD .L .LONG .ADDR PRINT$ LEN$ " ." CTYPE ?EXIT DATA? ERASE FILL CMOVE / <CMOVE s ms us CNT@ LAP LAP@ .LAP .ms HEX DEC BIN .S WORDS @WORDS GET$ / SEARCH $># @DATA HERE @HERE @CODES uemit ukey char delim names TASK REG / @WORD SPIN | || , [W] ["] NULL$ $! $= ASM FORGET CREATE$ CREATE VAR pub / pri pre : ; [ ] ' := ==! ALIGN DATCON ALLOT org bytes words longs byte / word long res [C] GRAB NFA' CPA CFA \ --- ( { } IFNDEF IFDEF TAQOZ TERM / AUTO SPIRD SPIRDL SPIWB SPICE SPIWC SPIWW SPIWM SPIWL SPIPINS SPIRX SPITXE / SPITX WSLED WAIT CLKDIV RCSLOW HUBSET WP WE CLKHZ ERROR SFPINS SF? SFWE / SFINS SFWD SFSID SFJID SFER4 SFER32 SFER64 SFERASE SFWRPG BACKUP RESTORE / SFRDS SFWRS SFC@ SFW@ SF@ SF .SF SDBUF sdpins MOUNT DIR !SD !SX SD? CMD / ACMD cid SDWR SDRDS SDWRS FLUSH FOPEN FLOAD FGET FREAD FWRITE SECTOR SDRD / SDRDS SDADR SD@ SD! SDC@ SDC! SDW@ SD @FAT @BOOT @ROOT fat END 433 ok
	SD BOOTER & MONITOR