# PROPELLER 2 MEMORY

In the Propeller 2, there are two primary types of memory:

HUB MEMORY

    128K bytes of main memory shared by all cogs

        - cogs launch from this memory
        - cogs can access this memory as bytes, words, longs, and quads (4 longs)
        - $00000..$00E7F is ROM - contains Booter, SHA-256/HMAC, and Monitor
        - $00E80..$1FFFF is RAM - for application usage

COG MEMORY (8 sets)

    512 longs of register RAM for code and data usage

        - simultaneous instruction, source, and destination reading, plus writing

    256 longs of push/pop RAM for data and video usage

        - pushes are 1-clock
        - pops are 2-clock
        - video circuit can read data simultaneously and asynchronously

## HUB MEMORY INSTRUCTIONS

These instructions read and write hub memory.

All instructions use D as the data conduit, except WRQUAD/RDQUAD/RDQUADC, which use the four QUAD
registers. The QUADs can be mapped into cog register space using the SETQUAD instruction or kept
hidden, in which case they are still useful as data conduit and as a read cache. If mapped, the QUADs
overlay four contiguous cog registers which can begin at any double-even address (%xxxxxxx00). These
overlaid registers can be read and written as any other registers, as well as executed.

The cached reads RDBYTEC/RDWORDC/RDLONGC/RDQUADC will do a RDQUAD if the current read address is
outside of the 4-long window of the prior RDQUAD. Otherwise, they will immediately return cached
data. The CACHEX instruction invalidates the cache, forcing a fresh RDQUAD next time a cached read
executes.

Hub memory instructions must wait for their cog's hub cycle, which comes once every 8 clocks. The
timing relationship between a cog's instruction stream and its hub cycle is generally indeterminant,
causing these instructions to take varying numbers of clocks. Timing can be made determinant, though,
by intentionally spacing these instructions apart so that after the first in a series executes, the
subsequent hub memory instructions fall on hub cycles, making them take the minimal numbers of
clocks. The trick is to write useful code to go between them.

WRBYTE/WRWORD/WRLONG/WRQUAD/RDQUAD complete on the hub cycle, making them take 1..8 clocks.

RDBYTE/RDWORD/RDLONG complete on the 2nd clock after the hub cycle, making them take 3..11 clocks.

RDBYTEC/RDWORDC/RDLONGC take only 1 clock if data is cached, otherwise 3..11 clocks.

RDQUADC takes only 1 clock if data is cached, otherwise 1..8 clocks.

After a RDQUAD, the QUAD registers are accessible via D and S on the 3rd clock and executable on the
5th clock.

instructions clocks
---------------------------------------------------------------------------------------------------------
000000 000 0 CCCC DDDDDDDDD SSSSSSSSS WRBYTE D,S 'write lower byte in D at S 1..8
000000 000 1 CCCC DDDDDDDDD SUPNNNNNN WRBYTE D,PTR 'write lower byte in D at PTR 1..8
000000 Z01 0 CCCC DDDDDDDDD SSSSSSSSS RDBYTE D,S 'read byte at S into D 3..11
000000 Z01 1 CCCC DDDDDDDDD SUPNNNNNN RDBYTE D,PTR 'read byte at PTR into D 3..11
000000 Z11 0 CCCC DDDDDDDDD SSSSSSSSS RDBYTEC D,S 'read cached byte at S into D 1, 3..11
000000 Z11 1 CCCC DDDDDDDDD SUPNNNNNN RDBYTEC D,PTR 'read cached byte at PTR into D 1, 3..11

000001 000 0 CCCC DDDDDDDDD SSSSSSSSS WRWORD D,S 'write lower word in D at S 1..8
000001 000 1 CCCC DDDDDDDDD SUPNNNNNN WRWORD D,PTR 'write lower word in D at PTR 1..8
000001 Z01 0 CCCC DDDDDDDDD SSSSSSSSS RDWORD D,S 'read word at S into D 3..11
000001 Z01 1 CCCC DDDDDDDDD SUPNNNNNN RDWORD D,PTR 'read word at PTR into D 3..11
000001 Z11 0 CCCC DDDDDDDDD SSSSSSSSS RDWORDC D,S 'read cached word at S into D 1, 3..11
000001 Z11 1 CCCC DDDDDDDDD SUPNNNNNN RDWORDC D,PTR 'read cached word at PTR into D 1, 3..11

000010 000 0 CCCC DDDDDDDDD SSSSSSSSS WRLONG D,S 'write D at S 1..8
000010 000 1 CCCC DDDDDDDDD SUPNNNNNN WRLONG D,PTR 'write D at PTR 1..8
000010 Z01 0 CCCC DDDDDDDDD SSSSSSSSS RDLONG D,S 'read long at S into D 3..11
000010 Z01 1 CCCC DDDDDDDDD SUPNNNNNN RDLONG D,PTR 'read long at PTR into D 3..11
000010 Z11 0 CCCC DDDDDDDDD SSSSSSSSS RDLONGC D,S 'read cached long at S into D 1, 3..11
000010 Z11 1 CCCC DDDDDDDDD SUPNNNNNN RDLONGC D,PTR 'read cached long at PTR into D 1, 3..11

000011 000 0 CCCC DDDDDDDDD 010110000 WRQUAD D 'write QUADs at D 1..8
000011 001 1 CCCC SUPNNNNNN 010110000 WRQUAD PTR 'write QUADs at PTR 1..8
000011 000 0 CCCC DDDDDDDDD 010110001 RDQUAD D 'read quad at D into QUADs 1..8
000011 001 1 CCCC SUPNNNNNN 010110001 RDQUAD PTR 'read quad at PTR into QUADs 1..8
000011 010 0 CCCC DDDDDDDDD 010110001 RDQUADC D 'read cached quad at D into QUADs 1, 1..8
000011 011 1 CCCC SUPNNNNNN 010110001 RDQUADC PTR 'read cached quad at PTR into QUADs 1, 1..8
---------------------------------------------------------------------------------------------------------

PTR expressions:

    INDEX = -32..+31 for simple offsets, 0..31 for ++'s, or 0..32 for --'s
    SCALE = 1 for byte, 2 for word, 4 for long, or 16 for quad

    S = 0 for PTRA, 1 for PTRB
    U = 0 to keep PTRx same, 1 to update PTRx
    P = 0 to use PTRx + INDEX*SCALE, 1 to use PTRx (post-modify)
    NNNNNN = INDEX
    nnnnnn = -INDEX

    SUPNNNNNN PTR expression
    -----------------------------------------------------------------------------
    000000000 PTRA 'use PTRA
    100000000 PTRB 'use PTRB
    011000001 PTRA++ 'use PTRA, PTRA += SCALE
    111000001 PTRB++ 'use PTRB, PTRB += SCALE
    011111111 PTRA-- 'use PTRA, PTRA -= SCALE
    111111111 PTRB-- 'use PTRB, PTRB -= SCALE
    010000001 ++PTRA 'use PTRA + SCALE, PTRA += SCALE
    110000001 ++PTRB 'use PTRB + SCALE, PTRB += SCALE
    010111111 --PTRA 'use PTRA - SCALE, PTRA -= SCALE
    110111111 --PTRB 'use PTRB - SCALE, PTRB -= SCALE

    000NNNNNN PTRA[INDEX] 'use PTRA + INDEX*SCALE
    100NNNNNN PTRB[INDEX] 'use PTRB + INDEX*SCALE
    011NNNNNN PTRA++[INDEX] 'use PTRA, PTRA += INDEX*SCALE
    111NNNNNN PTRB++[INDEX] 'use PTRB, PTRB += INDEX*SCALE
    011nnnnnn PTRA--[INDEX] 'use PTRA, PTRA -= INDEX*SCALE
    111nnnnnn PTRB--[INDEX] 'use PTRB, PTRB -= INDEX*SCALE
    010NNNNNN ++PTRA[INDEX] 'use PTRA + INDEX*SCALE, PTRA += INDEX*SCALE
    110NNNNNN ++PTRB[INDEX] 'use PTRB + INDEX*SCALE, PTRB += INDEX*SCALE
    010nnnnnn --PTRA[INDEX] 'use PTRA - INDEX*SCALE, PTRA -= INDEX*SCALE
    110nnnnnn --PTRB[INDEX] 'use PTRB - INDEX*SCALE, PTRB -= INDEX*SCALE

Examples:

000000 Z01 1 CCCC DDDDDDDDD 000000000 RDBYTE D,PTRA 'read byte at PTRA into D
000001 000 1 CCCC DDDDDDDDD 111000001 WRWORD D,PTRB++ 'write lower word in D at PTRB, PTRB += 2
000010 Z01 1 CCCC DDDDDDDDD 011111111 RDLONG D,PTRA-- 'read long at PTRA into D, PTRA -= 4
000011 001 1 CCCC 110000001 010110001 RDQUAD ++PTRB 'read quad at PTRB+16 into QUADs, PTRB += 16
000000 000 1 CCCC DDDDDDDDD 010111111 WRBYTE D,--PTRA 'write lower byte in D at PTRA-1, PTRA -= 1

000001 000 1 CCCC DDDDDDDDD 100000111 WRWORD D,PTRB[7] 'write lower word in D to PTRB+7*2
000010 Z11 1 CCCC DDDDDDDDD 011001111 RDLONGC D,PTRA++[15] 'read cached long at PTRA into D, PTRA += 15*4
000011 001 1 CCCC 111111101 010110000 WRQUAD PTRB--[3] 'write QUADs at PTRB, PTRB -= 3*16
000000 000 1 CCCC DDDDDDDDD 010000110 WRBYTE D,++PTRA[6] 'write lower byte in D to PTRA+6*1, PTRA += 6*1
000001 Z01 1 CCCC DDDDDDDDD 110110110 RDWORD D,--PTRB[10] 'read word at PTRB-10*2 into D, PTRB -= 10*2

Bytes, words, longs, and quads are addressed as follows:

    for WRBYTE/RDBYTE/RDBYTEC, address = %XXXXXXXXXXXXXXXXX (bits 16..0 are used)
    for WRWORD/RDWORD/RDWORDC, address = %XXXXXXXXXXXXXXXX- (bits 16..1 are used)
    for WRLONG/RDLONG/RDLONGC, address = %XXXXXXXXXXXXXXX-- (bits 16..2 are used)
    for WRQUAD/RDQUAD/RDQUADC, address = %XXXXXXXXXXXXX---- (bits 16..4 are used)

address byte word long quad
-------------------------------------------------------------------
00000- 50 *7250 *706F7250 *0C7CCC030C7C200020302E32706F7250
00001- 72 7250 706F7250 0C7CCC030C7C200020302E32706F7250
00002- 6F *706F 706F7250 0C7CCC030C7C200020302E32706F7250
00003- 70 706F 706F7250 0C7CCC030C7C200020302E32706F7250
00004- 32 *2E32 *20302E32 0C7CCC030C7C200020302E32706F7250
00005- 2E 2E32 20302E32 0C7CCC030C7C200020302E32706F7250
00006- 30 *2030 20302E32 0C7CCC030C7C200020302E32706F7250
00007- 20 2030 20302E32 0C7CCC030C7C200020302E32706F7250
00008- 00 *2000 *0C7C2000 0C7CCC030C7C200020302E32706F7250
00009- 20 2000 0C7C2000 0C7CCC030C7C200020302E32706F7250
0000A- 7C *0C7C 0C7C2000 0C7CCC030C7C200020302E32706F7250
0000B- 0C 0C7C 0C7C2000 0C7CCC030C7C200020302E32706F7250
0000C- 03 *CC03 *0C7CCC03 0C7CCC030C7C200020302E32706F7250
0000D- CC CC03 0C7CCC03 0C7CCC030C7C200020302E32706F7250
0000E- 7C *0C7C 0C7CCC03 0C7CCC030C7C200020302E32706F7250
0000F- 0C 0C7C 0C7CCC03 0C7CCC030C7C200020302E32706F7250
00010- 45 *FE45 *0DC1FE45 *0D7CC6010C7CC6010CFCB6E30DC1FE45
00011- FE FE45 0DC1FE45 0D7CC6010C7CC6010CFCB6E30DC1FE45
00012- C1 *0DC1 0DC1FE45 0D7CC6010C7CC6010CFCB6E30DC1FE45
00013- 0D 0DC1 0DC1FE45 0D7CC6010C7CC6010CFCB6E30DC1FE45
00014- E3 *B6E3 *0CFCB6E3 0D7CC6010C7CC6010CFCB6E30DC1FE45
00015- B6 B6E3 0CFCB6E3 0D7CC6010C7CC6010CFCB6E30DC1FE45
00016- FC *0CFC 0CFCB6E3 0D7CC6010C7CC6010CFCB6E30DC1FE45
00017- 0C 0CFC 0CFCB6E3 0D7CC6010C7CC6010CFCB6E30DC1FE45
00018- 01 *C601 *0C7CC601 0D7CC6010C7CC6010CFCB6E30DC1FE45
00019- C6 C601 0C7CC601 0D7CC6010C7CC6010CFCB6E30DC1FE45
0001A- 7C *0C7C 0C7CC601 0D7CC6010C7CC6010CFCB6E30DC1FE45
0001B- 0C 0C7C 0C7CC601 0D7CC6010C7CC6010CFCB6E30DC1FE45
0001C- 01 *C601 *0D7CC601 0D7CC6010C7CC6010CFCB6E30DC1FE45
0001D- C6 C601 0D7CC601 0D7CC6010C7CC6010CFCB6E30DC1FE45
0001E- 7C *0D7C 0D7CC601 0D7CC6010C7CC6010CFCB6E30DC1FE45
0001F- 0D 0D7C 0D7CC601 0D7CC6010C7CC6010CFCB6E30DC1FE45

* new word/long/quad

PTRA/PTRB INSTRUCTIONS
----------------------

Each cog has two 17-bit pointers, PTRA and PTRB, which can be read, written, modified,
and used to access hub memory.

On cog startup, the PTRA and PTRB registers are initialized as follows:

    PTRA = %X_XXXXXXXX_XXXXXXXX, data from launching cog, usually a pointer
    PTRB = %X_XXXXXXXX_XXXXXX00, long address in hub where cog code was loaded from

instructions clocks
-------------------------------------------------------------------------------------------------
000011 ZCR 1 CCCC DDDDDDDDD 000010010 GETPTRA D 'get PTRA into D 1
000011 ZCR 1 CCCC DDDDDDDDD 000010011 GETPTRB D 'get PTRB into D 1

000011 000 1 CCCC DDDDDDDDD 010110010 SETPTRA D 'set PTRA to D 1
000011 001 1 CCCC nnnnnnnnn 010110010 SETPTRA #n 'set PTRA to 0..511 1
000011 000 1 CCCC DDDDDDDDD 010110011 SETPTRB D 'set PTRB to D 1
000011 001 1 CCCC nnnnnnnnn 010110011 SETPTRB #n 'set PTRB to 0..511 1

000011 000 1 CCCC DDDDDDDDD 010110100 ADDPTRA D 'add D into PTRA 1
000011 001 1 CCCC nnnnnnnnn 010110100 ADDPTRA #n 'add 0..511 into PTRA 1
000011 000 1 CCCC DDDDDDDDD 010110101 ADDPTRB D 'add D into PTRB 1
000011 001 1 CCCC nnnnnnnnn 010110101 ADDPTRB #n 'add 0..511 into PTRB 1

000011 000 1 CCCC DDDDDDDDD 010110110 SUBPTRA D 'subtract D from PTRA 1
000011 001 1 CCCC nnnnnnnnn 010110110 SUBPTRA #n 'subtract 0..511 from PTRA 1
000011 000 1 CCCC DDDDDDDDD 010110111 SUBPTRB D 'subtract D from PTRB 1
000011 001 1 CCCC nnnnnnnnn 010110111 SUBPTRB #n 'subtract 0..511 from PTRB 1
-------------------------------------------------------------------------------------------------

QUAD-RELATED INSTRUCTIONS
-------------------------

Each cog has four QUAD registers which form a 128-bit conduit between the hub memory and the cog.
This conduit can transfer four longs every 8 clocks via the WRQUAD/RDQUAD instructions. It can
also be used as a 4-long/8-word/16-byte read cache, utilized by RDBYTEC/RDWORDC/RDLONGC/RDQUADC.

Initially hidden, these QUAD registers are mappable into cog register space by using the SETQUAD
instruction to set a double-even address (%xxxxxxx00) where the base register is to appear, with
the other three registers following. To hide the QUAD registers, use SETQUAD to set an address
which is not double-even.

instructions clocks
-------------------------------------------------------------------------------------------------
000011 000 1 CCCC 000000000 000001000 CACHEX 'invalidate cash 1
000011 Z01 1 CCCC DDDDDDDDD 000010001 GETTOPS D 'get top bytes of QUADs into D 1
000011 000 1 CCCC DDDDDDDDD 011100010 SETQUAD D 'set QUAD start address to D 1
000011 001 1 CCCC nnnnnnnnn 011100010 SETQUAD #n 'set QUAD start address to 0..511 1

## TIME-SLICING INSTRUCTIONS

These instructions configure the four hardware threads in a Cog.

There are 4 program counters in each cog. They are initialized as follows:
PC0 = $000
PC1 = $001
PC2 = $002
PC3 = $003
At first, the task register, which is 32 bits (16 two-bit fields), is cleared to 0, making all time slots execute task0.
JMPTASK sets up to all four PC's at once, using a bit field in S and an address in D.
JMPTASK #substart,#%1111 ...would set all PC's to substart
JMPTASK #substart,#%1000 ...would set PC3 to substart
JMPTASK #substart,#%0100 ...would set PC2 to substart
JMPTASK #substart,#%0010 ...would set PC1 to substart
JMPTASK #substart,#%0001 ...would set PC0 to substart
Until SETTASK is executed (initialized to $00000000), only PC0 is running, making the cog seem normal.
SETTASK #%%3210 ...would enable all tasks. If no JMPTASK was done, PC1..PC3 would begin execution from $001..$003 (better have some JMP's there)
When you do an immediate SETTASK #, the lower 8 bits of immediate data are replicated four times to fill 32 bits. To get more granularity, you could do a register, instead of an immediate, and 32 unique bits would be loaded into the task register, which rotates right after each instruction completion, with the 2 LSB's determining which task to execute next.

Example:

        org

        jmp #task0
        jmp #task1
        jmp #task2
        jmp #task3

task0 settask #%%3210 'turn on all tasks

:loop notp #0 'toggle P0
        jmp #:loop

task1 notp #1 'toggle P1
        jmp #task1

task2 notp #2 'toggle P2
        jmp #task2

task3 notp #3 'toggle P3
        jmp #task3