{{12 Sep 09   Harprit Sandhu

BlinkLED.spin

Propeller Tool Ver. 1.2.6

Chapter 02 Prog 01

This program turns an LED ON and OFF, with a programmable delay

It demonstrates the use of methods in an absolutely minimal way.

Since the clock is 10 MHz

Define the constants we will use.

}}

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ = 5_000_000           'the crystal frequency

inv_high      =0               'define the inverted High state

inv_low       =1               'define the inverted Low state

waitPeriod    =6_000_000       'about 1/2 sec switch cycle

output_pin    =27              'line the led is on

'High is defined as 0 and low is defined as a 1 because we are using an

'inverting buffer on the Propeller output

PUB Go

dira [output_pin]~~           'sets pin to an output line with ~~ notation

outa [output_pin]~~           'makes the pin high

repeat                        'repeat forever, no number after repeat

turnOff_LED                'method call

wait                       'method call

turnOn_LED                 'method call

wait                       'method call

PRI turnOn_LED                  'method to set the LED line high

outa[output_pin] :=inv_high 'line that actually sets the LED high

PRI turnOff_LED                 'method to set the LED line low

outa[output_pin] :=inv_low  'line that actually sets the LED low

PRI wait                        'delay method

waitCnt(waitPeriod + cnt)   'delay is specified by the waitPeriod

{{ Aug 31 09      Harprit Sandhu

FreqGen8.Spin

Propeller Tool Ver. 1.2.6

Chapter 03 Prog 01

This program generates 8 frequencies starting at 440 cycles/sec.

Depends on the position of Pot 1

}}

CON

_CLKMODE=XTAL1+ PLL2X      'The system clock spec

_XINFREQ = 5_000_000       'Crystal freq

Output     = 26            'output line for the speaker

Repfactor  = 100           'number of times to toggle line

VAR

{RAM assignment for cogs}

long  Stack1[50]       'this RAM will be assigned to COG1

long  Stack2[50]       'this RAM will be assigned to COG2

{variables used for reading pot}

word  PotValue         'value of the pot reading

long  NoteFreq         'actual frequency of the note

long  NoteDelay        'delay in cycles

{variables used in displaying LCD in Cog2}

'none

{variables used in GetTone}

Byte  toneNumber

OBJ                             'The Objects we will need for our calls

LCD  : "LCDRoutines4"         'for controlling the LCD

UTIL : "Utilities"            'for general methods

DAT

Tone word 440, 494, 523, 587, 659, 698, 784, 880

PUB GO                          'The main method in this program

'the potentiometer is read in this cog

cognew (COG_LCD,   @Stack1)   'create COG_TWO for LCD display

cognew (COG_PLAY,  @Stack2)   'create COG_THREE for toggling output

repeat                        'start repeat loop

PotValue:=UTIL.Read3202_0       'get potValue from the utilities

ToneNumber:=Potvalue/512 +1     'This reduces the value to 0-15

PRI COG_LCD                        'Handles display  to the LCD

LCD.INITIALIZE_LCD               'set up the LCD

REPEAT                           'repeat write to the LCD

LCD.POSITION (1,1)            'Go to 1st line 1st space

LCD.PRINT(STRING("PotPos =")) 'Potentiometer position

LCD.PRINT_DEC(ToneNumber)     'print the tune number

LCD.SPACE(2)                  'erase over overflows

LCD.POSITION (2,1)            'Go to 2nd line 1st space

LCD.PRINT(STRING("FreqOut=")) 'frequency label printed

LCD.PRINT_DEC(NoteFreq)       'print note cps

LCD.SPACE(2)                  'erase over overflows

PRI COG_PLAY                       'output for speaker

dira[Output]~~                   'output pin

repeat                           'outer loop

repeat RepFactor               'inner loop and repeat #

GetTone                      'gets value for NoteFre

!OUTA[output]                'toggle output line

NoteDelay:=12_000_000/(NoteFreq*2)   'calculate the delay

waitcnt(NoteDelay +cnt)       'wait for delay to synthesize freq

waitcnt(clkfreq/2+cnt)

PUB GetTone                       'gets the frequency to be played

NoteFreq := Tone[toneNumber-1]  'looks up position in DAT statements

{{12 Sep 09   Harprit Sandhu

BlinkLED.spin

Propeller Tool Ver. 1.2.6

Chapter04 Program 01

This program turns an LED ON and OFF, with a programmable delay

It demonstrates the use of methods in an absolutely minimal way.

Since the clock is 10 MHz

Define the constants we will use.

}}

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ = 5_000_000           'the crystal frequency

inv_high      =0               'define the inverted High state

inv_low       =1               'define the inverted Low state

waitPeriod    =6_000_000       'about 1/2 sec switch cycle

output_pin    =27              'line the led is on

'High is defined as 0 and low is defined as a 1 because we are using an

'inverting buffer on the Propeller output

PUB Go

dira [output_pin]~~           'sets pin to an output line with ~~ notation

outa [output_pin]~~           'makes the pin high

repeat                        'repeat forever, no number after repeat

turnOff_LED                'method call

wait                       'method call

turnOn_LED                 'method call

wait                       'method call

PRI turnOn_LED                  'method to set the LED line high

outa[output_pin] :=inv_high 'line that actually sets the LED high

PRI turnOff_LED                 'method to set the LED line low

outa[output_pin] :=inv_low  'line that actually sets the LED low

PRI wait                        'delay method

waitCnt(waitPeriod + cnt)   'delay is specified by the waitPeriod

{Chapter 7  Program 1  }

PRI

repeat                             'power PWM routine.

phsa:=PulseWidth                'Send a high pulse for PulseWidth counts

period:=period + Cycle_time     'Calculate cycle time

waitcnt(period)                 'Wait for the cycle time

{{14 Sep 09   Harprit Sandhu

PWM.spin

Propeller Tool Ver 1.2.6

Chapter 07 Program 02

This program generates a fixed PWM. Meaning that as programmed

the width does not vary. (Set at 50%) It is easy to recognise

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000          'crystal frequency

VAR

long pulsewidth           '

long cycle_time           '

long period               '

'

PUB Go

dira[7]~~                            'set output line

ctra[30..26]:=%00100                 'run PWM mode

ctra[5..0]:=7                        'Set the "A pin" of this cog

frqa:=1                              'Set this counter's frqa value to 1

PulseWidth:=-5000                    'Start with position=5_000

Cycle_time:=clkfreq/1000             'Set the time for the pulse width to 1 ms

period:=cnt                          'Store the current value of the counter

repeat                               'PWM routine.

phsa:=PulseWidth                   'Send a high pulse for PulseWidth counts

period:=period + Cycle_time        'Calculate cycle time

waitcnt(period)                    'Wait for the cycle time

{{14 Sep 09   Harprit Sandhu

PWM1.spin

Propeller Tool Ver 1.2.6

Chapter 07 Progarm 03

This program generates a variable PWM signal.

Based on a potentiometer reading

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000          'crystal frequency

VAR

long stack1[25]               'space for motor

long stack2[25]               'space for LCD

long pulsewidth               '

word pot                      '

OBJ

LCD     : "LCDRoutines4"      'for the LCD methods

UTIL    : "Utilities"         'for general methods

PUB Go

cognew(RunMotor(7),@Stack1)

cognew(LCD_manager,@stack2)

repeat

Pot:=UTIL.read3202_0              'read the pot at MCP3202  line 0

PUB RunMotor(Pin)|Cycle_time,period    'method to toggle the output

dira[7]~~                            'gain access to these three amplifier lines

dira[19..20]~                        'potentiometer location

ctra[30..26]:=%00100                 'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                      'Set the "A pin" of this cog to Pin

frqa:=1                              'Set this counter's frqa value to 1

PulseWidth:=50                       'Start with position=50

Cycle_time:=clkfreq/1000             'Set the time for the pulse width to 10 ms

period:=cnt                          'Store the current value of the counter

repeat                               'power PWM routine.

phsa:=-(pot*244/100)               'Send a high pulse for PulseWidth counts

period:=period+Cycle_time          'Calculate cycle time

waitcnt(period)                    'Wait for the cycle time to complete

PRI LCD_manager

LCD.INITIALIZE_LCD                 'initialize the LCD

repeat                             'LCD loop

LCD.POSITION (1,1)               'Go to 1st line 1st space

LCD.PRINT(STRING("Pot=" ))       'Potentiometer position ID

LCD.PRINT_DEC(pot)               'print the pot reading

LCD.SPACE(5)                     'erase over old data

{Chapter 9  Program 1  }

PRI

repeat                             'movement loop

iters:=pot2                      'set number of iterations to perform

index:=0                         'reset index

repeat iters                     'do iterations

index:=index+1                 'increment index

targetPosition:=targetPosition+index   'set new position

waitcnt(clkfreq/Pot1+cnt)              'wait time for iteration

repeat iters                     'now do the slow down

index:=index-1

targetPosition:=targetPosition+index

waitcnt(clkfreq/Pot1+cnt)

repeat while startFlag==0        'wait till done

waitcnt(clkfreq+cnt)             'delay to see stop

targetPosition:=startPosition    'set to go back

waitcnt(24_000+cnt)              'wait to get done

repeat while startFlag==0        'wait till done

waitcnt(clkfreq+cnt)             'delay to see stop

{{04 June 09     Harprit Sandhu

BlinkMethod.spin

Propeller Tool Ver. 1.2.6

Chapter 10 Program 01

Blinking an LED

This program turns an LED ON an OFF and demonstrates the use of subroutines

in an absolutely minimal way.

Define the constants we will use.

Propeller font schematic:

│   100 Ω

21├──────────┐

│         LED    │

 GND

}}

CON                             'CON defines the constants

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000          'external crystal

pin           =27              'select the pin to be used for the LED

waitPeriod    =500             'set the wait period

high          =1               'define the High state

low           =0               'define the Low state

{{

The following PUB Go is the main part of the program.

Everything else is in the 3 called Methods

}}

PUB Go

dira [pin]~~                   'sets pin to an output line with the ~~ notation

repeat                         'specifies times to repeat. Blank=forever

turnOn_LED                   'these 4 Methods are called by name alone

wait                         'these 4 Methods are called by name alone

turnOff_LED                  'these 4 Methods are called by name alone

wait                         'these 4 Methods are called by name alone

PRI turnOn_LED                   'Method to set the LED line high

outa[pin] :=high             'line that actually sets the LED high

PRI turnOff_LED                  'Method to set the LED line low

outa[pin] :=low              'line that actually sets the LED low

PRI wait                         'Method defines the delay

waitCnt((Clkfreq/1000)*waitperiod +cnt)  'wait till counter reaches this value

{{12 Sep 09   Harprit Sandhu

BlinkLED.spin

Propeller Tool Ver. 1.2.6

Chapter13 Program 1

This program turns an LED ON and OFF, with a programmable delay

It demonstrates the use of methods in an absolutely minimal way.

Since the clock is 10 MHz

Define the constants we will use.

}}

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ = 5_000_000           'the crystal frequency

inv_high      =0               'define the inverted High state

inv_low       =1               'define the inverted Low state

waitPeriod    =6_000_000       'about 1/2 sec switch cycle

output_pin    =27              'line the led is on

'High is defined as 0 and low is defined as a 1 because we are using an

'inverting buffer on the Propeller output

PUB Go

dira [output_pin]~~           'sets pin to an output line with ~~ notation

outa [output_pin]~~           'makes the pin high

repeat                        'repeat forever, no number after repeat

turnOff_LED                'method call

wait                       'method call

turnOn_LED                 'method call

wait                       'method call

PRI turnOn_LED                  'method to set the LED line high

outa[output_pin] :=inv_high 'line that actually sets the LED high

PRI turnOff_LED                 'method to set the LED line low

outa[output_pin] :=inv_low  'line that actually sets the LED low

PRI wait                        'delay method

waitCnt(waitPeriod + cnt)   'delay is specified by the waitPeriod

{{11 Sep 09     Harprit Sandhu

LCDminimal.spin

Propeller Tool Ver 1.2.6

Chapter 14  Program 1

PROGRAM TO BEGIN USING THE LCD

A minimal LCD implementation to allow us to use the LCD in our

experiments immediately.

This program is an absolutely minimal implementation to

make the LCD usable. You can work on improving it. We will improve it later

┌────────────┐

Schematic                                               │ ┌────────┐ │

│ │ ┌────┐ │ │

│ │ │    │ │ │

POWER ETC:

┌─────────-───-───────────────┴─┴─┴─┴─┴─┴┐   │ │ │

BASIC CONNECTIONS   │ 1 0 9 8 7 6 5 4│3 X X G│3 2 1 0 9 8 7 6│   │ │ │

FOR THE EDUCATION   │                │       │               │   │ │ │

KIT ARE STANDARD    │    Propeller   │       │     CHIP      │   │ │ │

CONNECTIONS AND ARE │ 0 1 2 3 4 5 6 7│G B R 3│8 9 0 1 2 3 4 5│   │ │ │

NOT SHOWN HERE

└─────────────────────────┬─┬─┬─┬─┬─┬─┬─┬┘   │ │ │

│ │ │ │ │ │ │ │    │ │ │

┌─────┼─┼─┼─┼─┼─┼─┼─┼────┼─┼─┘

│ ┌───┼─┼─┼─┼─┼─┼─┼─┼────┼─┘

5VDC  │ │ ┌─┼─┼─┼─┼─┼─┼─┼─┼────┘

   │ │ │ │ │ │ │ │ │ │ │

│   │ │ │ │ │ │ │ │ │ │ │

│   │ │ │ │ │ │ │ │ │ │ │

┌──────────┳─┼─┐ │ │ │ │ │ │ │ │ │ │ │

│          │ │ │ │ │ │ │ │ │ │ │ │ │ │

│

┌────┴─┴─┴─┴─┴─┴─┴─┴─┴─┴─┴─┴─┴─┴─────---------────┐

│     │    G 5 G S W E 0 1 2 3 4 5 6 7                  │

│     │

┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐  │

│     │

└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘  │

│     │

┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐  │

│     │

└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘  │

│

└───────────────────────────────────────---------─┘

│      16 CHAR BY 2 LINE LCD DISPLAY

 GND  8 BIT MODE

Revisions

Pin assignment are assigned as constants because the pins are fixed.

These numbers reflect the actual wiring on the board between the Propeller

and the 16x2 LCD display. If you want the LCD on other lines, that would

have to be specified here.  We are going to use 8 bit mode to transfer data for

now.  All these numbers refer to lines on the Propeller

}}

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ = 5_000_000           'the crystal frequency

RegSelect     = 16

ReadWrite     = 17

Enable        = 18

DataBit0      = 8

DataBit7      = 15

waitPeriod    =500_000                  'set the wait period

high          =1                        'define the High state

low           =0                        'define the Low state

{{

Defining high and low states will allow us to invert these when we use

buffers to amplify the output from the prop chip.  We will then make

low=1 and high=0 thus inverting all the values throughout the program

}}

PUB Go

DIRA[DataBit7..DataBit0]:=%11111111  'the lines for the LCD are outputs

DIRA[RegSelect] := High         'the lines for the LCD are outputs

DIRA[ReadWrite] := High         'the lines for the LCD are outputs

DIRA[Enable]    := High         'the lines for the LCD are outputs

INITIALIZE_LCD                  'initialize the LCD

waitcnt(1_000_000+cnt)          'wait for LCD to start up

CLEAR                           'clear the LCD

repeat 4                        'print 4 'A's

SEND_CHAR ("A")

repeat 4                        'print 4 'a's

SEND_CHAR ("b")

POSITION (1,2)                  'move to POSITION: line 2, space 1

repeat 4                        'print 4 'B's

SEND_CHAR ("C")

repeat 4                        'print 4 'b's

SEND_CHAR ("d")

repeat                          'this is a parking loop to keep the system

'from shutting down. It just loops here

'see what cursor does if it is omitted

PRI INITIALIZE_LCD                'The addresses and data used here are

waitcnt(500_000+cnt)            'specified in the Hitachi data sheet for

'display. YOU MUST CHECK THIS FOR YOURSELF

OUTA[RegSelect] := Low          'these three lines are specified to write

OUTA[ReadWrite] := Low          'the initial set up bits for the LCD

OUTA[Enable]    := Low          'See Hitachi HD44780 data sheet

'display. YOU MUST CHECK THIS FOR YOURSELF.

SEND_INSTRUCTION (%0011_0000)   'Send 1st

waitcnt(49_200+cnt)             'wait

SEND_INSTRUCTION (%0011_0000)   'Send 2nd

waitcnt(1_200+cnt)              'wait

SEND_INSTRUCTION (%0011_0000)   'Send 3rd

waitcnt(12_000+cnt)             'wait

SEND_INSTRUCTION (%0011_1000)   'Sets DL=8 bits, N=2 lines, F=5x7 font

SEND_INSTRUCTION (%0000_1111)   'Display on, Cursor on, Blink on

SEND_INSTRUCTION (%0000_0001)   'clear LCD

SEND_INSTRUCTION (%0000_0110)   'Move Cursor, Do not shift display

PUB CLEAR                          'Clear the LCD display and go home

SEND_INSTRUCTION (%0000_0001)

PUB POSITION (LINE_NUMBER, HOR_POSITION) | CHAR_LOCATION

'Position cursor

'HOR_POSITION : Horizontal Position : 1 to 16

'LINE_NUMBER : Line Number : 1 or 2

CHAR_LOCATION := (HOR_POSITION-1) * 64  'figure location

CHAR_LOCATION += (LINE_NUMBER-1) + 128  'figure location

SEND_INSTRUCTION (CHAR_LOCATION)   'send the instr to position cursor

PUB SEND_CHAR (DISPLAY_DATA)   'set up for writing to the display

CHECK_BUSY                   'wait for busy bit to clear before sending

OUTA[ReadWrite] := Low       'Set up to read busy bit

OUTA[RegSelect] := High      'Set up to read busy bit

OUTA[Enable]    := High      'Set up to toggle bit H>L

OUTA[DataBit7..DataBit0] := DISPLAY_DATA    'Ready to SEND data in

OUTA[Enable]    := Low       'Toggle the bit H>L

PUB CHECK_BUSY | BUSY_BIT       'routine to check busy bit

OUTA[ReadWrite] := High       'Set to read the busy bit

OUTA[RegSelect] := Low        'Set to read the busy bit

DIRA[DataBit7..DataBit0] := %0000_0000  'Set the entire port to be an input

REPEAT                        'Keep doing it till clear

OUTA[Enable]  := High       'set to 1 to get ready to toggle H>L this bit

BUSY_BIT := INA[DataBit7]   'the busy bit is bit 7 of the byte read

OUTA[Enable]  := Low        'make the enable bit go low for H>L toggle

WHILE (BUSY_BIT == 1)         'do it as long as the busy bit is 1

DIRA[DataBit7..DataBit0] := %1111_1111  'set the data port back to outputs

PUB SEND_INSTRUCTION (DISPLAY_DATA) 'set up for writing instructions

CHECK_BUSY                   'wait for busy bit to clear before sending

OUTA[ReadWrite] := Low       'Set up to read busy bit

OUTA[RegSelect] := Low       'Set up to read busy bit

OUTA[Enable]    := High      'Set up to toggle bit H>L

OUTA[DataBit7..DataBit0] := DISPLAY_DATA    'Ready to READ data in

OUTA[Enable]    := Low        'Toggle the bit H>L

{{12 Sep 09      Harprit Sandhu

ButtonLED.spin

Propeller Tool 1.2.6

Chapter 15 Prog 01

This program turns an LED ON if an input that has been pulled up is grounded

It demonstrates the use of subroutines in an absolutely minimal way.

First define the constants we will use.

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ      = 5_000_000

input_pin     =23            'select the pin to be used for input

output_pin    =27            'select the pin to be used for the LED

inv_high      =0             'define the inverted High state

inv_low       =1             'define the inverted Low state

'High is defined as 0 and low is defined as a 1 because we are using an

'inverting buffer on the output

PUB Go

dira [output_pin]~~   'sets pin to an output line with ~~ notation

outa [output_pin]~    'makes the pin a low output

dira [input_pin]~     'sets pin to an input line with the ~ notation

repeat                'repeat forever because there is no number after repeat

if ina[input_pin]==0    'check pin for high or low

turnOn_LED         'subroutine call

else

turnOff_LED       'subroutine call

PRI turnOn_LED                  'subroutine to set the LED line high

outa[output_pin] :=inv_high 'line that actually sets the LED high

PRI turnOff_LED                 'subroutine to set the LED line low

outa[output_pin] :=inv_low  'line that actually sets the LED low

{{Aug 31 09   Harprit Sandhu

ReadPot.spin

Propeller Tool Version 1.2.6

Chapter 16 Prog 01

READING A POTENTIOMETER

This routine ready a 10K pot with a 10 mfd cap

This routine is what is used in the utilities to read the pot

Pot is always read from the same line

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000          'Crystal spec

PotLine   = 19          'line the pot it on

OBJ

LCD : "LCDRoutines4"     'We will be using these METHODS in this program

VAR                       'these are the variables we will use.

long  startCnt         'count at start

long  endCount         'count at end

long  delay            'time difference

long  PotValue         'Value of the pot reading

PUB Go

LCD.INITIALIZE_LCD           'set up the LCD

repeat                       'loop

dira[PotLine]~~            'set potline as output

outa[PotLine]~~            'make it high so we can charge the capacitor

waitcnt(4000+cnt)          'wait for the capacitor to get charged

dira[PotLine]~             'make potline an input. line switches H>L

startCnt:=cnt              'read the counter at start of cycle and store

repeat                     'go into an endless loop

while ina[PotLine]~~       'keep doing it as long as the potline is high

EndCount := cnt            'read the counter at end of cycle and store

delay := ((EndCount-StartCnt)-1184)   'calculate time for line to go H>L

if delay>630000             'max permitted delay

delay:=630000             'clamp delay

PotValue:=(delay/2220)      'This reduces the value to 0-255 or 1 byte

PotValue <#=255             'clamp range

PotValue #>=1               'clamp range

LCD.POSITION (1,1)            'Go to 1st line 1st space

LCD.PRINT(STRING("PotPos =")) 'Potentiometer position

LCD.PRINT_DEC(PotValue)       'print value

LCD.SPACE(3)                  'erase over overflows

LCD.POSITION (2,1)            'Go to 2nd line 1st space

LCD.PRINT(STRING("Delay  =")) 'Print

LCD.PRINT_DEC(delay)          'print value

LCD.SPACE(3)                  'erase over overflows

{{11 Sep 09     Harprit Sandhu

Segment

Propeller Tool Ver 1.2.6

Chapter 16  Program 2

}}

PUB GetPotVal

dira[PotLine]~~                'set potline as output

valutotal:=0                   'clear total

repeat  repval               'repeat

dira[PotLine]~~            'set potline as output

outa[PotLine]~~            'make it high so we can charge the capacitor

waitcnt(4000+cnt)          'wait for the capacitor to get charged

dira[PotLine]~             'make potline an input. line switches H>L

startCnt:=cnt              'read the counter at start of cycle and store

repeat                     'go into an endless loop

while ina[PotLine]~~       'keep doing it as long as the potline is high

EndCount := cnt            'read the counter at end of cycle and store

delay := ((EndCount-StartCnt)-1184)   'calculate time for line to go H>L

if delay>610_000            'max permitted delay

delay:=610_000            'clamp delay

PotValue:=(delay/2300)      'This reduces the value to 0-255 or 1 byte

valutotal:=valutotal+potvalue    'figures total

potvalue:=valutotal/repval  'figure average

potvalue <#=255

potvalue #>=0

result:=PotValue                'figure average

{{03 Nov 09   Harprit Sandhu

MCP3202Read1.Spin

Version 1.00.00

Propeller Tool 1.2.6

Chapter 16 Prog 03

All the code in this program is in SPIN

This program reads channel 0 of the MCP3202 and displays the results

on the LCD both as a decimal value and as a binary value so that you

can see the bits flip as you turn the potentiometer.

The 3202 chip is connected as follows:

1 Chip select                                          P21

2 Channel 0 for voltage input from Pot                 Pot wiper

3 Channel 1 for voltage input from Pot, not used       Ground it

4 Ground Vss                                           Ground

5 Data into 3202 for setup                             P19

6 Data out from 3202 to be read into Propeller         P22

7 Clock to read in the data                            P20

8 Power 5 volts Vdd                                    5 volts

The Potentiometer is connected as follows:

Left    Ground

Center  To pin 2 of the 3202

Right   Power  5 volts

I used a 50K Pot

The connections to the LCD are as follows:

1   Ground

2   Power 5 volts

3   Ground

4   P16

5   P17

6   P18

7   Not connected, using 4 bit mode for data Xfer

8   Not connected, using 4 bit mode for data Xfer

9   Not connected, using 4 bit mode for data Xfer

10  Not connected, using 4 bit mode for data Xfer

11  Data  high nibble

12  Data  high nibble

13  Data  high nibble

14  Data  high nibble

STANDARD EDUCATION KIT SET UP.  Used as base

Revisions:

Error Reporting:

Please report errors to harprit.sandhu@gmail.com

}}

OBJ

LCD     : "LCDRoutines4" 'for the LCD methods

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000          'crystal spec

BitsRead =12

chipSel  = 19

chipClk  = chipSel+1

chipDout = chipSel+2

chipDin  = chipSel+3

VAR

long stack2[25]

word PotReading

word DataRead

PUB Go

cognew(Cog_LCD, @stack2)

DIRA[0..7]~

DIRA[chipSel]~~     'osc once to set up 3202

DIRA[chipDin]~~     'data set up to the chip

DIRA[chipDout]~     'data from the chip to the Propeller

DIRA[chipClk]~~     'oscillates to read in data from internals

repeat

DataRead:=0             'Clear out old data

outa[chipSel]~~         'Chip select has to be high to start off

outa[chipSel]~          'Go low to start process

outa[chipClk]~          'Clock MUST be low to load data

outa[chipDin]~~         'must start with Din high to set up 3202

outa[chipClk]~~         'Clock high to read data in

outa[chipClk]~          'Low to load

outa[chipDin]~~         'High single mode

outa[chipClk]~~         'High to read

outa[chipClk]~          'Low to load

outa[chipDin]~          'Odd = low channel 0

outa[chipClk]~~         'High to read

outa[chipClk]~          'Low to load

outa[chipDin]~~         'msbf high = MSB first

outa[chipClk]~~         'High to read

outa[chipDin]~          'making line low for rest of cycle

outa[chipClk]~          'Low to load Read/discard the null bit

outa[chipClk]~~         'High to read

repeat BitsRead          'Reads the data into DataRead in 12 steps

DataRead <<= 1         'Move data by shifting left 1 bit. Ready for next bit

outa[chipClk]~         'Low to load

DataRead:=DataRead+ina[chipDout]  'Xfer the data from pin chipDout

outa[chipClk]~~        'High to read

outa[chipSel]~~          'Put chip to sleep, for low power

PotReading:=DataRead     'Finished data read for display

PRI cog_LCD                      'manage the LCD

LCD.INITIALIZE_LCD             'initialize the LCD

repeat

LCD.POSITION (1,1)           'Go to 1st line 1st space

LCD.PRINT(STRING("Pot=" ))   'Print Label

LCD.PRINT_DEC(PotReading)    'print decimal value

LCD.SPACE(4)                 'erase over old data

LCD.POSITION (2,1)           'Go to 2nd line 1st space

LCD.PRINT_BIN(PotReading,BitsRead)   'Print it as bits.

{{12 Sep 09    Harprit Sandhu

BlinkLEDpot.spin

Propeller Tool Ver. 1.2.6

Chapter 16 Program 04

This program turns an LED ON and OFF, with a pot set delay

Define the constants we will use

}}

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ = 5_000_000           'the crystal frequency

inv_high      =0               'define the inverted High state

inv_low       =1               'define the inverted Low state

output_pin    =27

'High is defined as 0 and low is defined as a 1 because we are using an

'inverting buffer on the Propeller output

VAR

long   Potvalue

long   WaitPeriod

byte   div             'dividing factor for clock freq

OBJ                      'These are the methods we will need

LCD  : "LCDRoutines4"  'for the LCD methods

UTIL : "Utilities"     'for general methods

PUB Go

dira [output_pin]~~           'sets pin to an output line with ~~ notation

outa [output_pin]~~           'makes the pin high

LCD.INITIALIZE_LCD            'initialize the LCD

repeat                        'repeat forever, no number after repeat

PotValue:=UTIL.read3202_0  'reads the potentiometer

DIV:=1+PotValue/64         'adding 1 keeps value from going to zero

turnOff_LED                'method call

wait                       'method call

turnOn_LED                 'method call

wait                       'method call

LCD.POSITION (1,1)            'Go to 1st line 1st space

LCD.PRINT(STRING("Pot=" ))    'dividing value

LCD.PRINT_DEC(PotValue)       'print value

LCD.SPACE(2)                  'erase over old data

LCD.POSITION (2,1)            'Go to 2nd line 1st space

LCD.PRINT(STRING("Div=" ))    'dividing value

LCD.PRINT_DEC(div)            'print value

LCD.SPACE(2)                  'erase over old data

PRI turnOn_LED                   'method to set the LED line high

outa[output_pin] :=inv_high  'line that actually sets the LED high

PRI turnOff_LED                  'method to set the LED line low

outa[output_pin] :=inv_low   'line that actually sets the LED low

PRI wait                         'delay method

waitCnt(clkfreq/div + cnt)   'delay is specified by the div

{{11 Sep 09     Harprit Sandhu

Segment

Propeller Tool Ver 1.2.6

Chapter 17  Program 1

}}

PUB segment

dira[output]~~                     'output pin

repeat                             'loop

!OUTA[output]                  'toggle output line

waitcnt(11_364 +cnt)           'wait for the A4 freq

{{12 Sep 09    Harprit Sandhu

Play8Notes.spin

Propeller Tool Ver. 1.2.6

Chapter 17  Program 02

This program plays 8 notes, bare bones

Define the constants we will use

}}

CON

_CLKMODE=XTAL1 + PLL2X            'The system clock spec

_XINFREQ  = 5_000_000              'the crystal frequency

repfactor =500                     'number of times repeated

delayfact =1_000_000               'delay between notes

output    = 25

PUB Go

dira[output]~~                       'output pin

repeat                             'outer loop

repeat repfactor

!OUTA[output]                  'toggle output line

waitcnt(13_636 +cnt)           'wait to synthesize freq

waitcnt(delayfact+cnt)           'wait

repeat repfactor

!OUTA[output]                  'toggle output line

waitcnt(12_170 +cnt)           'wait to synthesize freq

waitcnt(delayfact+cnt)           'wait

repeat repfactor

!OUTA[output]                  'toggle output line

waitcnt(11470 +cnt)            'wait to synthesize freq

waitcnt(delayfact+cnt)           'wait

repeat repfactor

!OUTA[output]                  'toggle output line

waitcnt(10221 +cnt)            'wait to synthesize freq

waitcnt(delayfact+cnt)           'wait

repeat repfactor

!OUTA[output]                  'toggle output line

waitcnt(9104 +cnt)             'wait to synthesize freq

waitcnt(delayfact+cnt)           'wait

repeat repfactor

!OUTA[output]                  'toggle output line

waitcnt(8595 +cnt)             'wait to synthesize freq

waitcnt(delayfact+cnt)           'wait

repeat repfactor

!OUTA[output]                  'toggle output line

waitcnt(7639 +cnt)             'wait to synthesize freq

waitcnt(delayfact+cnt)           'wait

repeat repfactor

!OUTA[output]                  'toggle output line

waitcnt(6818 +cnt)             'wait to synthesize freq

waitcnt(delayfact+cnt)           'wait

{{ Aug 31 09      Harprit Sandhu

FreqGen8.Spin

Propeller Tool Ver. 1.2.6

Chapter 17 Program 3

This program generates 8 frequencies starting at 440 cycles/sec.

Depends on the position of Pot 1

}}

CON

_CLKMODE=XTAL1+ PLL2X      'The system clock spec

_XINFREQ = 5_000_000       'Crystal freq

Output     = 26            'output line for the speaker

Repfactor  = 100           'number of times to toggle line

VAR

{RAM assignment for cogs}

long  Stack1[50]       'this RAM will be assigned to COG1

long  Stack2[50]       'this RAM will be assigned to COG2

{variables used for reading pot}

word  PotValue         'value of the pot reading

long  NoteFreq         'actual frequency of the note

long  NoteDelay        'delay in cycles

{variables used in displaying LCD in Cog2}

'none

{variables used in GetTone}

Byte  toneNumber

OBJ                             'The Objects we will need for our calls

LCD  : "LCDRoutines4"         'for controlling the LCD

UTIL : "Utilities"            'for general methods

DAT

Tone word 440, 494, 523, 587, 659, 698, 784, 880

PUB GO                          'The main method in this program

'the potentiometer is read in this cog

cognew (COG_LCD,   @Stack1)   'create COG_TWO for LCD display

cognew (COG_PLAY,  @Stack2)   'create COG_THREE for toggling output

repeat                        'start repeat loop

PotValue:=UTIL.Read3202_0       'get potValue from the utilities

ToneNumber:=Potvalue/512 +1     'This reduces the value to 0-15

PRI COG_LCD                        'Handles display  to the LCD

LCD.INITIALIZE_LCD               'set up the LCD

REPEAT                           'repeat write to the LCD

LCD.POSITION (1,1)            'Go to 1st line 1st space

LCD.PRINT(STRING("PotPos =")) 'Potentiometer position

LCD.PRINT_DEC(ToneNumber)     'print the tune number

LCD.SPACE(2)                  'erase over overflows

LCD.POSITION (2,1)            'Go to 2nd line 1st space

LCD.PRINT(STRING("FreqOut=")) 'frequency label printed

LCD.PRINT_DEC(NoteFreq)       'print note cps

LCD.SPACE(2)                  'erase over overflows

PRI COG_PLAY                       'output for speaker

dira[Output]~~                   'output pin

repeat                           'outer loop

repeat RepFactor               'inner loop and repeat #

GetTone                      'gets value for NoteFre

!OUTA[output]                'toggle output line

NoteDelay:=12_000_000/(NoteFreq*2)   'calculate the delay

waitcnt(NoteDelay +cnt)       'wait for delay to synthesize freq

waitcnt(clkfreq/2+cnt)

PUB GetTone                       'gets the frequency to be played

NoteFreq := Tone[toneNumber-1]  'looks up position in DAT statements

{{05 Oct 09     Harprit Sandhu

FreqCounter.Spin

Propeller Tool Ver 1.2.6

Chapter 17 Prog 04

The program reads the frequency of a signal on the Input

line and displays it on the LCD. The signal is read as the

number of waves in 1 second. Controlled by Pot 1

Four Cogs are used

COG GO reads the frequency

COG COG_LCD displays values on LCD

COG FREQ_GEN generates the frequency

COG COG_OUT generates the 5 freq

}}

CON

_CLKMODE=XTAL1+ PLL2X  'The system clock spec

_XINFREQ = 5_000_000   'crystal

freq5    =25           '5X freq line

input    =26           'line for input for what is to be read

output   =27           'line for output of what is generated

VAR                       'these are the variables

long  Stack[50]         'For CogOne

long  Stack1[50]        'For freq_gen

long  Stack2[50]        'For freq_out

long  Freq              'read frequency

long  startTMR

long  StopTMR

long  elapsed

long  pot

OBJ                           'These are the methods we will need

LCD  : "LCDRoutines4"       'for controlling the LCD

UTIL : "Utilities"          'for general methods

PUB GO                        'This the main method in this program

Cognew (COG_LCD, @Stack)    'create Cog_TWO

Cognew (FREQ_GEN, @Stack1)  'create freq generator

Cognew (COG_OUT, @Stack2)   'create freq out

dira[input]~

repeat

repeat

while ina[input]==0        'hold at low

startTMR:=cnt              'start timer

repeat

while ina[input]==1        'hold at high

repeat

while ina[input]==0        'hold at low

stopTMR:=cnt               'read timer

elapsed:=stopTMR-startTMR

freq:=10_000_000/elapsed

pot:=util.read3202_0        'read Pot 1

PRI COG_LCD                     'This is the display, the LCD

LCD.INITIALIZE_LCD            'initialize up the LCD

REPEAT                        'Routine to write to the LCD

LCD.POSITION (1,1)         '

LCD.PRINT(STRING("FRQ="))  'Frequency

LCD.PRINT_DEC(Freq)        'print freq

LCD.SPACE(2)               'erase old data

LCD.POSITION (2,1)         '

LCD.PRINT(STRING("POT="))  'Frequency

LCD.PRINT_DEC(Pot)         'print Pot reading

LCD.SPACE(2)               'erase old data

PRI FREQ_GEN                    'Freq generation based on pot reading

dira[output]~~                  'set output line

pot:=1000                    'arbitrary non zero value

repeat                       'loop

outa[output]~~             'make line high

waitcnt(clkfreq/pot+cnt)   'wait based on pot

outa[output]~              'make line low

waitcnt(clkfreq/pot+cnt)   'wait based on pot

PRI COG_OUT                        'output signal generation.

dira[freq5]~~                    'Set pin direction as output

freq:=1000                       'arbitrary non zero value

repeat                           'loop

outa[freq5]~~                  'make line high

waitcnt(clkfreq/freq/5+cnt)    'wait 1/5 time for 5X freq

outa[freq5]~                   'Make line low

waitcnt(clkfreq/freq/5+cnt)    'wait 1/5 time for 5X freq

{{13 Sep 09    Harprit Sandhu

MemsicWidth.spin

Propeller Tool Ver 1.2.6

Chapter 18 Prog 01

This program measures the pulse width and wave length output

from a Memsic 2125 gravity sensor as it is tilted from

the horizontal plane to the vertical plane

COG_LCD manages the LCD output

COG_0 measures the pulse

}}

CON

_CLKMODE=XTAL1+ PLL2X      'The system clock spec

_XINFREQ = 5_000_000       'crystal frequency

xaxis  = 25                 '

output = 26

VAR

long  Stack[55]              'FOR LCD COG

long  Stack1[55]             'FOR OUTPUT COG

long  startWave              '

long  endPulse               '

long  endWave                '

long  PulseLen               '

long  waveLen                '

long  frequency

OBJ                            'These are the Objects we will need

LCD  : "LCDRoutines4"        'for controlling the LCD

UTIL : "Utilities"           'for general methods collection

PUB go                           'Cog_0

cognew (COG_LCD, @Stack)       'starting up Cog LCD

cognew (COG_OUT, @Stack1)      'starting up Cog OUT

DIRA[25]~                      'Make pin input

repeat                         'Set up the control loop

repeat while ina[xaxis]==1       'wait for line 1 to go low. See Manual

repeat while ina[xaxis]==0       'wait for line 1 to go low. See Manual

'the above 2 lines make sure that we see

'aa full wave when we start measuring

repeat while ina[xaxis]==1       'wait for line 1 to go low. See Manual

startWave:=CNT                   'read the timer count

repeat while ina[xaxis]==0       'wait for line 1 to go low. See Manual

endPulse:=CNT                    'read the timer count for second time

repeat while ina[xaxis]==1       'wait for line 1 to go low. See Manual.

endWave:=cnt

PulseLen:=endPulse-startWave     'figure the pulse

waveLen:=endWave-startWave       'figure the wave Len

frequency:=10_000_000/waveLen    'figure the freq

waitcnt(clkfreq/25+cnt)

PRI COG_LCD                      'This is running in the new cog

LCD.INITIALIZE_LCD             'set up the LCD u

repeat                         'Print to LCD routine

LCD.POSITION (1,1)           'Position LCD cursor

LCD.PRINT(String("PL="))     'Pulse

'    LCD.PRINT_DEC((startWave))  'print value

'    LCD.SPACE(2)                'write over old data

LCD.PRINT_DEC((pulselen))    'print data

LCD.SPACE(2)                 'write over old data

LCD.POSITION (2,1)           'Position LCD cursor

LCD.PRINT(String("WL="))     'Wave Length

LCD.PRINT_DEC((wavelen))     'print value

LCD.SPACE(2)                 'write over old data

LCD.POSITION (2,11)          'Position LCD cursor

LCD.PRINT(String("FR="))     'Frequency

LCD.PRINT_DEC((frequency))   'print value

LCD.SPACE(4)                 'write over old data

PRI COG_OUT                      'output signal generation.

dira[output]~~                 'Set pin direction as output

repeat                         'loop

outa[output]~~               'make line high

waitcnt(pulselen/10+cnt)     'Create hi part of wave

outa[output]~                'Make line low

waitcnt(100_000-pulselen+cnt)'Create rest of wave

{Chapter 18  Program 2  }

PRI COG_OUT                         'output signal generation.

dira[output]~~                    'Set pin direction as output

repeat                            'loop

outa[output]~~                  'make line high

waitcnt(pulselen/5+cnt)         'Create hi part of wave

outa[output]~                   'Make line low

waitcnt(200_000-pulselen+cnt)   'Create rest of wave

{{05 Oct 09     Harprit Sandhu

FreqCounter.Spin

Propeller Tool Ver 1.2.6

Chapter 18 Program 3

The program reads the frequency of a signal on the Input

line and displays it on the LCD. The signal is read as the

number of waves in 1 second. Controlled by Pot 1

Four Cogs are used

COG GO reads the frequency

COG COG_LCD displays values on LCD

COG FREQ_GEN generates the frequency

COG COG_OUT generates the 5 freq

}}

CON

_CLKMODE=XTAL1+ PLL2X  'The system clock spec

_XINFREQ = 5_000_000   'crystal

freq5    =25           '5X freq line

input    =26           'line for input for what is to be read

output   =27           'line for output of what is generated

VAR                       'these are the variables

long  Stack[50]         'For CogOne

long  Stack1[50]        'For freq_gen

long  Stack2[50]        'For freq_out

long  Freq              'read frequency

long  startTMR

long  StopTMR

long  elapsed

long  pot

OBJ                           'These are the methods we will need

LCD  : "LCDRoutines4"       'for controlling the LCD

UTIL : "Utilities"          'for general methods

PUB GO                        'This the main method in this program

Cognew (COG_LCD, @Stack)    'create Cog_TWO

Cognew (FREQ_GEN, @Stack1)  'create freq generator

Cognew (COG_OUT, @Stack2)   'create freq out

dira[input]~

repeat

repeat

while ina[input]==0        'hold at low

startTMR:=cnt              'start timer

repeat

while ina[input]==1        'hold at high

repeat

while ina[input]==0        'hold at low

stopTMR:=cnt               'read timer

elapsed:=stopTMR-startTMR

freq:=10_000_000/elapsed

pot:=util.read3202_0        'read Pot 1

PRI COG_LCD                     'This is the display, the LCD

LCD.INITIALIZE_LCD            'initialize up the LCD

REPEAT                        'Routine to write to the LCD

LCD.POSITION (1,1)         '

LCD.PRINT(STRING("FRQ="))  'Frequency

LCD.PRINT_DEC(Freq)        'print freq

LCD.SPACE(2)               'erase old data

LCD.POSITION (2,1)         '

LCD.PRINT(STRING("POT="))  'Frequency

LCD.PRINT_DEC(Pot)         'print Pot reading

LCD.SPACE(2)               'erase old data

PRI FREQ_GEN                    'Freq generation based on pot reading

dira[output]~~                  'set output line

pot:=1000                    'arbitrary non zero value

repeat                       'loop

outa[output]~~             'make line high

waitcnt(clkfreq/pot+cnt)   'wait based on pot

outa[output]~              'make line low

waitcnt(clkfreq/pot+cnt)   'wait based on pot

PRI COG_OUT                        'output signal generation.

dira[freq5]~~                    'Set pin direction as output

freq:=1000                       'arbitrary non zero value

repeat                           'loop

outa[freq5]~~                  'make line high

waitcnt(clkfreq/freq/5+cnt)    'wait 1/5 time for 5X freq

outa[freq5]~                   'Make line low

waitcnt(clkfreq/freq/5+cnt)    'wait 1/5 time for 5X freq

{{28 Sep 09  Harprit Sandhu

7SegDisplay.spin 7SegDisplay.spin

Propeller Tool Ver 1.2.6

Chapter 19 Program 1

Program controls the segments on one 7 segment display

Pot is used to change the delay time

Place Segment Display on perf board as sown in Pictures.

}}

CON

_CLKMODE=XTAL1+ PLL2X       'The system clock spec

_XINFREQ     =5_000_000     '10 MHz

VAR                      'these are the variables we will use.

long stack1[35]        'space for 7 Seg driver

word delay             'duration for each number

byte index             'numbering index

OBJ                      'These are the methods we will need

UTIL : "Utilities"     'for general methods

PUB Go                          'main cog

cognew(SevSeg,@Stack1)   'start new cog for segs

repeat                        'this main cog's main loop

delay:=util.getpotval*8

PRI SevSeg                     '

dira[8..15]~~

index:=0

repeat

index+=1

'index:=8    'can freeze index at 8 to see all segs on

case index

1:

repeat delay

outa[8..15]:=%01_111_111     'These numbers build

outa[8..15]:=%11_111_111     'up the numbers shown

outa[8..15]:=%11_011_111     'segment at a time

outa[8..15]:=%11_111_111     'number at a time.

outa[8..15]:=%11_111_111     'a ZERO turns a segment on

outa[8..15]:=%11_111_111     'in a common anode system

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_110

2:

repeat delay

outa[8..15]:=%11_111_111

outa[8..15]:=%10_111_111

outa[8..15]:=%11_011_111

outa[8..15]:=%11_101_111

outa[8..15]:=%11_110_111

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_101

outa[8..15]:=%11_111_110

3:

repeat delay

outa[8..15]:=%11_111_111

outa[8..15]:=%10_111_111

outa[8..15]:=%11_111_111

outa[8..15]:=%11_101_111

outa[8..15]:=%11_110_111

outa[8..15]:=%11_111_011

outa[8..15]:=%11_111_101

outa[8..15]:=%11_111_110

4:

repeat delay

outa[8..15]:=%01_111_111

outa[8..15]:=%11_111_111

outa[8..15]:=%11_101_111

outa[8..15]:=%11_110_111

outa[8..15]:=%11_111_011

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_110

5:

repeat delay

outa[8..15]:=%01_111_111

outa[8..15]:=%10_111_111

outa[8..15]:=%11_110_111

outa[8..15]:=%11_111_011

outa[8..15]:=%11_111_101

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_110

6:

repeat delay

outa[8..15]:=%01_111_111

outa[8..15]:=%10_111_111

outa[8..15]:=%11_110_111

outa[8..15]:=%11_011_111

outa[8..15]:=%11_111_011

outa[8..15]:=%11_111_101

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_111

7:

repeat delay

outa[8..15]:=%11_111_111

outa[8..15]:=%10_111_111

outa[8..15]:=%11_101_111

outa[8..15]:=%11_111_011

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_111

8:

repeat delay

outa[8..15]:=%01_111_111

outa[8..15]:=%10_111_111

outa[8..15]:=%11_011_111

outa[8..15]:=%11_101_111

outa[8..15]:=%11_110_111

outa[8..15]:=%11_111_011

outa[8..15]:=%11_111_101

outa[8..15]:=%11_111_111

9:

repeat delay

outa[8..15]:=%01_111_111

outa[8..15]:=%10_111_111

outa[8..15]:=%11_101_111

outa[8..15]:=%11_110_111

outa[8..15]:=%11_111_011

outa[8..15]:=%11_111_101

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_111

10:

repeat delay

outa[8..15]:=%01_111_111

outa[8..15]:=%10_111_111

outa[8..15]:=%11_011_111

outa[8..15]:=%11_101_111

outa[8..15]:=%11_111_111

outa[8..15]:=%11_111_011

outa[8..15]:=%11_111_101

outa[8..15]:=%11_111_111

11:

repeat delay*20   'blanks display for a while

outa[8..15]:=%11_111_111

if index>11      'index reset value

index:=0

{{29 Sep 09   Harprit Sandhu

Metronom1.Spin

Propeller Tool Ver 1.2.6

Chapter 20 Prog 1

Creating pulses

An electronic metronome.

Standard is 40 to 208 BPM (beats per minute)

4 Cogs are used

Cog0 GO, toggles power line once a sec

Cog1 LCD, displays values on LCD

Cog2 Counts, toggles the speaker

Cog3 Calc, calculates the beats

}}

CON

_CLKMODE=XTAL1+ PLL2X    'The system clock spec

_XINFREQ   = 5_000_000   'crystal rate

Clickline    = 25      'Clicks speaker

LED2Line     = 26      'Toggles the 2nd LED

ledLine      = 27      'the ON led, 1 sec cycle

VAR                      'these are the variables we use.

long  Stack [40]       'for lcd

long  Stack2[40]       'for counts

long  Stack3[40]       'for spkr

long  Stack4[40]       'for click

long  Pot              'for potentiometer reading

long  bpm              'beats per minute

OBJ                          'These are the methods we need

LCD  : "LCDRoutines4"      'for controlling the LCD

UTIL : "Utilities"         'for general methods, read potentiomter

PUB GO                            'This the main method in this program

cognew (lcd_COG,  @Stack)       'create COG for LCD

cognew (Counts_COG, @Stack2)    'create COG for speaker

cognew (Calc_COG, @Stack3)      'create COG for calculations

dira[ledLine]~~                 'Power indicator

repeat                          'The main cog blinks an LED only

outa[ledLine]~                'These lines just blink an LED

waitcnt(clkfreq/2+cnt)        'as an ON indicator as a one

outa[ledLine]~~               'second reference

waitcnt(clkfreq/2+cnt)        'line 27

PRI lcd_COG                       'This is the display to the LCD

LCD.INITIALIZE_LCD              'set up the LCD

REPEAT                          'Routine to write to the LCD

LCD.POSITION (1,1)            'Position cursor

LCD.PRINT(STRING("POT VAL="))    'identify signal

LCD.PRINT_DEC(pot)            'print the Pot reading

LCD.SPACE(4)                  'write over old data

LCD.POSITION (2,1)            'Position cursor

LCD.PRINT(STRING("BEATS/M="))    'Identify signal

LCD.PRINT_DEC(bpm)            'print the beats/min

LCD.SPACE(4)                  'write over old data

'

PRI Counts_COG                    'This COG Toggles the speaker

dira[LED2Line]~~                '26

bpm:=60                         'this initializes the value

repeat                          'repeat loop

outa[LED2Line]~~              'toggle second LED

waitcnt(clkfreq/(bpm/30)+cnt) 'wait time

Click_Speaker                 'calls method for this

outa[LED2Line]~               'turn it off

waitcnt(clkfreq/(bpm/30)+cnt) 'wait time

PRI Calc_COG                      'This COG calculates the beats

pot:=10                         'this initializes the value

bpm:=60                         'this initializes the value

repeat                          'repeat loop

pot:=util.Read3202_0          'read the potentiometer

bpm:=40+(10*pot)*(208-40)/40950    'calculate beats from pot reading

PRI Click_speaker                  'makes the click sound

dira[Clickline]~~                'line 25

outa[Clickline]~~                'turn on

outa[Clickline]~                 'turn off

{{Chapter 21 Program 01

}}

PRI INITIALIZE_LCD                  'The addresses and data used here are

waitcnt(150_000+cnt)              'specified in the Hitachi data sheet for the

'display. YOU MUST CHECK THE DATA SHEET.

OUTA[RegSelect] := 0              'three lines are specified so we can write

OUTA[ReadWrite] := 0              'the initial set up bits for the LCD

OUTA[Enable]    := 0              'See Hitachi HD44780 data sheet

'

SEND_INSTRUCTION (%0011_1000)     'Sets DL=8 bits, N=2 lines, F=5x7 font

waitcnt(50_000+cnt)’              'wait for instruction to execute

SEND_INSTRUCTION (%0000_1111)     'Display on, Cursor on, Blink on

waitcnt(12_000+cnt)               'wait for instruction to execute

SEND_INSTRUCTION (%0000_0110)     'Move Cursor, Do not shift display

waitcnt(12_000+cnt)               'wait for instruction to execute

{{Chapter 21 Program 02

}}

PUB CLEAR                            'Clear the LCD display and go home

SEND_INSTRUCTION (%0000_0001)      'to the 1,1 position

{{Chapter 21 Program 03

}}

PUB POSITION (LINE_NUMBER, HOR_POSITION) | CHAR_LOCATION

'Position the cursor at location

'HOR_POSITION : Horizontal Position : 1 to 16

'LINE_NUMBER : Line Number : 1 or 2

CHAR_LOCATION := (HOR_POSITION-1) * 64   'figure location

CHAR_LOCATION += (LINE_NUMBER-1) + 128   'figure location

SEND_INSTRUCTION (CHAR_LOCATION)         'send the instruction to position

cursor

{{Chapter 21 Program 04

}}

PRI CHECK_BUSY | BUSY_BIT                     'routine to check busy bit

OUTA[ReadWrite] := 1                        'Set to read the busy bit

OUTA[RegSelect] := 0                        'Set to read the busy bit

DIRA[DataBit7..DataBit0] := %0000_0000      'Set the entire port to be an input

REPEAT                                      'Keep doing it till clear

OUTA[Enable]  := 1              'set to 1 to get ready to toggle H>L this bit

BUSY_BIT := INA[DataBit7]       'the busy bit is bit 7 of the byte read

OUTA[Enable]  := 0              'make the enable bit go low for H>L toggle

WHILE (BUSY_BIT == 1)                    'do it as long as the busy bit is 1

DIRA[DataBit7..DataBit0] := %1111_1111   'done, set the data port back to

output

{{Chapter 21 Program 05

}}

PRI SEND_CHAR (DISPLAY_DATA)                  'set up for writing to the display

CHECK_BUSY                          'wait for busy bit to clear before sending

OUTA[ReadWrite] := 0                        'Set up to read busy bit

OUTA[RegSelect] := 1                        'Set up to read busy bit

OUTA[Enable]    := 1                        'Set up to toggle bit H>L

OUTA[DataBit7..DataBit0] := DISPLAY_DATA    'Ready to SEND data in

OUTA[Enable]    := 0                        'Toggle the bit H>L

{{Chapter 21 Program 06

}}

PRI SEND_INSTRUCTION (DISPLAY_DATA)     'set up for writing instructions

CHECK_BUSY                            'wait for busy bit to clear before sending

OUTA[ReadWrite] := 0                  'Set up to read busy bit

OUTA[RegSelect] := 0                  'Set up to read busy bit

OUTA[Enable]    := 1                        'Set up to toggle bit H>L

OUTA[DataBit7..DataBit0] := DISPLAY_DATA    'Ready to READ data in

OUTA[Enable]    := 0                        'Toggle the bit H>L

{{11 Sep 09     Harprit Sandhu

LCDminimal.spin

Propeller Tool Ver 1.2.6

PROGRAM TO BEGIN USING THE LCD

A minimal LCD implementation to allow us to use the LCD in our

experiments immediately.

This program is an absolutely minimal implementation to

make the LCD usable. You can work on improving it.

┌────────────┐

Schematic                                               │ ┌────────┐ │

│ │ ┌────┐ │ │

│ │ │    │ │ │

POWER ETC:

┌─────────-───-───────────────┴─┴─┴─┴─┴─┴┐   │ │ │

BASIC CONNECTIONS   │ 1 0 9 8 7 6 5 4│3 X X G│3 2 1 0 9 8 7 6│   │ │ │

FOR THE EDUCATION   │                │       │               │   │ │ │

KIT ARE STANDARD    │    PROPELLER   │       │     CHIP      │   │ │ │

CONNECTIONS AND ARE │ 0 1 2 3 4 5 6 7│G B R 3│8 9 0 1 2 3 4 5│   │ │ │

NOT SHOWN HERE

└─────────────────────────┬─┬─┬─┬─┬─┬─┬─┬┘   │ │ │

│ │ │ │ │ │ │ │    │ │ │

┌─────┼─┼─┼─┼─┼─┼─┼─┼────┼─┼─┘

│ ┌───┼─┼─┼─┼─┼─┼─┼─┼────┼─┘

5VDC  │ │ ┌─┼─┼─┼─┼─┼─┼─┼─┼────┘

   │ │ │ │ │ │ │ │ │ │ │

│   │ │ │ │ │ │ │ │ │ │ │

│   │ │ │ │ │ │ │ │ │ │ │

┌──────────┳─┼─┐ │ │ │ │ │ │ │ │ │ │ │

│          │ │ │ │ │ │ │ │ │ │ │ │ │ │

│

┌────┴─┴─┴─┴─┴─┴─┴─┴─┴─┴─┴─┴─┴─┴─────---------────┐

│     │    G 5 G S W E 0 1 2 3 4 5 6 7                  │

│     │

┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐  │

│     │

└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘  │

│     │

┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐┌─┐  │

│     │

└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘└─┘  │

│

└───────────────────────────────────────---------─┘

│      16 CHAR BY 2 LINE LCD DISPLAY

 GND  8 BIT MODE

Revisons

}}

CON

{{

Pin assignment are assigned as constants because the pins are fixed.

These numbers reflect the actual wiring on the board between the Propeller

and the 16x2 LCD display. If you want the LCD on other lines, that would

have to be specified here.  We are going to use 8 bit mode to transfer data

All these numbers refer to lines on the Propeller

}}

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ = 5_000_000           'the oscillator frequency

RegSelect     = 16

ReadWrite     = 17

Enable        = 18

DataBit0      = 8

DataBit7      = 15

waitPeriod    =500_000                      'set the wait period in Milliseconds

high          =1                        'define the High state

low           =0                        'define the Low state

{{

Defining high and low states will allow us to invert these when we use

buffers to amplify the output from the prop chip.  We will then make

low=1 and high=0 thus inverting all the values throughout the program

}}

PUB Go

DIRA[DataBit7..DataBit0]:=%11111111  'the lines for the LCD are outputs

DIRA[RegSelect] := High         'the lines for the LCD are outputs

DIRA[ReadWrite] := High         'the lines for the LCD are outputs

DIRA[Enable]    := High         'the lines for the LCD are outputs

INITIALIZE_LCD                  'initialize the LCD

waitcnt(5_000_000+cnt)          'wait for LCD to start up

CLEAR                           'clear the LCD

repeat                            'repeat forever

clear

repeat 4                        'print 4 'A's

SEND_CHAR ("A")

repeat 4                        'print 4 'a's

SEND_CHAR ("b")

POSITION (1,2)                  'move to POSITION: line 2, space 1

repeat 4                        'print 4 'B's

SEND_CHAR ("C")

repeat 4                        'print 4 'b's

SEND_CHAR ("d")

waitcnt(10_000_000+cnt)

PRI INITIALIZE_LCD                'The addresses and data used here are

waitcnt(500_000+cnt)          'specified in the Hitachi data sheet for

'display. YOU MUST CHECK THIS FOR YOURSELF

OUTA[RegSelect] := Low          'these three lines are specified to write

OUTA[ReadWrite] := Low          'the initial set up bits for the LCD

OUTA[Enable]    := Low          'See Hitachi HD44780 data sheet

'YOU MUST CHECK THIS FOR YOURSELF.

SEND_INSTRUCTION (%0011_0000)   'Send 1sr

waitcnt(49_200+cnt)             'wait

SEND_INSTRUCTION (%0011_0000)   'Send 2nd

waitcnt(1_200+cnt)              'wait

SEND_INSTRUCTION (%0011_0000)   'Send 3rd

waitcnt(12_000+cnt)             'wait

SEND_INSTRUCTION (%0011_1000)   'Sets DL=8 bits, N=2 lines, F=5x7 font

SEND_INSTRUCTION (%0000_1111)   'Display on, Cursor on, Blink on

SEND_INSTRUCTION (%0000_0001)   'clear LCD

SEND_INSTRUCTION (%0000_0110)   'Move Cursor, Do not shift display

PUB CLEAR                          'Clear the LCD display and go home

SEND_INSTRUCTION (%0000_0001)

PUB POSITION (LINE_NUMBER, HOR_POSITION) | CHAR_LOCATION

'Position cursor

'HOR_POSITION : Horizontal Position : 1 to 16

'LINE_NUMBER : Line Number : 1 or 2

CHAR_LOCATION := (HOR_POSITION-1) * 64  'figure location

CHAR_LOCATION += (LINE_NUMBER-1) + 128  'figure location

SEND_INSTRUCTION (CHAR_LOCATION)   'send the instr to position cursor

PUB SEND_CHAR (DISPLAY_DATA)   'set up for writing to the display

CHECK_BUSY                   'wait for busy bit to clear before sending

OUTA[ReadWrite] := Low       'Set up to read busy bit

OUTA[RegSelect] := High      'Set up to read busy bit

OUTA[Enable]    := High      'Set up to toggle bit H>L

OUTA[DataBit7..DataBit0] := DISPLAY_DATA    'Ready to SEND data in

OUTA[Enable]    := Low       'Toggle the bit H>L

PUB CHECK_BUSY | BUSY_BIT      'routine to check busy bit

OUTA[ReadWrite] := High      'Set to read the busy bit

OUTA[RegSelect] := Low        'Set to read the busy bit

DIRA[DataBit7..DataBit0] := %0000_0000  'Set the entire port to be an input

REPEAT                        'Keep doing it till clear

OUTA[Enable]  := High       'set to 1 to get ready to toggle H>L this bit

BUSY_BIT := INA[DataBit7]   'the busy bit is bit 7 of the byte read

OUTA[Enable]  := Low        'make the enable bit go low for H>L toggle

WHILE (BUSY_BIT == 1)         'do it as long as the busy bit is 1

DIRA[DataBit7..DataBit0] := %1111_1111  'set the data port back to outputs

PUB SEND_INSTRUCTION (DISPLAY_DATA) 'set up for writing instructions

CHECK_BUSY                   'wait for busy bit to clear before sending

OUTA[ReadWrite] := Low       'Set up to read busy bit

OUTA[RegSelect] := Low       'Set up to read busy bit

OUTA[Enable]    := High      'Set up to toggle bit H>L

OUTA[DataBit7..DataBit0] := DISPLAY_DATA    'Ready to READ data in

OUTA[Enable]    := Low        'Toggle the bit H>L

{{11 Sep 09     Harprit Sandhu

LCDminimal2.spin

Propeller Tool Ver 1.2.6

Chapter 21 Program 8

LCD control.  Comprehensive.

Here are the improvement to program

Can now send DECIMAL values to the LCD

Can now send HEX     values to the LCD

Can now send BINARY  values to the LCD

Delays in the print routines have been eliminate to speed things up

The output blinks "Hello world" and 1234567890”on the two lines

}}

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ = 5_000_000           'the oscillator frequency

DataBit0   =  8        'Data uses 8 bits from

DataBit7   = 15        'lines 8 to 15

RegSelect  = 16        'The three control lines, register select

ReadWrite  = 17        'Read Write and

Enable     = 18        'Enable  line

waitPeriod =5_000_000  'set the wait period, about 1/2 sec

high       =1          'define the High state

low        =0          'define the Low state

VAR

long index             'used to count the chars in the string

long char_index        'used to count the chars in the string

PUB START

DIRA[16..18]~~                          'set these 8 lines to outputs

INITIALIZE_LCD                           'this METHOD initializes on the LCD

DIRA[DataBit7..DataBit0] := %1111_1111   '11 lines control the LCD as outputs

DIRA[RegSelect] := 1                         'select the register for the LCD

DIRA[ReadWrite] := 1                         'set to write

DIRA[Enable]    := 1                         'enable operation

repeat                                       'this loops forever

initialize_lcd                             'init the LCD

waitCnt(waitPeriod + cnt)                  'wait to see it clear

position (1,1)                             ' go to pos 1,1

PRINT(string("Hello world"))               'display text message

POSITION (2, 1)                            'pos to line 2 position 1

PRINT_DEC (1234567890)                     'print the number

waitCnt(waitPeriod + cnt)                  'wait a while before looping

PRI INITIALIZE_LCD                    'The addresses and data used here are

waitcnt(500_000+cnt)                'specified in the Hitachi data sheet for the

'display. YOU MUST CHECK THIS FOR YOURSELF.

OUTA[RegSelect] := 0                'three lines are specified so we can write

OUTA[ReadWrite] := 0                'the initial set up bits for the LCD

OUTA[Enable]    := 0                'See Hitachi HD44780 data sheet

SEND_INSTRUCTION (%0011_1000)       'Sets DL=8 bits, N=2 lines, F=5x7 font

SEND_INSTRUCTION (%0000_0001)           'clears the LCD

SEND_INSTRUCTION (%0000_1100)           'Display on, Cursor off, Blink off

SEND_INSTRUCTION (%0000_0110)           'Move Cursor, Do not shift display

{this blank line ends this method}

PRI CLEAR                           'Clear the LCD display and go home

SEND_INSTRUCTION (%0000_0001)     'This is the clear screen and go home

command

{this blank line ends this method}

PRI PRINT (the_line)               'routine handles more Chars at a time

'called as PRINT(string("the_line")) “

'the line" contains the pointer to the line.

'because we have to point to the line

'zero terminated but we will not use that.

'We will use the string size instead.

'This was is easier to understand

index:=0                         'Reset the counter to count chars sent

repeat                           'repeat for all chars in the list

char_index:= byte[the_line][index++]   'char_index contains the char/byte

'pointed to by the index

SEND_CHAR (char_index)                 'send the 'pointed to' char to the LCD

while index<strsize(the_line)            'keep doing it till last char is sent

PRI POSITION (LINE_NUMBER, HOR_POSITION) | CHAR_LOCATION    'Position

the cursor

'at location

CHAR_LOCATION := (LINE_NUMBER-1) * 64   'fig loc. See Hitachi HD44780

data sht

CHAR_LOCATION += (HOR_POSITION-1) + 128 'fig loc. See Hitachi HD44780

data sht

SEND_INSTRUCTION (CHAR_LOCATION)        'send the instruction to position

cursor

PRI SEND_CHAR (DISPLAY_CHAR)            'set up for writing to the display

CHECK_BUSY                            'wait for busy bit to clear before sending

OUTA[ReadWrite] := 0                        'Set up to read busy bit

OUTA[RegSelect] := 1                        'Set up to read busy bit

OUTA[Enable]    := 1                        'Set up to toggle bit H>L

OUTA[DataBit7..DataBit0] := DISPLAY_CHAR    'Ready to SEND data in

OUTA[Enable]    := 0                        'Toggle the bit H>L

PRI CHECK_BUSY | BUSY_BIT                     'routine to check busy bit

OUTA[ReadWrite] := 1                        'Set to read the busy bit

OUTA[RegSelect] := 0                        'Set to read the busy bit

DIRA[DataBit7..DataBit0] := %0000_0000      'Set the entire port to be an input

REPEAT                                      'Keep doing it till clear

OUTA[Enable]  := 1              'set to 1 to get ready to toggle H>L this bit

BUSY_BIT := INA[DataBit7]       'the busy bit is bit 7 of the byte read

'INA is the 32 input pins on the PROP and we

'are reading data bit 7 which is on pin 15!

OUTA[Enable]  := 0              'make the enable bit go low for H>L toggle

WHILE (BUSY_BIT == 1)                   'do it as long as the busy bit is 1

DIRA[DataBit7..DataBit0] := %1111_1111  'done set the data port back to

outputs

PRI SEND_INSTRUCTION (DISPLAY_DATA)    'set up for writing instructions

CHECK_BUSY                           'wait for busy bit to clear before sending

OUTA[ReadWrite] := 0                        'Set up to read busy bit

OUTA[RegSelect] := 0                        'Set up to read busy bit

OUTA[Enable]    := 1                        'Set up to toggle bit H>L

OUTA[DataBit7..DataBit0] := DISPLAY_DATA    'Ready to READ data in

OUTA[Enable]    := 0                        'Toggle the bit H>L

PRI PRINT_DEC (VALUE) | TEST_VALUE      'for printing values in decimal format

IF (VALUE < 0)                        'if it is a negative value

-VALUE                              'change it to a positive

SEND_CHAR("-")                      'and print a - sign on the LCD

TEST_VALUE := 1_000_000_000           'we get individual digits by comp to this

'value

REPEAT 10                             'There are 10 digits maximum

IF (VALUE => TEST_VALUE)            'see if our num is bigger than testValue

SEND_CHAR(VALUE / TEST_VALUE + "0")  'if it is divide to get the digit

VALUE //= TEST_VALUE                 'figure the nxt val for the nxt digit

RESULT~~                             'result so we can pass it on

ELSEIF (RESULT OR TEST_VALUE == 1)     'if the result 1 then division was

even

SEND_CHAR("0")                       'so we sent out a zero

TEST_VALUE /= 10                       'we div by 10 to test the next digit

PRI PRINT_HEX (VALUE, DIGITS)              'for printing values in HEX format

VALUE <<= (8 - DIGITS) << 2              'you can specify up to 8 digits or

'FFFFFFFF max

REPEAT DIGITS                            'do each digit

SEND_CHAR(LOOKUPZ((VALUE <-= 4) & $F : "0".."9", "A".."F"))

'use look up table to select character

PRI PRINT_BIN (VALUE, DIGITS)                 'for printing values in BINARY format

VALUE <<= 32 - DIGITS                       '32 digits is the max for our system

REPEAT DIGITS                               'Repeat for digits desired

SEND_CHAR((VALUE <-= 1) & 1 + "0")        'send a 1 or a 0

{this blank line ends this method}

{{ 21 - 09}}

OBJ

LCD : "LCDRoutines"         'We will be using these METHODS in this program

UTIL : "Utilities"          'We will be using these METHODS in this program

{{21 Sep 09     Harprit Sandhu

LCDRoutines.spin

Propeller Tool Ver 1.2.6

Chapter 21 Program 10

LCD ROUTINES

The following are the names of the methods described in this program

INITIALIZE_LCD

INITIALIZE_LCD4 not yet working right.

PRINT (the_line)

POSITION (LINE_NUMBER, HOR_POSITION) | CHAR_LOCATION

SEND_CHAR (DISPLAY_CHAR)

SEND_CHAR (DISPLAY_CHAR)

PRINT_DEC (VALUE) | TEST_VALUE

PRINT_HEX (VALUE, DIGITS)

PRINT_BIN (VALUE, DIGITS)

CLEAR

HOME

SPACE (QTY)

Revisions

04 Oct 09  Initialize made more robust, misc unnecessary calls removed.

}}

CON                             'all the constants used by all the METHODS

'in this program have to be listed here

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000          '10 Mhz

DataBit0   =  8               'Data uses 8 bits from here on

DataBit1   =  9

DataBit2   = 10

DataBit3   = 11               'All these bits dont need to be named but

DataBit4   = 12               'are named so that they can be called by

DataBit5   = 13               'name if the need ever arises

DataBit6   = 14

DataBit7   = 15

RegSelect  = 16               'The three control lines

ReadWrite  = 17               '

Enable     = 18               '

high       =1                 {define the High state}

low        =0                 {define the Low state}

VAR                             'these are the variables we will use.

byte  temp                   'for use as a pointer

byte  index                  'to count characters

PUB Go

INITIALIZE_LCD

repeat

print(String("1234567890  L1"))

position(2,1)

print(String("On second line"))

waitcnt(3_000_000+cnt)

clear

waitcnt(3_000_000+cnt)

'===========================================================

=====================

{{initialize the LCD to use 8 lines of data

Includes a half second delay, clears the display and positons to 1,1

no variables used

}}

PUB INITIALIZE_LCD                     'The addressses and data used here are

waitcnt(5_000_000+cnt)               'specified in the Hitachi data sheet

DIRA[DataBit0..Enable]~~             'YOU MUST CHECK THIS FOR YOURSELF.

SEND_INSTRUCTION (%0011_0000)        'Send 1

waitcnt(49_200+cnt)                  'wait

SEND_INSTRUCTION (%0011_0000)        'Send 2

waitcnt(1_200+cnt)                   'wait

SEND_INSTRUCTION (%0011_0000)        'Send 3

waitcnt(12_000+cnt)                  'wait

SEND_INSTRUCTION (%0011_1000)        'Sets DL=8 bits, N=2 lines, F=5x7 font

SEND_INSTRUCTION (%0000_1110)        'Display on, Blink on, Sq Cursor off

SEND_INSTRUCTION (%0000_0110)        'Move Cursor, Do not shift display

SEND_INSTRUCTION (%0000_0001)        'clears the LCD

POSITION (1,1)

'===========================================================

=====================

{{Sends instructions as opposed to a character to the LCD

no variables are used

}}

PUB SEND_INSTRUCTION (D_DATA)    'set up for writing instructions

CHECK_BUSY                           'wait for busy bit to clear b

OUTA[ReadWrite] := 0                 'Set up to read busy bit

OUTA[RegSelect] := 0                 'Set up to read busy bit

OUTA[Enable]    := 1                 'Set up to toggle bit H>L

OUTA[DataBit7..DataBit0] := D_DATA   'Ready to READ data in

OUTA[Enable]    := 0                 'Toggle the bit H>L to xfer the data

'===========================================================

=====================

{{Sends a character to the LCD

}}

PUB SEND_CHAR (D_CHAR)           'set up for writing to the display

CHECK_BUSY                           'wait for busy bit to clear

OUTA[ReadWrite] := 0                 'Set up to read busy bit

OUTA[RegSelect] := 1                 'Set up to read busy bit

OUTA[Enable]    := 1                 'Set up to toggle bit H>L

OUTA[DataBit7..DataBit0] := D_CHAR    'Ready to SEND data in

OUTA[Enable]    := 0                 'Toggle the bit H>L

'===========================================================

=====================

{{Print a line of characters to the LCD

uses variables index and temp

}}

PUB PRINT (the_line)              'This routine handles more than one Char

'called as PRINT(string("the_line"))

'"the_line" contains the pointer to line.

'because we have to point to the line

'zero terminated but will not use that.

'use the string size instead. Easier

index:=0                        'Reset the counter we are using

repeat                          'repeat for all chars in the list

temp:= byte[the_line][index++]'temp contains the char pointed by index

SEND_CHAR (temp)              'send the 'pointed to' char to the LCD

while index<strsize(the_line)   'keep doing it till the last char is sent

'===========================================================

=====================

{{Position cursor

}}

PUB POSITION (LINE_NUMBER, HOR_POSITION) | CHAR_LOCATION  'Position

the cursor

'Horizontal Position : 1 to 16       'specified by the two numbers

'Line Number : 1 or 2

CHAR_LOCATION := (LINE_NUMBER-1) * 64   'figr loc. See Hitachi HD44780

data

CHAR_LOCATION += (HOR_POSITION-1) + 128 'figr loc. See Hitachi HD44780

data

SEND_INSTRUCTION (CHAR_LOCATION)     'send the instruction to position

cursor

'===========================================================

=====================

{{Check for busy

}}

PUB CHECK_BUSY | BUSY_BIT        'routine to check busy bit

OUTA[ReadWrite] := 1           'Set to read the busy bit

OUTA[RegSelect] := 0           'Set to read the busy bit

DIRA[DataBit7..DataBit0] := %0000_0000  'Set the entire port to be an input

REPEAT                         'Keep doing it till clear

OUTA[Enable]  := 1           'set to 1 to get ready to toggle H>L this bit

BUSY_BIT := INA[DataBit7]    'the busybit is bit 7 of the byte read

'INA is the 32 input pins on the PROP and we

'are reading data bit 7 which is on pin 15!

OUTA[Enable]  := 0           'make the enable bit go low for H>L toggle

WHILE (BUSY_BIT == 1)          'do it as long as the busy bit is 1

DIRA[DataBit7..DataBit0] := %1111_1111  'set the data port back to outputs

'===========================================================

=====================

{{Print decimal

}}

PUB PRINT_DEC (VALUE) | TEST_VALUE'for printing values in decimal format

IF (VALUE < 0)                  'if it is a negative value

-VALUE                        'change it to a positive

SEND_CHAR("-")                'and print a - sign on the LCD

'

TEST_VALUE := 1_000_000_000     'we get individual digits by comp to this

'value and then div by 10 to get the nxt val

REPEAT 10                       'There are 10 digits maximum in our system

IF (VALUE => TEST_VALUE)      'see if our number is bigger than testValue

SEND_CHAR(VALUE / TEST_VALUE + "0")     'if it is, divide to get the digit

VALUE //= TEST_VALUE             'figure the next value for the next digit

RESULT~~                         'result we can pass it on below

ELSEIF (RESULT OR TEST_VALUE == 1) 'if the result was a 1 then div was

even

SEND_CHAR("0")                 'so we sent out a zero

TEST_VALUE /= 10                 'we divide by 10 to test for the next digit

'===========================================================

=====================

{{Print Hex

}}

PUB PRINT_HEX (VALUE, DIGITS)      'for printing values in HEX format

VALUE <<= (8 - DIGITS) << 2      'you can specify up to 8 digits or FFFFFFFF

max

REPEAT DIGITS                    'do each digit

SEND_CHAR(LOOKUPZ((VALUE <-= 4) & $F : "0".."9", "A".."F"))

'use lookup table to select character

'===========================================================

=====================

{{Print Binary

}}                                              '

PUB PRINT_BIN (VALUE, DIGITS)      'for printing values in BINARY format

VALUE <<= 32 - DIGITS            '32 binary digits is the max for our system

REPEAT DIGITS                    'Repeat for each digit desired

SEND_CHAR((VALUE <-= 1) & 1 + "0") 'send a 1 or a 0

'===========================================================

=====================

{{Clear screen

}}

PUB CLEAR                       'Clear the LCD display and go home

SEND_INSTRUCTION (%0000_0001) 'This is the clear screen and go home

command

'===========================================================

=====================

{{Go to position 1,1

}}

PUB HOME                          'go to position 1,1.

SEND_INSTRUCTION (%0000_0011)   'Not cleared

'===========================================================

=====================

{{Print spaces

}}

PUB SPACE (qty)                'Prints spaces, for between numbers

repeat (qty)

PRINT(STRING(" "))

'===========================================================

=====================

{{

}}

{{11 Oct 09     Harprit Sandhu

LCDTester.Spin

Propeller Tool Ver. 1.2.6

Chapter 21 Program 11

Test program for LCD Routines

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000

high       =1          'define the High state

low        =0          'define the Low state

VAR

byte index             'used as counter for various uses

OBJ

LCD : "LCDRoutines"    'Using their METHODS in this program

UTIL : "Utilities"     'Using their METHODS in this program

PUB Go

LCD.initialize_lcd

LCD.print (string("Initialized OK"))

LCD.position(2,1)

LCD.print (string("Print test"))

UTIL.pause (1500)

LCD.clear

LCD.position (1,1)

LCD.print (string("this is 1st line"))

UTIL.pause (300)

LCD.position(2,1)

LCD.print (string("ok is on line 2"))

UTIL.pause (1500)

LCD.clear

LCD.print (string("Position test"))

UTIL.pause (1500)

index:=0

repeat 16

index := index +1

LCD.clear

LCD.position (1,index)

LCD.print (string("X"))

UTIL.pause (300)

index:=0

repeat 16

index := index +1

LCD.clear

LCD.position (2,index)

LCD.print (string("X"))

UTIL.pause (300)

LCD.clear

LCD.print (string("End"))

repeat

{{21 Sep 09    Harprit Sandhu

Utilities0.spin

Propeller Tool Ver 1.2.6

Chapter 21 Program 12

Program UTILITIES

Flash         flashes a pin once, toggles it slowly

Pause         pause in milliseconds

}}

CON

high          =1

low           =0

waitperiod    =100

PUB FLASH (color)                    'routine to flash an LED by color

outa[color] :=high               'line that actually sets the LED high

waitCnt(waitPeriod +cnt)         'wait till counter reaches this value

outa[color] :=low                'line that actually sets the LED low

waitCnt(waitPeriod +cnt)         'wait till counter reaches this value

'

PUB PAUSE(millisecs)                 'As set up here it is .25 millisceconds

waitcnt((clkfreq/1000)*millisecs +cnt)      'based on Osc freq

{{21 Sep 09     Harprit Sandhu

LCDRoutines4.spin

Propeller Tool Version 1.2.6

Chapter 21 Program 13 and Appendix

LCD ROUTINES for a 4 bit data path.

The following are the names of the methods described in this program

INITIALIZE_LCD

PRINT (the_line)

POSITION (LINE_NUMBER, HOR_POSITION) | CHAR_LOCATION

SEND_CHAR (DISPLAY_CHAR)

SEND_CHAR (DISPLAY_CHAR)

PRINT_DEC (VALUE) | TEST_VALUE

PRINT_HEX (VALUE, DIGITS)

PRINT_BIN (VALUE, DIGITS)

CLEAR

HOME

SPACE (QTY)

Revisions

04 Oct 09  Initialize made more robust, misc unnecessary calls removed.

}}

CON                             'all the constants used by all the METHODS

'in this program have to be listed here

_CLKMODE=XTAL1 + PLL2X        'The system clock spec. 2 X multiplier

_XINFREQ   = 5_000_000        'ext crystal is 5 Mhz, so 10 Mhz operation

DataBit4   = 12               'are named so that they can be called by

DataBit5   = 13               'name if the need ever arises

DataBit6   = 14               '

DataBit7   = 15               '

RegSelect  = 16               'The three control lines

ReadWrite  = 17               'The three control lines

Enable     = 18               'The three control lines

high       =1                 'define the High state

low        =0                 'define the Low state

Inv_high   =0                 'define the Inverted High state

Inv_low    =1                 'define the Inverted Low state

VAR                             'these are the variables we will use

byte  temp                   'for use as a pointer

byte  index                  'to count characters

PUB Go

INITIALIZE_LCD

repeat

print(String("4bit mode line 1"))

position(2,1)

print(String("4bit mode line 2"))

waitcnt(clkfreq/4+cnt)

clear

waitcnt(clkfreq/4+cnt)

{{initialize the LCD to use 4 lines of data

Includes the half second delay, clears the display and positons to 1,1

no variables used

}}

PUB INITIALIZE_LCD                'The addresses and data used here are

waitcnt(150_000+cnt)            'specified in the Hitachi data sheet for the

DIRA[DataBit4..Enable]~~        'display. YOU MUST CHECK THIS FOR

YOURSELF.

SEND_INSTRUCTION (%0011)        'Send 1st

waitcnt(49_200+cnt)             'wait

SEND_INSTRUCTION (%0011)        'Send 2nd

waitcnt(1_200+cnt)              'wait

SEND_INSTRUCTION (%0011)        'Send 3rd

waitcnt(12_000+cnt)             'wait

SEND_INSTRUCTION (%0010)        'set for 4 bit mode

waitcnt(12_000+cnt)             'wait

SEND_INSTRUCTION2 (%0010_1000)  'Sets DL=4 bits, N=2 lines, F=5x7 font

' waitcnt(12_000+cnt)            'wait

SEND_INSTRUCTION2 (%0000_1110)  'Display on, Blink on, Sq Cursor off

' waitcnt(12_000+cnt)            'wait

SEND_INSTRUCTION2 (%0000_0110)  'Move Cursor, Do not shift display

' waitcnt(12_000+cnt)            'wait

SEND_INSTRUCTION2 (%0000_0001)  'clears the LCD

'waitcnt(12_000+cnt)            'wait

POSITION (1,1)

{{Sends instructions as opposed to a character to the LCD

no variables are used

}}

PUB SEND_INSTRUCTION (D_DATA)        'set up for writing instructions

CHECK_BUSY                         'wait for busy bit to clear before sending

OUTA[ReadWrite] := 0               'Set up to read busy bit

OUTA[RegSelect] := 0               'Set up to read busy bit

OUTA[Enable]    := 1               'Set up to toggle bit H>L

OUTA[DataBit7..DataBit4] := D_DATA 'Ready to READ data in

OUTA[Enable]    := 0               'Toggle the bit H>L to xfer the data

{{Sends an instruction as opposed to a character to the LCD

no variables are used

}}

PUB SEND_INSTRUCTION2 (D_DATA)      'set up for writing instructions

CHECK_BUSY                        'wait for busy bit to clear before sending

OUTA[ReadWrite] := 0              'Set up to read busy bit

OUTA[RegSelect] := 0              'Set up to read busy bit

OUTA[Enable]    := 1              'Set up to toggle bit H>L

OUTA[DataBit7..DataBit4] := D_DATA>>4   'Ready to READ data in

OUTA[Enable]    := 0                 'Toggle the bit H>L to xfer the data

OUTA[Enable]    := 1                 'Set up to toggle bit H>L

OUTA[DataBit7..DataBit4] := D_DATA   'Ready to READ data in

OUTA[Enable]    := 0                 'Toggle the bit H>L to xfer the data

{{Sends a single character to the LCD in two halves

}}

PUB SEND_CHAR (D_CHAR)           'set up for writing to the display

CHECK_BUSY                     'wait for busy bit to clear before sending

OUTA[ReadWrite] := 0           'Set up to send data

OUTA[RegSelect] := 1           'Set up to send data

OUTA[Enable]    := 1           'go high

OUTA[DataBit7..DataBit4] := D_CHAR>>4  'Send high 4 bits

OUTA[Enable]    := 0                 'Toggle the bit H>L

OUTA[Enable]    := 1                 'go high again

OUTA[DataBit7..DataBit4] :=D_CHAR    'send low 4 bits

OUTA[Enable]    := 0                 'Toggle the bit H>L

{{Print a line of characters to the LCD

uses variables index and temp

}}

PUB PRINT (the_line)       'This routine handles more than one Char at a time

'called as PRINT(string("the_line"))

'"the_line" contains the pointer to line. Line is

'because we have to point to the line

'zero terminated but we will not use that.  We will

'use the string size instead. Easier to understand

index:=0                 'Reset the counter we are using to count chars sent

repeat                   'repeat for all chars in the list

temp:= byte[the_line][index++] 'temp contains the char/byte pointed by index

SEND_CHAR (temp)               'send the 'pointed to' char to the LCD

while index<strsize(the_line)    'keep doing it till the last char is sent

{{Position cursor

}}

PUB POSITION (LINE_NUMBER, HOR_POSITION) | CHAR_LOCATION  'Position

the cursor  'Line Number : 1 to 4

'Horizontal Position : 1 to 20          'specified by the two numbers

CHAR_LOCATION := (LINE_NUMBER-1) * 64   'figure location. See Hitachi

HD44780

CHAR_LOCATION += (HOR_POSITION-1) + 128 'figure location. See Hitachi

HD44780

' CHAR_LOCATION += (HOR_POSITION-1) + 128

' CHAR_LOCATION += (HOR_POSITION-1) + 128

SEND_INSTRUCTION2 (CHAR_LOCATION)       'send the instruction to position

cursor

{{Check for busy

}}

PUB CHECK_BUSY | BUSY_BIT              'routine to check busy bit

OUTA[ReadWrite] := 1                 'Set to read the busy bit

OUTA[RegSelect] := 0                 'Set to read the busy bit

DIRA[DataBit7..DataBit4] := %0000    'Set the entire port to be an input

REPEAT                          'Keep doing it till clear

OUTA[Enable]  := 1            'set to 1 to get ready to toggle H>L this bit

BUSY_BIT := INA[DataBit7]     'the busybit is bit 7 of the byte read

'INA is the 32 input pins on the PROP and we

'are reading data bit 7 which is on pin 15!

OUTA[Enable]  := 0            'make the enable bit go low for H>L toggle

WHILE (BUSY_BIT == 1)           'do it as long as the busy bit is 1

DIRA[DataBit7..DataBit4] := %1111 'done, so set the data port back to outputs

{{Print a decimal value, whole numbers only

}}

PUB PRINT_DEC (VALUE) | TEST_VALUE   'for printing values in decimal format

IF (VALUE < 0)                  'if it is a negative value

-VALUE                        'change it to a positive

SEND_CHAR("-")                'and print a - sign on the LCD

TEST_VALUE := 1_000_000_000     'we get individual digits by comparing to this

'value and then dividing by 10 to get next value

REPEAT 10                       'There are 10 digits maximum in our system

IF (VALUE => TEST_VALUE)      'see if our number is bigger than testValue

SEND_CHAR(VALUE / TEST_VALUE + "0")     'if it is, divide to get the digit

VALUE //= TEST_VALUE        'figure the next value for the next digit

RESULT~~                    'result of what just did pass it on below

ELSEIF (RESULT OR TEST_VALUE == 1) 'if the result was a 1 then div was

even

SEND_CHAR("0")               'so we sent out a zero

TEST_VALUE /= 10               'we divide by 10 to test for the next digit

{{Print a Hexadecimal value

}}

PUB PRINT_HEX (VALUE, DIGITS)     'for printing values in HEX format

VALUE <<= (8 - DIGITS) << 2     'you can specify up to 8 digits or FFFFFFFF

max

REPEAT DIGITS                   'do each digit

SEND_CHAR(LOOKUPZ((VALUE <-= 4) & $F : "0".."9", "A".."F"))

'use lookup table to select character

{{Print a Binary value

}}                                              '

PUB PRINT_BIN (VALUE, DIGITS)          'for printing values in BINARY format

VALUE <<= 32 - DIGITS                '32 binary digits is the max for our sys

REPEAT DIGITS                        'Repeat for each digit desired

SEND_CHAR((VALUE <-= 1) & 1 + "0") 'send a 1 or a 0

{{Clear screen

}}

PUB CLEAR                              'Clear the LCD display and go home

SEND_INSTRUCTION2 (%0000_0001)       'This is the clear screen and go home

command

{{Go to position 1,1   Does not clear the screen

}}

PUB HOME                               'go to position 1,1.

SEND_INSTRUCTION2 (%0000_0011)       'Not cleared

{{Print spaces

}}

PUB SPACE (qty)                        'Prints spaces, for between numbers

repeat (qty)

PRINT(STRING(" "))

{{Dec 31 09    Harprit Sandhu

Chapter 24 Program 01

outa[ServoLine]~

waitcnt((166,667-(PotValue * 15000 / 4095) + 7500 + cnt)

outa[ServoLine]~~

waitcnt((PotValue * 15000 / 4095))+ 7500 + cnt)

{{ 06 Sep 09     Harprit Sandhu

RC_ServoPosition.spin

Propeller Tool Version 1.2.6

Chapter 24 Program 02

READING A SERVO'S POSITION  uses pin 23

This program allows you to tie the signal sent to an

R/C servo to the position that it goes to.

Connections

White  P23 signal from Prop

Red 5 volts

Black ground

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000

outPin  =23                   'line the servo is on

VAR                             'these are the variables we will use.

long ServoPos                 'The program will read this variable from

'the main Hub RAM to determine the

'servo signal's high pulse duration

long stack [15]               'space for Cog for LCD

long stack2[50]               'space for Move Motor Cog

long pcount                   '

OBJ                              'These are the methods we will need for our calls

LCD  : "LCDRoutines4"          'for the LCD methods

UTIL : "Utilities"             'for general methods, pot

PUB Go                           'main cog

dira[outPin]~~                     'set direction for amplifier

cognew(MoveMotor(outPin),@Stack)   'start a new cog and run the MoveMotor

method

'on it and output pulses on Pin 23

'The new cog that is started above continuously

'reads the "position" variable as it's changed

'by the example Spin code below

cognew(cog_two, @stack2)       'start new cog for the LCD

repeat                         'this is the Cog's main loop

pcount:=UTIL.Read3202_0      'get the pot reading from the utilities

ServoPos:=7200+pcount*4      'calculate position count

Pub cog_two                         'set up and run the LCD

LCD.INITIALIZE_LCD                'initialize the LCD

repeat                            'LCD loop

LCD.POSITION (1,1)              'Go to 1st line 1st space

LCD.PRINT(STRING("Pot Pos="))   'Potentiometer position ID

LCD.PRINT_DEC(Pcount)           'print the pot reading

LCD.SPACE(2)                    'erase over old text

PUB MoveMotor(Pin)|LowTime,period   'method to toggle the output line, set

'up first

dira[Pin]~~                       'Set the direction of "Pin" to be an output

ctra[30..26]:=%00100              'Set this cog's "A Counter" in single

'ended NCO/PWM mode (where frqa always

'accumulates to phsa and the Apin output

'state is bit 31 of the phsa value)

ctra[5..0]:=Pin                   'Set the "A pin" of this cog's "A Counter"

'to be "Pin"

frqa:=1                           'Set this counter's frqa value to 1 (so 1

'will be added to phsa on each clock pulse)

ServoPos:=0                       'Start with position=0 (until the position

'value is changed by another cog)

LowTime:=clkfreq/60               'Set the time that the pulse will be low

'to 16ms = 1/60 secs

period:=cnt                       'Store current value of the system counter

repeat                            'line toggling routine.

phsa:=-ServoPos                 'Send a high pulse for "position" number of

'clock cycles. Note negative sign

period:=period+LowTime          'Calculate what system clock's value will

'be at the end of this cycle's period

waitcnt(period)                 'Wait for the system counter to reach the

'"period" value (end of cycle)

{{04 Sep 09     Harprit Sandhu

RunMotorOnly.spin

Propeller Tool Version 1.2.6

Chapter 25 Program 01

RUNNING A DC MOTOR. ON CONTROL ONLY TO

CONFIRM CONNECTIONS

This program runs the motor if turned on

Lines on Xavien amp as identified in the diagram are

line 1    Brake tie it to ground to turn it off

line 2    PWM signal     line 6 on Prop

line 3    Direction      line 7 on Prop

Connections are

Amplifier brake       P5

Amplifier PWM         P6

Amplifier direction   P7

}}

CON

_CLKMODE=XTAL1+ PLL2X              'The system clock spec

_XINFREQ = 5_000_000               'crystal

BRK = 2

PWM = BRK + 1

DIR = PWM + 1

PUB Go                               'main Cog

dira[BRK..DIR]~~                   'set direction for 3 lines

outa[BRK..DIR]:=%000               'make the lines low at start

repeat

outa[PWM]~~                      'turn on the PWM 100%

{{04 Sep 09  Harprit Sandhu

ReadDisplayPot.spin

Propeller Tool Version 1.2.6

Chapter 25 program 2

RUNNING A MOTOR, Read Pot/NO SPEED CONTROL

This program runs the motor backward or forward

at full speed based on the potentiometer position.

Reverses at 2048

Pot position is displayed on the LCD

Lines on Xavien amp as identified in the diagram are

line 1    Brake tie it to ground to turn it off

line 2    PWM signal     line 6 on Prop

line 3    Direction      line 7 on Prop

Connections are

Amplifier brake       P5

Amplifier PWM         P6

Amplifier direction   P7

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000                   '

BRK  =  5

PWM  =  BRK+1

DIR  =  BRK+2

VAR

long position

long stack2[50]               'space for Cog two

long pcount                   'potentiometer reading.

long  potpos

OBJ                             'These are the methods we will need

LCD  : "LCDRoutines4"          'for the LCD methods

UTIL : "Utilities"            'for general methods

PUB Go                          'main Cog

dira[BRK..DIR]~~              'set direction for lines

outa[BRK..DIR]:=%011          'make the lines high, brake off

Cognew(cog_two, @stack2)      'start new Cog for the LCD

repeat                        'this Cog's main loop

pcount:=UTIL.Read3202_0     'get he pot reading from the utilities

if pcount<2048              'check for center position

outa[DIR]~                'forward direction set

pcount:=(2048-pcount)*2   'set center and double the 127 to get near 255

else                        'or

outa[DIR]~~               'reverse direction

pcount:=(pcount-2048)*2   'set center and double the 127 to get near 255

potpos:=pcount

Pub Cog_two                     'set up and run the LCD

LCD.INITIALIZE_LCD            'initialize the LCD

repeat                        'LCD loop

LCD.POSITION (1,1)          'Go to 1st line 1st space

LCD.PRINT(STRING("Pot position")) 'Potentiometer position ID

LCD.POSITION (2,1)          'Go to 1st line 1st space

LCD.PRINT_DEC(Potpos)       'print the pot reading

LCD.SPACE(2)                'erase over old data

{{07 Sep 09   Harprit Sandhu

MotorFromPot.spin

RUNNING A DC MOTOR FROM A POTENTIOMETER

Chapter 25 Program 3

This program allows you to control the speed and the direction

of a motor from a potentiometer

Lines on Xavien amp as identified in the diagram are

line 1    Brake tie it to ground to turn it off

line 2    PWM signal     line 6 on Prop

line 3    Direction      line 7 on Prop

Connections are

Amplifier brake       P5

Amplifier PWM         P6

Amplifier direction   P7

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000          'crystal

'

BRK  =  5

PWM  =  BRK+1

DIR  =  BRK+2

PotMax = 1000          'The maximum power to the motor OUT OF 4095

PotMin =  40           'The minimum power to the motor OUT OF 4095

VAR                      'these are the variables we will use.

long PulsWidth         'The assembly program will read this variable from

'the main Hub RAM to determine the

'servo signal's high pulse duration

long stack [50]        'space for Cog managing the motor pulses

long stack2[50]        'space for Cog two

long pcount            'potentiometer reading.

byte arrow             'motor direction arrow

OBJ                       'These are the methods we need

LCD  : "LCDRoutines4"   'for the LCD methods

UTIL : "Utilities"      'for general methods

PUB Go                          'main cog

dira[BRK..DIR]~~              'set direction for amplifier

outa[BRK..DIR]:=%000

cognew(MoveMotor(6),@Stack)   'start a new cog and run the MoveMotor method

'on it and output pulses on Pin 7

'The new cog that is started above continuously

'reads the "position" variable as it's changed

'by the example Spin code below

cognew(cog_two, @stack2)      'start new cog for the LCD

repeat                        'this cog's main loop

pcount:=UTIL.Read3202_0     'get he pot reading from the utilities

if pcount<2047              'check for center position

outa[DIR]~                'forward direction set

arrow:=0                  'direction arrow

pcount:=(2047-pcount)*2   'set center and double the 127 to get near 255

else                        'or

outa[DIR]~~              'reverse direction

arrow:=1                 'direction arrow

pcount:=(pcount-2047)*2  'set center and double the 127 to get near 255

if pcount<PotMin            'check Min value

pcount:=Potmin           'set Min value

if pcount>PotMax            'check Max value

pcount:=Potmax           'check Max value

PulsWidth:=pcount*24        'multiply reading to get 4095

'(10000/4096=24)

PUB cog_two                        'set up and run the LCD

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Pos="))      'Potentiometer position ID

LCD.PRINT_DEC(pulsWidth/24)    'print the pot reading

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (1,11)             'Go to 1st line 1st space

LCD.PRINT(STRING("Dir="))      'Potentiometer position ID

LCD.PRINT_DEC(arrow)           'print the pot reading

LCD.SPACE(2)                   'erase over old data

PUB MoveMotor(Pin)|WaveLength,period  'subroutine to toggle the output line, set

'up first

dira[Pin]~~                      'Set the direction of "Pin" to be an output

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run in single

'ended NCO/PWM mode (where frqa always

'accumulates to phsa and the Apin output

'state is bit 31 of the phsa value)

ctra[5..0]:=Pin                  'Set the "A pin" of this cog's "A Counter"

'to be "Pin"

frqa:=1                          'Set this counter's frqa value to 1 (so 1

'will be added to phsa on each clock pulse)

PulsWidth:=1000                  'Start with position=0 (until the position

'value is changed by another cog)

WaveLength:=clkfreq/100          'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the system counter

repeat                           'line toggling routine.

phsa:=-PulsWidth               'Send a high pulse for "position" number of

'clock cycles. NOTE minus sign on PulseWidth.

period:=period+WaveLength      'Calculate what the system clock's value will

'be at the end of this cycle's period

waitcnt(period)                'Wait for the system counter to reach the

'"period" value (end of cycle)

{{09 Sep 09       Harprit Sandhu

StepperFromPot.spin

Propeller Tool Ver 1.2.6

Chapter 26 Program 4

RUNNING A STEPPER MOTOR FROM A POTENTIOMETER

UNI-DIRECTIONAL CONTROL

This program allows you to control the speed of a STEPPER motor

from a potentiometer

Xavien amplifier lines are

Coil #1

Brake is on     line P2 of the propeller

PWM is on       line P3 of the propeller

Direction is on line P4 of the propeller

Coil #2

Brake is on     line P5 of the propeller

Direction is on line P6 of the propeller

PWM is on       line P7 of the propeller

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000

Brk1=2

Pwm1=Brk1+1

Dir1=Brk1+2

Dir2=Brk1+3

Brk2=Brk1+4

Pwm2=Brk1+5

VAR                      'these are the variables we will use.

long stack1[35]        'space for Cog_LCD

long stack2[35]        'space for Cog MoveStepper

word Pcount            'potentiometer reading

OBJ                      'These are the methods we will need

LCD  : "LCDRoutines4"  'for the LCD methods

UTIL : "Utilities"     'for general methods

PUB Go                          'main cog

cognew(MoveStepper,@Stack1)

cognew(cog_LCD,    @stack2)   'start a new cog for the LCD

repeat                        'this main cog's main loop

pcount:=UTIL.read3202_0 + 1 'get the pot reading from the utilities

'the 1 eliminates a 0 reading

Pub cog_LCD                        'set up and run the LCD

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Div Fac=" )) 'Potentiometer position ID

LCD.PRINT_DEC(pcount)          'print the pot reading

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (2,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Mtr Rpm=" )) 'Potentiometer position ID

LCD.PRINT_DEC(6*pcount/10)     'print rpm

LCD.SPACE(2)                   'erase over old data

PUB MoveStepper

dira[Brk1..Pwm2]~~

pcount:=50

repeat        'BPD DBP            B=Brake, P=PWM, D=direction.

outa[Brk1..Pwm2]:=%011_010            'on  off

waitcnt(clkfreq/(pcount)+cnt)    '

outa[Brk1..Pwm2]:=%100_101            'off on

waitcnt(clkfreq/(pcount)+cnt)    '

outa[Brk1..Pwm2]:=%010_010            'rev off

waitcnt(clkfreq/(pcount)+cnt)    '

outa[Brk1..Pwm2]:=%100_001            'off rev

waitcnt(clkfreq/(pcount)+cnt)    '

{{09 Sep 09    Harprit Sandhu

StepperFwdRev.spin

Propeller Tool Ver 1.2.6

Chapter 26 Program 5

RUNNING A STEPPER MOTOR FROM A POTENTIOMETER

Fwd-Rev control From Pot 1

Speed control from Pot 2

Xavien amplifier lines are

Coil #1

Brake is on     line P2 of the propeller

PWM is on       line P3 of the propeller

Direction is on line P4 of the propeller

Coil #2

Brake is on     line P5 of the propeller

Direction is on line P6 of the propeller

PWM is on       line P7 of the propeller

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000

Brk1=2                         'line assignments

Pwm1=Brk1+1

Dir1=Brk1+2

Dir2=Brk1+3

Brk2=Brk1+4

Pwm2=Brk1+5

divmin = 4

divmax = 4500

VAR                      'these are the variables we will use.

long stack2[25]        'space for Cog_LCD

long stack3[25]        'space for Cog MoveStepper

byte Pcount            'potentiometer reading.

word divider           'divides clkfreq for delays

byte direction         'stepper direction

long range

OBJ                      'These are the methods we will need

LCD  : "LCDRoutines4"   'for the LCD methods

UTIL : "Utilities"      'for general methods

PUB Go                          'main Cog

Cognew(MoveStepper,@Stack3)

Cognew(cog_LCD,    @stack2)   'start a new Cog for the LCD

repeat                        'this main Cog's main loop

pcount:=UTIL.Read3202_0/16  'get the pot reading from the utilities

range:=UTIL.Read3202_1+10   'get the pot reading for range

if pcount<128

pcount:=127-pcount

direction:=0

else

pcount:=pcount-128

direction:=1

if range<divmin                'check min

range:=divmin                'set min

if range>divmax                'check max

range:=divmax                'set max

divider:=range                 'set divider value

Pub cog_LCD                        'set up and run the LCD

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Div Fac=" )) 'Potentiometer position ID

LCD.PRINT_DEC(pcount)          'print the pot reading

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (2,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Mtr Rpm=" )) 'Potentiometer position ID

LCD.PRINT_DEC(range)           'print range/pot

LCD.SPACE(2)                   'erase over old data

PUB MoveStepper

dira[Brk1..Pwm2]~~

outa[Brk1..Pwm2]~~

divider:=500

repeat

if direction==0

outa[Brk1..Pwm2]:=%011_010            'on  off

waitcnt(clkfreq/divider+cnt)          '

outa[Brk1..Pwm2]:=%100_001             'off rev

waitcnt(clkfreq/divider+cnt)          '

outa[Brk1..Pwm2]:=%010_010            'rev off

waitcnt(clkfreq/divider+cnt)          '

outa[Brk1..Pwm2]:=%100_101            'off on

waitcnt(clkfreq/divider+cnt)          '

else                                    '

outa[Brk1..Pwm2]:=%011_010            'on  off

waitcnt(clkfreq/divider+cnt)          '

outa[Brk1..Pwm2]:=%100_101            'off on

waitcnt(clkfreq/divider+cnt)          '

outa[Brk1..Pwm2]:=%010_010            'rev off

waitcnt(clkfreq/divider+cnt)          '

outa[Brk1..Pwm2]:=%100_001            'off rev

waitcnt(clkfreq/divider+cnt)          '

{{10 Sep 09  Harprit Sandhu

StepperDistPot.spin

Propeller Tool Ver 1.2.6

Chapter 26 Program 6

RUNNING A STEPPER MOTOR FROM A POTENTIOMETER

STEPPER position FOLLOWS POT position

This program allows you to control the speed of a STEPPER motor

from a potentiometer and run motor back and forth

Xavien amplifier lines are

Coil #1

Brake is on     line P2 of the propeller

PWM is on       line P3 of the propeller

Direction is on line P4 of the propeller

Coil #2

Brake is on     line P5 of the Propeller

Direction is on line P6 of the Propeller

PWM is on       line P7 of the propeller

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000

Brk1=2                         'line assignments

Pwm1=Brk1+1

Dir1=Brk1+2

Dir2=Brk1+3

Brk2=Brk1+4

Pwm2=Brk1+5

VAR                      'these are the variables we will use.

long stack2[35]        'space for Cog_LCD

long stack3[35]        'space for Cog MoveStepper

byte Pcount            'potentiometer reading.

word divider           'divides clkfreq for delays

byte servopos          'servo position

OBJ                      'These are the methods we will need

LCD  : "LCDRoutines4"  'for the LCD methods

UTIL : "Utilities"     'for general methods

PUB Go                          'main Cog

Cognew(MoveStepper,@Stack3)

Cognew(cog_LCD,    @stack2)   'start a new Cog for the LCD

servopos:=32                  'any non 0 OK

repeat                        'this main Cog's main loop

pcount:=UTIL.Read3202_0/16  'get the pot reading from the utilities

repeat 8                    'do 8 at at ime to speed thing up

MoveStepper               'move motor

Pub Cog_LCD                        'set up and run the LCD

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (2,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Target  =" ))     'Potentiometer position ID

LCD.PRINT_DEC(pcount)          'print the pot reading

LCD.SPACE(5)                   'erase over old data

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Position=" ))     'Potentiometer position ID

LCD.PRINT_DEC(servoPos)         'print the pot reading

LCD.SPACE(5)                    'erase over old data

Pub MoveStepper                     'stepper move routine

dira[Brk1..Pwm2]~~                'set at outputs

outa[Brk1..Pwm2]~~                'set high

divider:=750                      'max acceptable divider

case servopos-pcount    'this is the error in the position

-1..-255:            'neg error move to + direction

outa[Brk1..Pwm2]:=%011_010            'on  off

waitcnt(clkfreq/divider+cnt)    '

outa[Brk1..Pwm2]:=%100_101            'off on

waitcnt(clkfreq/divider+cnt)    '

outa[Brk1..Pwm2]:=%010_010            'rev off

waitcnt(clkfreq/divider+cnt)    '

outa[Brk1..Pwm2]:=%100_001            'off rev

waitcnt(clkfreq/divider+cnt)    '

servoPos:=servoPos+1

0:                   'no error so do nothing

1..255:              'pos error so move in- direction

outa[Brk1..Pwm2]:=%011_010            'on  off

waitcnt(clkfreq/divider+cnt)    '

outa[Brk1..Pwm2]:=%100_001            'off rev

waitcnt(clkfreq/divider+cnt)    '

outa[Brk1..Pwm2]:=%010_010            'rev off

waitcnt(clkfreq/divider+cnt)    '

outa[Brk1..Pwm2]:=%100_101            'off on

waitcnt(clkfreq/divider+cnt)    '

servoPos:=servoPos-1

{{10 Sep 09  Harprit Sandhu

StepBackForthPot.spin

Propeller Tool Ver 1.2.6

Chapter 26 Program 8

RUNNING A STEPPER MOTOR FROM A POTENTIOMETER

MOVES BACK AND FORTH

Po1 1 controls distance

Pot 2 controls max speed.

Xavien amplifier lines are same as before

Coil #1

Brake is on     line P2 of the propeller

PWM is on       line P3 of the propeller

Direction is on line P4 of the propeller

Coil #2

Brake is on     line P5 of the Propeller

Direction is on line P6 of the Propeller

PWM is on       line P7 of the propeller

}}

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000

Brk1=2                         'line assignments

Pwm1=Brk1+1

Dir1=Brk1+2

Dir2=Brk1+3

Brk2=Brk1+4

Pwm2=Brk1+5

divstt  = 200          'starting speed

VAR                      'these are the variables we will use.

long stack2[25]        'space for Cog_LCD

long stack3[25]        'space for Cog MoveStepper

word Pcount            'potentiometer reading.

word divider           'divides clkfreq for delays

word divmax            '

OBJ                      'These are the methods we will need

LCD  : "LCDRoutines4"   'for the LCD methods

UTIL : "Utilities"     'for general methods

PUB Go                          'main Cog

Cognew(MoveStepper,@Stack3)   'start new Cog for stepper moves

Cognew(cog_LCD,    @stack2)   'start a new Cog for the LCD

repeat                        'this main Cog's main loop

pcount:=UTIL.Read3202_0/4   '

divmax:=100*UTIL.Read3202_1*2/82+2   'max ia 10000

Pub Cog_LCD                        'set up and run the LCD

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Div =" ))    'Potentiometer position ID

LCD.PRINT_DEC(divider)         'print the pot reading

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (1,12)            'Go to 1st line 1st space

LCD.PRINT_DEC(divmax)          'max division

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (2,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Dist=" ))    'Potentiometer position ID

LCD.PRINT_DEC(pcount)          'print the pot reading

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (2,12)            'Go to 1st line 1st space

LCD.PRINT(STRING("Max"))       'max division

LCD.SPACE(2)                   'erase over old data

PUB MoveStepper

dira[BRK1..PWM2]~~

outa[BRK1..PWM2]~~

divider:=divstt

repeat

repeat pcount

divider:=divider*divstt/(divstt-10)

if divider>divmax

divider:=divmax               'BPD DBP B=Brake,P=PWM,D=direction.

outa[BRK1..PWM2]:=%011_010            'on  off

waitcnt(clkfreq/divider+cnt)    '

outa[BRK1..PWM2]:=%100_101            'off on

waitcnt(clkfreq/divider+cnt)    '

outa[BRK1..PWM2]:=%010_010            'rev off

waitcnt(clkfreq/divider+cnt)    '

outa[BRK1..PWM2]:=%100_001            'off rev

waitcnt(clkfreq/divider+cnt) '

divider:=divstt

waitcnt(clkfreq/3+cnt)

repeat pcount

divider:=divider*divstt/(divstt-10)

if divider>divmax

divider:=divmax

outa[BRK1..PWM2]:=%011_010            'on  off

waitcnt(clkfreq/divider+cnt)    '

outa[BRK1..PWM2]:=%100_001            'off on

waitcnt(clkfreq/divider+cnt)    '

outa[BRK1..PWM2]:=%010_010            'rev off

waitcnt(clkfreq/divider+cnt)    '

outa[BRK1..PWM2]:=%100_101            'off rev

waitcnt(clkfreq/divider+cnt) '

divider:=divstt

waitcnt(clkfreq/3+cnt)

{{24 Sep 09     Harprit Sandhu

StepFromPot.spin

Propeller Tool Ver. 1.2.6

Chapter 26 Program 9

Running a stepper motor from a potentiometer

Moves back and forth a variable distance

Max speed fixed but can be changed at divmax constant

Control distance moved with the potentiometer.

Finished program

This program allows you to control the distance moved by a STEPPER

motor from a potentiometer as it moves back and forth automatically

The number of steps it goes up and down is determined by the pot

and is initially set for a maximum move of ~100 turns for a motor

with 100 steps per revolution. (which I was using).

Display shows the divider value used and Pot reading

Xavien amplifier lines

Coil #1

Brake is on     line P2 of the propeller

PWM is on       line P3 of the propeller

Direction is on line P4 of the propeller

Coil #2

Brake is on     line P5 of the Propeller

Direction is on line P6 of the Propeller

PWM is on       line P7 of the propeller

}}

CON

_CLKMODE=XTAL1+ PLL2X  'The system clock spec

_XINFREQ     =5_000_000

divmax       =8000          'the higher this is the faster the speed

divstart     =200           'starting speed

divDecrement =20            'rate at which speed changes

VAR                      'these are the variables we will use.

long stack1[35]        'space for Cog_LCD

long stack2[35]        'space for Cog MoveStepper

word Pcount            'potentiometer reading.

word divider           'divides clkfreq for delays

OBJ                      'These are the methods we will need

LCD  : "LCDRoutines4"  'for the LCD methods

UTIL : "Utilities"     'for general methods

PUB Go                          'main Cog

Cognew(cog_LCD,    @stack1)   'start a new Cog for the LCD

Cognew(MoveStepper,@Stack2)   'start new Cog for stepper moves

repeat                        'this is main Cogs main loop

pcount:=UTIL.read3202_0/4+1 'get the pot reading from the utilities

PRI Cog_LCD                        'set up and run the LCD

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Div =" ))    'dividing value

LCD.PRINT_DEC(divider)         'print valoue

LCD.SPACE(5)                   'erase over old data

LCD.POSITION (2,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Dist=" ))    'Distance moved

LCD.PRINT_DEC(pcount)          'print value

LCD.SPACE(5)                   'erase over old data

PRI MoveStepper                    '

dira[2..7]~~                     'all outputs

outa[2..7]~~                     'all high

divider:=divstart                'set starting point for div

repeat                           'outer loop

repeat pcount                  'move loop, forward

divider:=divider*divstart/(divstart-divDecrement)

if divider>divmax               'check div

divider:=divmax               'clamp div

outa[2..7]:=%011_010            'on  off

waitcnt(clkfreq/divider+cnt)    '

outa[2..7]:=%100_101            'off on

waitcnt(clkfreq/divider+cnt)    '

outa[2..7]:=%010_010            'rev off

waitcnt(clkfreq/divider+cnt)    '

outa[2..7]:=%100_001            'off rev

waitcnt(clkfreq/divider+cnt)    '

divider:=divstart                  'reset divider

waitcnt(clkfreq/8+cnt)

repeat pcount                     'move loop, backwards

divider:=divider*divstart/(divstart-divDecrement)

if divider>divmax               'check div

divider:=divmax               'clamp div

outa[2..7]:=%011_010            'on  off

waitcnt(clkfreq/divider+cnt)    '

outa[2..7]:=%100_001            'off on

waitcnt(clkfreq/divider+cnt)    '

outa[2..7]:=%010_010            'rev off

waitcnt(clkfreq/divider+cnt)    '

outa[2..7]:=%100_101            'off rev

waitcnt(clkfreq/divider+cnt)

divider:=divstart                 'reset divider

waitcnt(clkfreq/8+cnt)

{{4 Sep 09       Harprit Sandhu

MotorHoldPos.Spin

Propeller Tool Version 1.2.6

Chapter 27 Program 01, 02, 03 depending on gain algorithm in use

This program holds and encoded motor at the starting position.

If you disturb the motor it will return to its initial position.

You may have to adjust the gain variable for your particular motor

You adjust it with POT1. Low values are needed or the motor

oscillates

Connections are

Amplifier brake       P2

Amplifier PWM         P3

Amplifier direction   P4

Potentiometer read through MCP3202 at P18..P21

LCD on the usual      P12..P18 standard. Set Up.

Revisions

OCT 29 08  Revisions to make variable universal

added software runaway IF on motor direction

DEC 24 09  Changed to 3202 pots. Uses PotOne

}}

OBJ

Encoder : "Quadrature Encoder" 'for encoder readings

LCD     : "LCDRoutines4"       'for the LCD methods

UTIL    : "Utilities"          'for general methods

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ    = 5_000_000

MotorRev    =1  'set this to 0 to reverse a runaway motor

'set to 1 for normal operations.

'You can also fix this runaway by reversing

'the encoder leads S1 and S2.

BRK      =2     'Connections to the amplifier

PWM      =BRK+1 'next line

DIR      =BRK+2 'next line

VAR

long     Pos[3]         'Create buffer for encoder

long stack2[25]         'space for Cog_LCD

long stack3[25]         'space for Cog_SetMotorPower

long stack4[25]         'space for Cog_RunMotor

long stack5[25]         'space for Cog_FigureGain

long Pulswidth          'pulse width

long PresPosition       'Present Position

long TargetPosition     'Target Position

long PositionError      'Positional errro

long MinGain            'Minimum gain

long Gain               'Actual gain used

long MaxGain            'Maxim gain permitted

long Index              'Countin ginded

word Integ              'Integration value

word PotOne             'Potentiometer reading

PUB Go

cognew(Cog_LCD,             @stack2)

cognew(Cog_SetMotPower,     @stack3)

cognew(Cog_RunMotor(PWM),   @Stack4)

cognew(Cog_FigGain,         @stack5)

Encoder.Start(0, 1, 0, @Pos)     'Read the encoder position

MaxGain:=2000               'Maxim gain

MinGain:=100                'Minimum gain

repeat

PotOne:=UTIL.Read3202_0   'Read pot

PRI cog_LCD                        'manage the LCD

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Err=" ))     'Error id

LCD.PRINT_DEC(PositionError)   'print error

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (2,1)             'Go to 2nd line 1st space

LCD.PRINT(STRING("Gain=" ))    'Potentiometer

LCD.PRINT_DEC(gain)            'print the gain

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (1,11)            'Go to 2nd line 1st space

LCD.PRINT(STRING("Integ"))     'integrated value

LCD.SPACE(1)                   'set position for cursor

LCD.POSITION (2,11)            'Go to 2nd line 1st space

LCD.PRINT_DEC(Integ)           'print the integ

LCD.SPACE(2)                   'erase over old data

PUB Cog_SetMotPower

dira[BRK..DIR]~~                 'These pins control the motor amp

TargetPosition:=0                'we want to stay where we are

outa[BRK]~                       'turn off the amp brake

repeat                           'loop

PresPosition:=pos[0]           'reads the encoder position

PositionError:=TargetPosition-PresPosition

case PositionError             'decision variable

-1_000_000..-1:              'range

if MotorRev                'negative range

outa[DIR]~~             'move positive

else                       'decide

outa[DIR]~              'move negative

PULSWIDTH:=gain*244/10     'set gain

-0..0 :                      'range for stopping

PULSWIDTH:=0              'gain is set to 0

1..1_000_000:                'range

if MotorRev                'positive range

outa[DIR]~              'move negative

else                       'decide

outa[DIR]~~             'move positive

PULSWIDTH:=gain*244/10     'set gain

PUB Cog_RunMotor(Pin)|WaveLength,period  'subroutine to toggle the output line

dira[BRK..DIR]~~                 'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin# here

frqa:=1                          'Set this counter's frqa value to 1

PulsWidth:=0                     'Start with pulsewidth=0

WaveLength:=clkfreq/100          'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=-PulsWidth               'Send a high pulse for Pulsewidth counts

period:=period+WaveLength      'Calculate wave length

waitcnt(period)                'Wait for the wavelength

PRI Cog_FigGain                     'The Cog we are playing with

repeat                            'loop

gain:=PotOne                    'how we define gain here

{{EXERCISE: Play with the equation on the last line to see what happens

to the motor response.

Turn power to motor off and then turn motor by hand and watch what the

LCD shows and look at PWM line P3 to see what the power to the motor

does while you turn POT1

We will be using this set up a lot so leave it all hooked up

}}

{{4 Sep 09       Harprit Sandhu

MotorHoldPotPos.Spin

Propeller Tool Version 1.2.6

Chapter 28 Program 01

This program moves the encoded motor to a position controlled

by a potentiometer. Range is 4095 encoder counts. This makes a

servo like an R/C hobby servo only much much more powerful.

You may have to adjust the gain variable for your particular motor

Connections are

Amplifier brake         P2

Amplifier PWM           P3

Amplifier direction     P4

Potentiometer 3202      P19..P22

LCD on the usual   P12..P18

Revisions

Oct 09 08  Revisions to make variables universal

Added software runaway fin on motor direction

Dec 24 09  Changed over to 4095 pots

}}

OBJ

Encoder : "Quadrature Encoder"

LCD     : "LCDRoutines4"       'for the LCD methods

UTIL    : "Utilities"          'for general methods

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ    = 5_000_000

MotorRev    =1              'set this to 0 to reverse a runaway motor

'set to 1 for normal operations.

'You can also fix this runaway by reversing

'encoder leads.

BRK      =2

PWM      =BRK+1

DIR      =BRK+2

VAR

long     Pos[3]         'Create buffer for encoder

long stack2[25]         'space for Cog_LCD

long stack3[25]         'space for Cog_SetMotorPower

long stack4[25]         'space for Cog_RunMotor

long stack5[25]         'space for Cog_FigureGain

long Pulswidth          '

long PresPosition       '

long initPosition       '

long TargetPosition     '

long PositionError      '

long MinGain            '

long Gain               '

long MaxGain            '

long Index              '

word Integ              '

word PotOne             '

PUB Go

cognew(Cog_LCD,             @stack2)

cognew(Cog_SetMotPower,     @stack3)

cognew(Cog_RunMotor(PWM),   @Stack4)

cognew(Cog_FigGain,         @stack5)

Encoder.Start(0, 1, 0, @Pos)     'Read the encoder position

MaxGain:=2000

MinGain:=100

repeat

PotOne:=UTIL.Read3202_0

PRI cog_LCD                        'manage the LCD

pulswidth:=89

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Err=" ))     'Error

LCD.PRINT_DEC(PositionError)   'print error

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (2,1)             'Go to 2nd line 1st space

LCD.PRINT(STRING("Gain=" ))    'Potentiometer

LCD.PRINT_DEC(gain)            'print the pot reading

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (1,11)            'Go to 2nd line 1st space

LCD.PRINT(STRING("Integ"))

LCD.SPACE(1)                   'set position for cursor

LCD.POSITION (2,11)            'Go to 2nd line 1st space

LCD.PRINT_DEC(Integ)           'print the index

LCD.SPACE(2)                   'erase over old data

PUB Cog_SetMotPower

dira[BRK..DIR]~~                 'These pins control the motor amp

outa[BRK]~                       'turn off the amp brake

repeat                           'loop

PresPosition:=pos[0]           'reads the encoder position

TargetPosition:=InitPosition+PotOne

PositionError:=TargetPosition-PresPosition

case PositionError             'decisions variable

-1000000..-2:

if MotorRev                'negative range

outa[DIR]~~             'move positive

else

outa[DIR]~              'move negative

PULSWIDTH:=gain*244/10     'set gain

-1..0 :                      'range for stopping

PULSWIDTH:=0              'gain is set to 0

1..1000000:

if MotorRev                'positive range

outa[DIR]~              'move negative

else

outa[DIR]~~             'move positive

PULSWIDTH:=gain*244/10     'set gain

PUB Cog_RunMotor(Pin)|WaveLength,period  'subroutine to toggle the output line,

set

dira[BRK..DIR]~~                 'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin# here

frqa:=1                          'Set this counter's frqa value to 1

PulsWidth:=0                     'Start with pulsewidth=0

WaveLength:=clkfreq/100          'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=-PulsWidth               'Send a high pulse for Pulsewidth counts

period:=period+WaveLength      'Calculate wave length

waitcnt(period)                'Wait for the wavelength

PRI Cog_FigGain

repeat                           'loop

if ||PositionError=<1          'if no error ‘

Integ:=0                    'set the variables to zero

Index:=0                    'set the variables to zero

Else                           'Otherwise

index:=index+1               'increment the index counter

If index==5                    'when it reaches set value

integ:=integ+1              'increase the integrating function

index:=0                    'and reset the index to 0

if integ > 2000                'set limit on integrated gain

integ:=2000                 'clamp value

gain:=8+||positionError+integ  'add it all up for the gain.

gain:=gain <# MaxGain          'gain must be less than MaxGain

{{EXERCISES:

Play with the equation on the last few line to see what happens

to the motor response to the error signal.

Adjust the

TargetPosition:=InitPosition+PotOnne

line to see what happens

Work on making the response faster. There is a delay right now.

How do you handle the overshoot when the gain has to increase real

fast?

Disconnect power to motor and turn shaft and watch the LCD and the

oscilloscope to see how  the gain changes as the error changes.

This is very instructive and very important to understand well.

}}

{{4 Sep 09   Harprit Sandhu

MotorHoldPotSpd.Spin

Propeller Tool Version 1.2.6

Chapter 28 Program 04

This program controls the speed of the motor from a potentiometer.

You may have to adjust the gain variable for your particular motor

Connections are

Amplifier brake         P2

Amplifier PWM           P3

Amplifier direction     P4

Potentiometer          P19

LCD on the usual   P12..P18

Revisions

Oct 09 08  Revisions to make variables universal

Added software runaway fin on motor direction

Dec 24 09  Changed over to 4095 pots

}}

OBJ

Encoder : "Quadrature Encoder"

LCD     : "LCDRoutines4"       'for the LCD methods

UTIL    : "Utilities"          'for general methods

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ    = 5_000_000

MotorRev    =1              'set this to 0 to reverse a runaway motor

'set to 1 for normal operations.

'You can also fix this runaway by reversing

'encoder leads.

BRK      =2

PWM      =BRK+1

DIR      =BRK+2

VAR

long     Pos[3]         'Create buffer for encoder

long stack2[25]         'space for Cog_LCD

long stack3[25]         'space for Cog_SetMotorPower

long stack4[25]         'space for Cog_RunMotor

long stack5[25]         'space for Cog_FigureGain

long Pulswidth          '

long PresPosition       '

long initPosition

long TargetPosition     '

long PositionError      '

long MinGain            '

long Gain               '

long MaxGain            '

long Index              '

word Integ              '

word PotOne             '

PUB Go

cognew(Cog_LCD,             @stack2)

cognew(Cog_SetMotPower,     @stack3)

cognew(Cog_RunMotor(PWM),   @Stack4)

cognew(Cog_FigGain,         @stack5)

Encoder.Start(0, 1, 0, @Pos)     'Read the encoder position

MaxGain:=2000

MinGain:=100

TargetPosition:=0                'we want to stay where we are

repeat

PotOne:=UTIL.Read3202_0

PRI cog_LCD                        'manage the LCD

pulswidth:=89

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Err=" ))     'Error

LCD.PRINT_DEC(PositionError)   'print error

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (2,1)             'Go to 2nd line 1st space

LCD.PRINT(STRING("Gain=" ))    'Potentiometer

LCD.PRINT_DEC(gain)            'print the pot reading

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (1,11)            'Go to 2nd line 1st space

LCD.PRINT(STRING("Integ"))

LCD.SPACE(1)                   'set position for cursor

LCD.POSITION (2,11)            'Go to 2nd line 1st space

LCD.PRINT_DEC(Integ)           'print the index

LCD.SPACE(2)                   'erase over old data

PUB Cog_SetMotPower

dira[BRK..DIR]~~                 'These pins control the motor amp

outa[BRK]~                       'turn off the amp brake

repeat                           'loop

PresPosition:=pos[0]           'reads the encoder position

TargetPosition:=TargetPosition+PotOne/256/3

PositionError:=TargetPosition-PresPosition

case PositionError             'decision variable

-1_000_000..-1:

if MotorRev                'negative range

outa[DIR]~~             'move positive

else

outa[DIR]~              'move negative

PULSWIDTH:=gain*244/10     'set gain

-0..0 :                      'range for stopping

PULSWIDTH:=0              'gain is set to 0

1..1_000_000:

if MotorRev                'positive range

outa[DIR]~              'move negative

else

outa[DIR]~~             'move positive

PULSWIDTH:=gain*244/10     'set gain

PUB Cog_RunMotor(Pin)|WaveLength,period  'subroutine to toggle the output line,

set

dira[BRK..DIR]~~                 'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin# here

frqa:=1                          'Set this counter's frqa value to 1

PulsWidth:=0                     'Start with pulsewidth=0

WaveLength:=clkfreq/100          'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=-PulsWidth               'Send a high pulse for Pulsewidth counts

period:=period+WaveLength      'Calculate wave length

waitcnt(period)                'Wait for the wavelength

PRI Cog_FigGain

repeat                           'loop

if ||PositionError=<1          'if no error ‘

Integ:=0                    'set the variables to zero

Index:=0                    'set the variables to zero

Else                           'Otherwise

index:=index+1               'increment the index counter

If index==5                    'when it reaches set value

integ:=integ+1              'increase the integrating function

index:=0                    'and reset the index to 0

if integ > 2000                'set limit on integrated gain

integ:=2000                 'clamp value

gain:=8+||positionError+integ/4  'add it all up for the gain.

gain:=gain <# MaxGain          'gain must be less than MaxGain

{{EXERCISES:

Play with the equation on the last few line to see what happens

to the motor response to the error signal.

Adjust the

TargetPosition:=TargetPosition+PotOne

line to see what happens

Work on making the response faster. There is a delay right now.

How do you handle the overshoot when the gain has to increase real

fast?

Disconnect power to motor and turn shaft and watch the LCD and the

oscilloscope to see how  the gain changes as the error changes.

This is very instructive and very important to understand well.

}}

{{4 Sep 09   Harprit Sandhu

HoldMotorPotSpd.Spin

Propeller Tool Version 1.2.6

Chapter 28sProgram 05

This program controls the speed of the motor from a potentiometer.

You may have to adjust the gain variable for your particular motor

Connections are

Amplifier brake         P2

Amplifier PWM           P3

Amplifier direction     P4

Potentiometer          P19

LCD on the usual   P12..P18

Revisions

Oct 09 08  Revisions to make variables universal

Added software runaway fin on motor direction

Dec 24 09  Changed over to 4095 pots

}}

OBJ

Encoder : "Quadrature Encoder"

LCD     : "LCDRoutines4"       'for the LCD methods

UTIL    : "Utilities"          'for general methods

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ    = 5_000_000

MotorRev    =1              'set this to 0 to reverse a runaway motor

'set to 1 for normal operations.

'You can also fix this runaway by reversing

'encoder leads.

BRK      =2

PWM      =BRK+1

DIR      =BRK+2

VAR

long     Pos[3]         'Create buffer for encoder

long stack2[25]         'space for Cog_LCD

long stack3[25]         'space for Cog_SetMotorPower

long stack4[25]         'space for Cog_RunMotor

long stack5[25]         'space for Cog_FigureGain

long Pulswidth          '

long PresPosition       '

long initPosition

long TargetPosition     '

long PositionError      '

long MinGain            '

long Gain               '

long MaxGain            '

long Index              '

word Integ              '

word PotOne             '

PUB Go

cognew(Cog_LCD,             @stack2)

cognew(Cog_SetMotPower,     @stack3)

cognew(Cog_RunMotor(PWM),   @Stack4)

cognew(Cog_FigGain,         @stack5)

Encoder.Start(0, 1, 0, @Pos)     'Read the encoder position

MaxGain:=2000

MinGain:=100

TargetPosition:=0                'we want to stay where we are

repeat

PotOne:=UTIL.Read3202_0

PRI cog_LCD                        'manage the LCD

pulswidth:=89

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Err=" ))     'Error

LCD.PRINT_DEC(PositionError)   'print error

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (2,1)             'Go to 2nd line 1st space

LCD.PRINT(STRING("Gain=" ))    'Potentiometer

LCD.PRINT_DEC(gain)            'print the pot reading

LCD.SPACE(2)                   'erase over old data

LCD.POSITION (1,11)            'Go to 2nd line 1st space

LCD.PRINT(STRING("Integ"))

LCD.SPACE(1)                   'set position for cursor

LCD.POSITION (2,11)            'Go to 2nd line 1st space

LCD.PRINT_DEC(Integ)           'print the index

LCD.SPACE(2)                   'erase over old data

PUB Cog_SetMotPower

dira[BRK..DIR]~~                 'These pins control the motor amp

outa[BRK]~                       'turn off the amp brake

repeat                           'loop

PresPosition:=pos[0]           'reads the encoder position

TargetPosition:=TargetPosition+PotOne/256/3

PositionError:=TargetPosition-PresPosition

case PositionError             'decision variable

-1_000_000..-1:

if MotorRev                'negative range

outa[DIR]~~             'move positive

else

outa[DIR]~              'move negative

PULSWIDTH:=gain*244/10     'set gain

-0..0 :                      'range for stopping

PULSWIDTH:=0              'gain is set to 0

1..1_000_000:

if MotorRev                'positive range

outa[DIR]~              'move negative

else

outa[DIR]~~             'move positive

PULSWIDTH:=gain*244/10     'set gain

PUB Cog_RunMotor(Pin)|Cycle_time,period  'subroutine to toggle the output line,

set

dira[BRK..DIR]~~                 'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin# here

frqa:=1                          'Set this counter's frqa value to 1

PulsWidth:=0                     'Start with pulsewidth=0

Cycle_time:=clkfreq/100          'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=-PulsWidth               'Send a high pulse for Pulsewidth counts

period:=period+Cycle_time      'Calculate cycle time

waitcnt(period)                'Wait for the cycle time

PRI Cog_FigGain

repeat                           'loop

if ||PositionError=<1          'if no error ‘

Integ:=0                    'set the variables to zero

Index:=0                    'set the variables to zero

Else                           'Otherwise

index:=index+1               'increment the index counter

If index==5                    'when it reaches set value

integ:=integ+1              'increase the integrating function

index:=0                    'and reset the index to 0

if integ > 2000                'set limit on integrated gain

integ:=2000                 'clamp value

gain:=8+||positionError+integ/4  'add it all up for the gain.

gain:=gain <# MaxGain          'gain must be less than MaxGain

{{EXERCISES:

Play with the equation on the last few line to see what happens

to the motor response to the error signal.

Adjust the

TargetPosition:=TargetPosition+PotOne

line to see what happens

Work on making the response faster. There is a delay right now.

How do you handle the overshoot when the gain has to increase real

fast?

Disconnect power to motor and turn shaft and watch the LCD and the

oscilloscope to see how  the gain changes as the error changes.

This is very instructive and very important to understand well.

}}

{{14 Sep 09       Harprit Sandhu

MotorHoldPotSpdDir.Spin

Propeller Tool Version 1.2.6

Chapter 28  Program 6

This program runs the motor back or forth at a speed and direction

as controlled by the potentiometer.

You may have to adjust the gain variable for your particular motor

Connections are

Amplifier brake       P2

Amplifier PWM         P3

Amplifier direction   P4

Potentiometer         P19

LCD on the usual P12..P18

Revisions

}}

OBJ

Encoder : "Quadrature Encoder"

LCD     : "LCDRoutines4" 'for the LCD methods

UTIL    : "Utilities"  'for general methods

VAR

long     Pos[3]         'Create buffer for two encoders

'plus room for delta position support of 1st encoder)

long stack2[35]         'space for Cog

long stack3[35]         'space for Cog

long stack4[35]         'space for Cog

word pcount             '

long pulswidth          '

word dcount

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000

PotMax   = 100         'The maximum power to the motor OUT OF 255

PotMin   = 0           'The minimum power to the motor OUT OF 255

AmpBrk   = 2

AmpPWM   = AmpBrk+1

AmpDir   = AmpBrk+2

PUB Go

cognew(cog_LCD, @stack2)         'start a new cog

cognew(SetMotorPower, @stack3)   'start a new cog

cognew(RunMotor(AmpPWM),@Stack4)      'start a new cog

Encoder.Start(0, 1, 0, @Pos)     'read encoder

dira[AmpBrk]~~                   'make output

outa[AmpBrk]~                    'turn brake off

PUB SetMotorPower

dira[AmpDir]~~

pos[0]:=0

repeat

pcount:=UTIL.Read3202_0/16    'get the pot reading from the utilities

case pcount                 'depends on pcount

0..127:                   'check for center position

outa[AmpDir]~           'forward direction set

pcount:=(127-pcount)*2  'set center and double the 127 to get near 255

128..129:                 'zero position

pcount:=0               'clamp to 0

130..255:                 'or

outa[AmpDir]~~          'reverse direction

pcount:=(pcount-128)*2  'set center and double the 127 to get near 255

if pcount<PotMin            'check Min value

pcount:=Potmin           'Clamp to Min value

if pcount>PotMax            'check Max value

pcount:=Potmax          'clamp to Max value

PulsWidth:=pcount*450       'multiply reading to get higher count needed

dcount:=pcount

PRI cog_LCD

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("EncCnt=" ))  'Potentiometer position ID

LCD.PRINT_DEC(Pos[0])          'print the pot reading

LCD.SPACE(3)                   'erase over old data

LCD.POSITION (2,1)             'Go to 2nd line 1st space

LCD.PRINT(STRING("Pot   =" ))  'Potentiometer position ID

LCD.PRINT_DEC(dcount)          'print the pot reading

LCD.SPACE(3)                   'erase over old data

PUB RunMotor(Pin)|WaveLength,period   'subroutine to toggle the output line, set

dira[2..4]~~                     'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin

frqa:=1                          'Set this counter's frqa value to 1

PulsWidth:=0                     'Start with position=0

WaveLength:=clkfreq/100          'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=-PulsWidth               'Send a high pulse for Pulsewidth counts

period:=period+WaveLength      'Calculate wave length

waitcnt(period)                'Wait for the wavelength

{{04 Nov 09   Harprit Sandhu

MotorBckForPotGain.Spin

Propeller Tool Version 1.2.6

Chapter 28  Program 7

This program runs the motor back and forth a while you vary

the gain and distance moved with two potentiometers.

Pot1 controls the distance and

Pot2 controls the gain.

How we control the gain is determined by the method that

sets the gain at the bottom of the programs

We will use the information gained here to design the equations

to set the gain to make the move as fast as possible without

overshoot.

You may have to adjust the parameters for your particular motor

Connections are

Amplifier brake       P2

Amplifier PWM         P3

Amplifier direction   P4

Potentiometer        P19

LCD on the usual P8..P18

}}

OBJ

Encoder : "Quadrature Encoder"

LCD     : "LCDRoutines4" 'for the LCD methods

UTIL    : "Utilities"  'for general methods

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000

VAR

long     Pos[3]         'Create buffer for encoder

long stack2[25]         'space for Cog_LCD

long stack3[25]         'space for Cog_SetMotorPower

long stack4[25]         'space for Cog_RunMotor

long stack5[25]         'space for Cog_FigureGain

long stack6[25]         'space for Cog_Start

long stack7[25]         'space for readpots

long pulswidth          '

long PresentPosition    '

long TargetPosition     '

long PositionError      '

long gain               '

long dgain              'displayed gain

word PotReading         '

word startFlag          '

long startPosition      '

long distance           '

long pot1               '

long Pot2               '

PUB Go

cognew(cog_LCD, @stack2)

cognew(SetMotorPower, @stack3)

cognew(RunMotor(3),@Stack4)

cognew(figureGain,  @stack5)

cognew(StrtFlag,  @stack6)

cognew(ReadPots,  @stack7)

Encoder.Start(0, 1, 0, @Pos)  'Reads the encoder position

startPosition:=Pos[0]         'position read

distance:=42*0                'number of 1/4th revs is 8 for 1 rev

repeat

targetPosition:=StartPosition+distance

waitcnt(24_000+cnt)

repeat while startFlag==0

{The start flag is needed to make sure that one instruction

gets done before the nexst instructions starts. This is

managed with the start flag. Try eliminating these

instructions to see what happens. Is there a better way to

manage this. As long as the start flag is 0 the program holds

at this line. It took me a while to get this one figured out!

}

waitcnt(2_000_000+cnt)

targetPosition:=startPosition

waitcnt(24_000+cnt)

repeat while startFlag==0

waitcnt(2_000_000+cnt)

PRI SetMotorPower

dira[2..4]~~                      'These pins control the motor amp

repeat                            'loop

PresentPosition:=pos[0]         'read the encoder position

PositionError:=TargetPosition-PresentPosition

case PositionError              'decision variable

-100_000_000..-2:             'negative range

outa[4]~~                  'move in position direction

PULSWIDTH:=gain*450        'set gain

-1..1 :                       'range for stopping

PULSWIDTH:=0*450           'gain is 0

2..100_000_000:               'positive range

OUTA[4]~                   'move in negative direction

PULSWIDTH:=gain*450        'set gain

PRI cog_LCD                         'manage the LCD

LCD.INITIALIZE_LCD                'initialize the LCD

repeat                            'LCD loop

LCD.POSITION (1,1)              'Go to 1st line 1st space

LCD.PRINT(STRING("Er=" ))       'Error

LCD.PRINT_DEC(PositionError)    'print error

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (1,10)             'Go to 1st line 1st space

LCD.PRINT_DEC(pot1)             'print error

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (1,14)             'Go to 1st line 1st space

LCD.PRINT_DEC(pot2)             'erase over old data

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (2,1)              'Go to 2nd line 1st space

LCD.PRINT(STRING("Gain=" ))     'Potentiometer

LCD.PRINT_DEC(dgain)            'print the pot reading

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (2,10)             'Go to 2nd line 1st space

LCD.PRINT(STRING("Start=" ))    'Potentiometer

LCD.PRINT_DEC(StartFlag)        'print the pot reading

distance:=pot1*21

PRI RunMotor(Pin)|WaveLength,period  'subroutine to toggle the output line, set

dira[2..4]~~                     'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin=3

frqa:=1                          'Set this counter's frqa value to 1

PulsWidth:=0                     'Start with position=0

WaveLength:=clkfreq/100          'Set the time for the wave L to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=-PulsWidth               'Send a high pulse for Pulsewidth counts

period:=period+WaveLength      'Calculate wave length

waitcnt(period)                'Wait for end of wavelength

PRI StrtFlag                 'used to determine if motor completed move

repeat

if ||PositionError<2     'is move almost done

startFlag:=1           'if it is its ok to start

else                     '1f not

startFlag:=0           'do not start next move

PUB figureGain                'power to motor

repeat                      'loop

case ||PositionError      'pot is NOT READ

0..20:gain:=pot2/10           'in these comparisons

21..80:gain:=pot2/4          'the gain is set by the

81..200:gain:=pot2/2        'amount of the error

101..80000:gain:=pot2     'in the position.

gain#>=8

dgain:=gain

PRI Readpots

repeat

pot1:=UTIL.Read3202_0/16

pot2:=UTIL.Read3202_1/16

{{14 Sep 09   Harprit Sandhu

MotorBakForPlayGain.Spin

Propeller Tool Version 1.2.6

Chapter 28  Program 8

This program runs the motor back and forth a fixed number

of counts while you can vary the gain with the equations

at the bottom of the programs to see what happens to

the motor dampening function.  We will use the information

gained here to design the equations to set the gain to make

the move as fast as possible without overshoot.

You may have to adjust the parameters for your particular motor

Connections are

Amplifier brake       P2

Amplifier PWM         P3

Amplifier direction   P4

Potentiometer        P19

LCD on the usual P8..P18

}}

OBJ

Encoder : "Quadrature Encoder"

LCD     : "LCDRoutines4" 'for the LCD methods

UTIL    : "Utilities"  'for general methods

CON

_CLKMODE=XTAL1+ PLL2X   'The system clock spec

_XINFREQ = 5_000_000

distance =168*8         'full revs

VAR

long     Pos[3]         'Create buffer for encoder

long stack2[25]         'space for Cog_LCD

long stack3[25]         'space for Cog_SetMotorPower

long stack4[25]         'space for Cog_RunMotor

long stack5[25]         'space for Cog_FigureGain

long stack6[25]         'space for Cog_Start

long pulswidth          '

long PresentPosition    '

long gain               '

long TargetPosition     '

long PositionError      '

byte startFlag          '

long startPosition      '

PUB Go

cognew(cog_LCD, @stack2)

cognew(SetMotorPower, @stack3)

cognew(RunMotor(3),@Stack4)

cognew(figureGain,  @stack5)

cognew(StaartFlag,  @stack6)

Encoder.Start(0, 1, 0, @Pos)     'Reads the encoder position

startPosition:=Pos[0]

repeat

targetPosition:=StartPosition+distance

waitcnt(10000+cnt)

repeat while startFlag==0

waitcnt(2_000_000+cnt)

targetPosition:=startPosition

waitcnt(10000+cnt)

repeat while startFlag==0

waitcnt(2_000_000+cnt)

PUB SetMotorPower

dira[2..4]~~                      'These pins control the motor amp

repeat                            'loop

PresentPosition:=pos[0]         'read the encoder position

PositionError:=TargetPosition-PresentPosition

case PositionError              'decision variable

-100_000_000..-2:             'negative range

outa[4]~~                  'move in position direction

PULSWIDTH:=gain*450        'set gain

-1..1 :                       'range for stopping

PULSWIDTH:=0*450           'gain is 0

2..100_000_000:               'positive range

OUTA[4]~                   'move in negative direction

PULSWIDTH:=gain*450        'set gain

PRI cog_LCD                         'manage the LCD

LCD.INITIALIZE_LCD                'initialize the LCD

repeat                            'LCD loop

LCD.POSITION (1,1)              'Go to 1st line 1st space

LCD.PRINT(STRING("Err=" ))      'Error

LCD.PRINT_DEC(PositionError)    'print error

LCD.SPACE(5)                    'erase over old data

LCD.POSITION (2,1)              'Go to 2nd line 1st space

LCD.PRINT(STRING("Gain=" ))     'gain

LCD.PRINT_DEC(gain)             'print the pot reading

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (2,10)             'Go to 2nd line 1st space

LCD.PRINT(STRING("Start=" ))    'Flag

LCD.PRINT_DEC(StartFlag)        'print flag status

PUB RunMotor(Pin)|WaveLength,period       'subroutine to toggle the output line,

set

dira[2..4]~~                     'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin

frqa:=1                          'Set this counter's frqa value to 1

PulsWidth:=0                     'Start with position=0

WaveLength:=clkfreq/100          'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=-PulsWidth               'Send a high pulse for Pulsewidth counts

period:=period+WaveLength      'Calculate wave length

waitcnt(period)                'Wait for the wavelength

PUB figureGain                     'power to motor 0-255

repeat                           'loop

case ||PositionError           'pot is NOT READ

1..20:gain:=6                'in these comparisons

21..80:gain:=10              'the gain is set by the

81..200:gain:=40             'amount of the error

101..80000:gain:=80          'in the position.

PRI StaartFlag             'The start flag is used to inhibit the execution of

repeat                   'the next move to make sure that each move executes

if ||PositionError<2   'fully. Then the wait command lets you see that the

startFlag:=1         'motor actually stopped before proceeding to reversing

else                   'the motor.  See main Cog above for more.

startFlag:=0

{{14 Sep 09   Harprit Sandhu

MotorPotSpeedTable.Spin

Propeller Tool Version 1.2.6

Chapter 28 Program 9

This program controls speed of motor from the pot.

Displays speed and pot setting

You may have to adjust the gain variable for your particular motor

Connections are

Encoder 1             P0

Encoder 2             P1

Encoder 3             5 Volts

Encoder 4             Ground

Also need power and ground for encoder connected

Amplifier brake       P2    Xavien  1

Amplifier PWM         P3    Xavien  2

Amplifier direction   P4    Xavien  3

Potentiometer        P19

LCD on the usual P8..P18

The values read are based on a 13.5 volts power

supply for the motor. (Table in book)

}}

OBJ

Encoder : "Quadrature Encoder"

LCD     : "LCDRoutines4" 'for the LCD methods

UTIL    : "Utilities"    'for general methods

CON

_CLKMODE=XTAL1+ PLL2X         'The system clock spec

_XINFREQ = 5_000_000

VAR

long     Pos[3]         'Create buffer for encoder

long stack2[25]         'space for Cog_LCD

long stack3[25]         'space for Cog_SetMotorPower

long stack4[25]         'space for Cog_RunMotor

long stack5[25]         'space for Cog_FigureGain

long pulswidth          '

long speed              '

long start              '

long end                '

PUB Go

cognew(cog_LCD, @stack2)

cognew(SetMotorPower, @stack3)

cognew(RunMotor(3),@Stack4)

cognew(FigureCounts,  @stack5)

Encoder.Start(0, 1, 0, @Pos)      'Read the encoder position

PUB SetMotorPower

dira[2..4]~~                      'These pins control the motor amp

repeat                            'loop

PulsWidth:=Util.Read3202_0/16   'read the 4095 pot position to a byte

PRI cog_LCD                        'manage the LCD

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Speed=" ))   'Error

LCD.PRINT_DEC(Speed)           'print error

LCD.SPACE(3)                   'erase over old data

LCD.POSITION (2,1)             'Go to 2nd line 1st space

LCD.PRINT(STRING("Gain =" ))   'Potentiometer

LCD.PRINT_DEC(pulswidth)            'print the pot reading

LCD.SPACE(3)                   'erase over old data

PUB RunMotor(Pin)|Cycle_time,period   'subroutine to toggle the output line, set

dira[2..4]~~                     'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin

frqa:=1                          'Set this counter's frqa value to 1

PulsWidth:=0                     'Start with position=0

Cycle_time:=clkfreq/100          'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=-PulsWidth*24*16         'Send a high pulse for Pulsewidth counts

period:=period+Cycle_time      'Calculate cycle time

waitcnt(period)                'Wait for the cycle time

PUB FigureCounts                   'encoder counts

repeat                           'loop

start:=Pos[0]                  'read encoder

waitcnt(clkfreq+cnt)           'pause 1 sec

end:=Pos[0]                    'read encoder

speed:=(end-start)             'counts moved

{{

Chapter 28 Prog 10

}}

PUB FigureGain             'power to motor

repeat                   'loop

Case time              'base the gain on the time segment number

0..50:               'first 50 segments

gain:=20           'slow speed

51..150:             'next 100 segments

gain:=100          'fast speed

151..200:            'next 50 segments

gain:=20           'slow speed

201..300:            'next 100 segments

gain:=0            'Gain=0 means stop for a while

waitcnt(120_000+cnt)   'define length of each time segment as 0.1 secs

time:=time+1           'add to time segment number

if time==300           'check top time value

time:=0              'reset time counter

{{4 Sep 09   Harprit Sandhu

MotorSloFstSlo.Spin

Propeller Tool Version 1.2.6

Chapter 28  Program 11

This program moves the motor in a slow, fast ,slow, stop sequence

to demonstrate the control of the speed over a period of equal time

segments. This is an absolutely minimal ramping demonstration. Only

two speeds are used. This could be expanded to a very complicated

algorithm with lots of gains and speed specifications.

We are not using the encoder or the potentiometers in this program.

Connections are

Amplifier brake       P2

Amplifier PWM         P3

Amplifier direction   P4

Potentiometer        P19

LCD on the usual P12..P18 4 bit mode

Revisions

}}

OBJ

LCD     : "LCDRoutines4" 'for the LCD methods

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ    = 5_000_000

AmpBrake    =2

AmpPWM      =3

MotorDir    =4

VAR

long     Pos[3]         'Create buffer for encoder

long stack2[25]         'space for Cog_LCD

long stack3[25]         'space for Cog_SetMotorPower

long stack4[25]         'space for Cog_RunMotor

long stack5[25]         'space for Cog_FigureGain

long gain               '

long time

long pulswidth

PUB Go

cognew(cog_LCD, @stack2)

cognew(SetMotorPower, @stack3)

cognew(RunMotor(AmpPWM),@Stack4)

cognew(FigureGain,  @stack5)

repeat

PRI cog_LCD                        'manage the LCD

LCD.INITIALIZE_LCD               'initialize the LCD

repeat                           'LCD loop

LCD.POSITION (1,1)             'Go to 1st line 1st space

LCD.PRINT(STRING("Time=" )) 'Error

LCD.PRINT_DEC(time)             'print the pot reading

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (2,1)             'Go to 2nd line 1st space

LCD.PRINT(STRING("Gain=" ))     'Potentiometer

LCD.PRINT_DEC(gain)             'print the pot reading

LCD.SPACE(2)                    'erase over old data

PUB SetMotorPower

dira[AmpBrake..MotorDir]~~       'These pins control the motor amp

outa[AmpBrake]~                  'turn off the amp brake

repeat                           'loop

outa[MotorDir]~                'move negative

PULSWIDTH:=gain*450            'set gain

PUB RunMotor(Pin)|WaveLength,period   'subroutine to toggle the output line, set

dira[AmpBrake..MotorDir]~~       'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin# here

frqa:=1                          'Set this counter's frqa value to 1

PulsWidth:=0                     'Start with pulsewidth=0

WaveLength:=clkfreq/50           'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=-PulsWidth               'Send a high pulse for Pulsewidth counts

period:=period+WaveLength      'Calculate wave length

waitcnt(period)                'Wait for the wavelength

PUB FigureGain             'power to motor

repeat                   'loop

Case time              'base the gain on the time segment number

0..100:              'first 50 segments

gain:=30           'slow speed

101..200:            'next 100 segments

gain:=200          'fast speed

201..300:            'next 50 segments

gain:=30           'slow speed

301..399:            'next 100 segments

gain:=0            'Gain=0 means stop for a while

waitcnt(120_000+cnt)   'define length of each time segment as 0.1 secs

time:=time+1           'add to time segment number

if time==400           'check top time value for reset

waitcnt(clkfreq/4+cnt) 'wait to look at LCD

time:=0              'reset time counter

{{14 Sep 09   Harprit Sandhu

MotorPositionRC.Spin

Propeller Tool Version 1.2.6

Chapter 28  Program 14

This program Positions the DC motor from a hobby R/C transmitter

just like it would a R/C hobby servo, but many revs

You may have to adjust the parameters for your particular motor

Connections are

Amplifier brake       P2

Amplifier PWM         P3

Amplifier direction   P4

Radio signal in       P24

LCD on the usual      P8..P18

}}

OBJ

Encoder : "Quadrature Encoder"

LCD     : "LCDRoutines4" 'for the LCD methods

UTIL    : "Utilities"  'for general methods

CON

_CLKMODE=XTAL1+ PLL2X   'The system clock spec

_XINFREQ = 5_000_000

BRK      =2

PWM      =BRK+1

DIR      =BRK+2

PulseIn  =24

VAR

long     Pos[3]         'Create buffer for encoder

long stack2[35]         'space for Cog_LCD

long stack3[35]         'space for Cog_SetMotorPower

long stack4[35]         'space for Cog_RunMotor

long stack5[35]         'space for Cog_Encoder

long startcycle         '

long endPulse           '

long endCycle           '

long CycleLen           '

long PulseLen           '

long pulswidth

long freq               '

long MotPwr             '

long PresPos

long TargPos

PUB Go

cognew(cog_LCD,       @stack2)

cognew(SetMotorPower, @stack3)

cognew(PosMotor(3),   @Stack4)

cognew(Enco,          @Stack5)

Encoder.Start(0, 1, 0, @Pos)       'Read the encoder position

Dira[PulseIn]~

repeat

waitpeq(|<PulseIn, |<PulseIn, 0)  'wait for line to go low.

waitpeq(0, |<PulseIn, 0)          'wait for line to go low.

waitpeq(|<PulseIn, |<PulseIn, 0)  'wait for line to go low.

startCycle:=CNT                   'read the timer count 0)

waitpeq(0, |<PulseIn, 0)          'wait for line to go low...

endPulse:=CNT                     'read the timer count for second time

waitpeq(|<PulseIn, |<PulseIn, 0)  'wait for line to go low.

endCycle:=CNT                     'read the timer count for second time

pulswidth:=(endPulse-startCycle)  'figure the pulse

freq:=clkfreq/(endCycle- startCycle)  'figure the freq

PRI cog_LCD                         'manage the LCD

LCD.INITIALIZE_LCD                'initialize the LCD

repeat                            'LCD loop

LCD.POSITION (1,1)              'Go to 1st line 1st space

LCD.PRINT(STRING("POSN=" ))     'P0SITION

LCD.PRINT_DEC(Prespos)          'print position

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (1,11)             'Go to 1st line 11 space

LCD.PRINT(STRING("DIR=" ))      'Direction of motor power

LCD.PRINT_DEC(ina[Dir])         'print

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (2,1)              'Go to 2nd line 1st space

LCD.PRINT(STRING("TARG=" ))     'TARGET

LCD.PRINT_DEC(TargPos)          'print

LCD.SPACE(2)                    'erase over old data }

PUB SetMotorPower

dira[BRK..DIR]~~                  'These pins control the motor amp

repeat                            '

targPos:=pulswidth/10           'loop

if TargPos<PresPos              '

OUTA[DIR]~~                  '

dira[BRK]~                   '

MotPwr:=||(TargPos-PresPos)*200

if TargPos==PresPos             '

dira[BRK]~~                  '

MotPwr:=0                    '

if TargPos>PresPos              '

OUTA[DIR]~                   '

dira[BRK]~                   '

MotPwr:=4|(TargPos-PresPos)*200    '

PUB PosMotor(Pin)|WaveLength,period  'subroutine to toggle the output line

dira[BRK..DIR]~~                 'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin# here

frqa:=1                          'Set this counter's frqa value to 1

motpwr:=0                        'Start with pulsewidth=0

WaveLength:=clkfreq/100          'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=-MotPwr                  'Send a high pulse for Pulsewidth counts

period:=period+WaveLength      'Calculate wave length

waitcnt(period)                'Wait for the wavelength

PRI Enco

dira[0..1]~

repeat

PresPos:=Pos[0]

{{14 Sep 09   Harprit Sandhu

MotorSpeedDirRC.Spin

Propeller Tool Version 1.2.6

Chapter 28  Program 15

This program runs the motor back and forth from a

signal received from a hobby R/C transmitter as would

be use by a servo

You may have to adjust the parameters for your particular motor

Connections are

Amplifier brake       P2

Amplifier PWM         P3

Amplifier direction   P4

Radio signal in       P24

LCD on the usual      P8..P18

}}

OBJ

Encoder : "Quadrature Encoder"

LCD     : "LCDRoutines4" 'for the LCD methods

UTIL    : "Utilities"  'for general methods

CON

_CLKMODE=XTAL1+ PLL2X   'The system clock spec

_XINFREQ = 5_000_000

BRK      =2

PWM      =BRK+1

DIR      =BRK+2

RadioIn  =24

VAR

long     Pos[3]         'Create buffer for encoder

long stack2[25]         'space for Cog_LCD

long stack3[25]         'space for Cog_SetMotorPower

long stack4[25]         'space for Cog_RunMotor

long startcycle         '

long endPulse           '

long endCycle           '

long CycleLen           '

long PulseLen           '

long freq               '

long MotPwr             '

PUB Go

cognew(cog_LCD,       @stack2)

cognew(SetMotorPower, @stack3)

cognew(RunMotor(3),@Stack4)

Dira[RadioIn]~

repeat

repeat while ina[RadioIn]==1     'wait for line 1 to go low.

'make sure that we see

'at full wave when we start measuring

repeat while ina[RadioIn]==0     'wait for line 1 to go low. See Manual

startCycle:=CNT                  'read the timer count

repeat while ina[RadioIn]==1     'wait for line 1 to go hi. See Manual

endPulse:=CNT                    'read the timer count for second time

repeat while ina[RadioIn]==0     'wait for line 1 to go low. See Manual.

endCycle:=cnt

PulseLen:=(endPulse-startCycle)/10    'figure the pulse

CycleLen:=endCycle-startCycle         'figure the cycleLen

freq:=10_000_000/CycleLen             'figure the freq

PRI cog_LCD                         'manage the LCD

LCD.INITIALIZE_LCD                'initialize the LCD

repeat                            'LCD loop

LCD.POSITION (1,1)              'Go to 1st line 1st space

LCD.PRINT(STRING("PWR=" ))      'Power

LCD.PRINT_DEC(MotPwr)           'print power

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (1,11)             'Go to 1st line 11 space

LCD.PRINT(STRING("DIR=" ))      'Direction

LCD.PRINT_DEC(ina[Dir])         'print

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (2,1)              'Go to 2nd line 1st space

LCD.PRINT(STRING("WLN=" ))      'Cycle length

LCD.PRINT_DEC(CycleLen)         'print

LCD.SPACE(2)                    'erase over old data

LCD.POSITION (2,11)             'Go to 2nd line 11 space

LCD.PRINT(STRING("FRQ=" ))      'Freq

LCD.PRINT_DEC(freq)             'print

LCD.SPACE(2)                    'erase over old data

PUB SetMotorPower

dira[BRK..DIR]~~                  'These pins control the motor amp

repeat                            'loop

case pulselen                  '

300..1500:                   'low vzlues

outa[DIR]~                 'Motor dir low

MotPwr:=1500-pulselen      'reset value

1501..3000:                  'high values

outa[DIR]~~                'Motor dir hi

MotPwr:=pulselen-1500      'reset value

PUB RunMotor(Pin)|WaveLength,period   'subroutine to toggle the output line, set

dira[2..4]~~                     'gain access to these three amplifier lines

ctra[30..26]:=%00100             'Set this cog's "A Counter" to run PWM

ctra[5..0]:=Pin                  'Set the "A pin" of this cog to Pin

frqa:=1                          'Set this counter's frqa value to 1

PulseLen:=0                      'Start with position=0

WaveLength:=clkfreq/100          'Set the time for the pulse width to 10 ms

period:=cnt                      'Store the current value of the counter

repeat                           'power PWM routine.

phsa:=(-MotPwr+70)*50          'Send a high pulse for Pulsewidth counts

period:=period+WaveLength      'Calculate wave length

waitcnt(period)                'to end of wave

{{21 Sep 09     Harprit Sandhu

LCDRoutines4.spin

Propeller Tool Version 1.2.6

Appendix

LCD ROUTINES for a 4 bit data path.

The following are the names of the methods described in this program

INITIALIZE_LCD

PRINT (the_line)

POSITION (LINE_NUMBER, HOR_POSITION) | CHAR_LOCATION

SEND_INSTRUCTION (DISPLAY_CHAR)

SEND_INSTRUCTION2 (DISPLAY_CHAR)

SEND_CHAR (DISPLAY_CHAR)

PRINT_DEC (VALUE) | TEST_VALUE

PRINT_HEX (VALUE, DIGITS)

PRINT_BIN (VALUE, DIGITS)

CLEAR

HOME

SPACE (QTY)

Revisions

04 Oct 09  Initialize made more robust, misc unnecessary calls removed.

10 Apr 10  Added 4 lines and eliminated blink on cursor

}}

CON                             'all the constants used by all the METHODS

'in this program have to be listed here

_CLKMODE=XTAL1 + PLL4X        'The system clock spec. 2 X multiplier

_XINFREQ   = 5_000_000        'ext crystal is 5 Mhz, so 10 Mhz operation

DataBit4   = 12               'are named so that they can be called by

DataBit5   = 13               'name if the need ever arises

DataBit6   = 14               '

DataBit7   = 15               '

RegSelect  = 16               'The three control lines

ReadWrite  = 17               'The three control lines

Enable     = 18               'The three control lines

high       =1                 'define the High state

low        =0                 'define the Low state

Inv_high   =0                 'define the Inverted High state

Inv_low    =1                 'define the Inverted Low state

VAR                             'these are the variables we will use

byte  temp                   'for use as a pointer

byte  index                  'to count characters

PUB Go

INITIALIZE_LCD

repeat

position(1,1)

print(String("Test routine only"))

position(2,1)

print(String("4 bit mode line 2"))

position(3,1)

print(String("4 bit mode line 3"))

position(4,1)

print(String("4 bit mode line 4"))

waitcnt(clkfreq/2+cnt)

clear

waitcnt(clkfreq/4+cnt)

PUB INITIALIZE_LCD                'The addresses and data used here are

{{initialize the LCD to use 4 lines of data

Includes the 1/20 second delay, clears the display and positons to 1,1

no variables used}}

waitcnt(clkfreq/20+cnt)         'specified in the Hitachi data sheet for the

DIRA[DataBit4..Enable]~~        'display. YOU MUST CHECK THIS FOR

YOURSELF.

SEND_INSTRUCTION (%0011)        'Send 1st

waitcnt(clkfreq/200+cnt)        'wait

SEND_INSTRUCTION (%0011)        'Send 2nd

waitcnt(clkfreq/8_000+cnt)      'wait

SEND_INSTRUCTION (%0011)        'Send 3rd

waitcnt(clkfreq/8_000+cnt)      'wait

SEND_INSTRUCTION (%0010)        'set for 4 bit mode

waitcnt(clkfreq/8_000+cnt)      'wait

SEND_INSTRUCTION2 (%0010_1000)  'Sets DL=4 bits, N=2 lines, F=5x7 font

waitcnt(clkfreq/8_000+cnt)      'wait

SEND_INSTRUCTION2 (%0000_1100)  'Display on, Blink off, Sq Cursor off

waitcnt(clkfreq/8_000+cnt)      'wait

SEND_INSTRUCTION2 (%0000_0110)  'Move Cursor, Do not shift display

waitcnt(clkfreq/8_000+cnt)      'wait

SEND_INSTRUCTION2 (%0000_0001)  'clears the LCD

waitcnt(clkfreq/8_000+cnt)      'wait

POSITION (1,1)

PUB SEND_INSTRUCTION (D_DATA)        'set up for writing instructions

{{Sends instruction as opposed to a character to the LCD

no variables are used}}

CHECK_BUSY                         'wait for busy bit to clear before sending

OUTA[ReadWrite] := 0               'Set up to read busy bit

OUTA[RegSelect] := 0               'Set up to read busy bit

OUTA[Enable]    := 1               'Set up to toggle bit H>L

OUTA[DataBit7..DataBit4] := D_DATA 'Ready to READ data in

OUTA[Enable]    := 0               'Toggle the bit H>L to xfer the data

PUB SEND_INSTRUCTION2 (D_DATA)      'set up for writing instructions

{{Sends a character to the LCD no variables are used}}

CHECK_BUSY                        'wait for busy bit to clear before sending

OUTA[ReadWrite] := 0              'Set up to read busy bit

OUTA[RegSelect] := 0              'Set up to read busy bit

OUTA[Enable]    := 1              'Set up to toggle bit H>L

OUTA[DataBit7..DataBit4] := D_DATA>>4   'Ready to READ data in

OUTA[Enable]    := 0                 'Toggle the bit H>L to xfer the data

OUTA[Enable]    := 1                 'Set up to toggle bit H>L

OUTA[DataBit7..DataBit4] := D_DATA   'Ready to READ data in

OUTA[Enable]    := 0                 'Toggle the bit H>L to xfer the data

PUB SEND_CHAR (D_CHAR)           'set up for writing to the display

{{Sends a single character to the LCD in two halves}}

CHECK_BUSY                     'wait for busy bit to clear before sending

OUTA[ReadWrite] := 0           'Set up to send data

OUTA[RegSelect] := 1           'Set up to send data

OUTA[Enable]    := 1           'go high

OUTA[DataBit7..DataBit4] := D_CHAR>>4  'Send high 4 bits

OUTA[Enable]    := 0                 'Toggle the bit H>L

OUTA[Enable]    := 1                 'go high again

OUTA[DataBit7..DataBit4] :=D_CHAR    'send low 4 bits

OUTA[Enable]    := 0                 'Toggle the bit H>L

PUB PRINT (the_line)

{{Print a line of characters to the LCD uses variables index and temp}}

'This routine handles more than one Char at a time

'called as PRINT(string("the_line"))

' "the_line" contains the pointer to line. Line is

'because we have to point to the line

'zero terminated but we will not use that.  We will

'use the string size instead. Easier to understand

index:=0                 'Reset the counter we are using to count chars sent

repeat                   'repeat for all chars in the list

temp:= byte[the_line][index++] 'temp contains the char/byte pointed by index

SEND_CHAR (temp)               'send the 'pointed to' char to the LCD

while index<strsize(the_line)    'keep doing it till the last char is sent

PUB POSITION (LINE_NUMBER, HOR_POSITION) | CHAR_LOCATION

{{Position cursor}}  'Line Number : 1 to 4

'Horizontal Position : 1 to 20          'specified by the two numbers

case LINE_NUMBER

1,2:

CHAR_LOCATION := (LINE_NUMBER-1) * 64   'figure location. See Hitachi

HD44780

CHAR_LOCATION += (HOR_POSITION-1) + 128 'figure location. See Hitachi

HD44780

3:

CHAR_LOCATION :=148+(HOR_POSITION-1)'for line 3

4:

CHAR_LOCATION :=212+(HOR_POSITION-1)'for line 4

SEND_INSTRUCTION2 (CHAR_LOCATION)       'send the instruction to position

cursor

PUB CHECK_BUSY | BUSY_BIT              'routine to check busy bit

{{Check for busy}}

OUTA[ReadWrite] := 1                 'Set to read the busy bit

OUTA[RegSelect] := 0                 'Set to read the busy bit

DIRA[DataBit7..DataBit4] := %0000    'Set the entire port to be an input

REPEAT                          'Keep doing it till clear

OUTA[Enable]  := 1            'set to 1 to get ready to toggle H>L this bit

BUSY_BIT := INA[DataBit7]     'the busybit is bit 7 of the byte read

'INA is the 32 input pins on the PROP and we

'are reading data bit 7 which is on pin 15!

OUTA[Enable]  := 0            'make the enable bit go low for H>L toggle

WHILE (BUSY_BIT == 1)           'do it as long as the busy bit is 1

DIRA[DataBit7..DataBit4] := %1111 'done, so set the data port back to outputs

PUB PRINT_DEC (VALUE) | TEST_VALUE   'for printing values in decimal format

{{Print a decimal value, whole numbers only}}

IF (VALUE < 0)                  'if it is a negative value

-VALUE                        'change it to a positive

SEND_CHAR("-")                'and print a - sign on the LCD

TEST_VALUE := 1_000_000_000     'we get individual digits by comparing to this

'value and then dividing by 10 to get next value

REPEAT 10                       'There are 10 digits maximum in our system

IF (VALUE => TEST_VALUE)      'see if our number is bigger than testValue

SEND_CHAR(VALUE / TEST_VALUE + "0")     'if it is, divide to get the digit

VALUE //= TEST_VALUE        'figure the next value for the next digit

RESULT~~                    'result of what just did pass it on below

ELSEIF (RESULT OR TEST_VALUE == 1) 'if the result was a 1 then div was

even

SEND_CHAR("0")               'so we sent out a zero

TEST_VALUE /= 10               'we divide by 10 to test for the next digit

PUB PRINT_HEX (VALUE, DIGITS)     'for printing values in HEX format

{{Print a Hexadecimal value}}

VALUE <<= (8 - DIGITS) << 2     'you can specify up to 8 digits or FFFFFFFF

max

REPEAT DIGITS                   'do each digit

SEND_CHAR(LOOKUPZ((VALUE <-= 4) & $F : "0".."9", "A".."F"))

'use lookup table to select character

'

PUB PRINT_BIN (VALUE, DIGITS)          'for printing values in BINARY format

{{Print a Binary value}}

VALUE <<= 32 - DIGITS                '32 binary digits is the max for our sys

REPEAT DIGITS                        'Repeat for each digit desired

SEND_CHAR((VALUE <-= 1) & 1 + "0") 'send a 1 or a 0

{{Clear screen}}

PUB CLEAR                              'Clear the LCD display and go home

SEND_INSTRUCTION2 (%0000_0001)       'This is the clear screen and go home

command

PUB HOME                               'go to position 1,1.

{{Go to position 1,1   Does not clear the screen}}

SEND_INSTRUCTION2 (%0000_0011)       'Not cleared

PUB SPACE (qty)                        'Prints spaces, for between numbers

{{Print spaces}}

repeat (qty)

PRINT(STRING(" "))

{{21 Sep 09    Harprit Sandhu

Utilities.spin

Propeller Tool Ver 1.2.6

Appendix

Program UTILITIES

Flash         flashes a pin once, toggles it slowly

Pause         pause in milliseconds

GetPotValue   returns PotValue  0-255

GetPotValue2  returns PotValue  0-255

Read3202_0    reads Channel 0 on the 3202, 0-4095

Read3202_1    reads Channel 1 on the 3202, 0-4095

Since the pot readers are an important part of

the utilities, they are read separately

Using two methods allows you to use two different pot values

one for each pot.

Potentiometer connections are as follows

3202 connections

1  Chip select

2  Pot 1  xxxxxxxxxxxxxxxxx

3  Pot 2  xxxxxxxxxxxxxxxxx

4  Ground

5  Data In

6  Data out

7  Clock

8  5 Volts

Prop connections from 3202 are

chipSel  = 19

chipClk  = chipSel+1

chipDout = chipSel+2

chipDin  = chipSel+3

Revisions

21 Sep 09   Set min and max for Pot readings, reduced delay div

from 2920 to 2900

Displays both pots and both delays now.

Using two routines to read the pots allows two pots

with different values to be set used. Have to be set

up. Currently they are identical.

New Xtal changes made.

14 Nov 09   Added potvalue2 to read second pot.

Added ReadChannel,X to read any of 2 channels from

a MCP 3202

14 Nov 09   Added independent routines to read the two lines of

A2D on the MCP3202.

18 May 10   Added connections comments above.

Error Reporting:

Please report errors to harprit.sandhu@gmail.com

}}

CON

_CLKMODE=XTAL1 + PLL2X         'The system clock spec

_XINFREQ = 5_000_000           'the oscillator frequency

high     =1

low      =0

PotLine  =19

PotLine2 =20

repval   =2

repval2  =2

BitsRead =12

BitsRead2=12

BitsRead3 =12

BitsRead4=12

chipSel  = 19

chipClk  = chipSel+1

chipDout = chipSel+2

chipDin  = chipSel+3

chipSel2  = 23

chipClk2  = chipSel2+1

chipDout2 = chipSel2+2

chipDin2  = chipSel2+3

VAR

long  startCnt

long  startCnt2

long  endCount

long  endCount2

long  delay

long  delay2

long  PotValue

long  PotValue2

long  ValuTotal

long  ValuTotal2

word  PotReading1

word  PotReading2

word  PotReading3

word  PotReading4

word  DataRed

OBJ                              'The methods we will need

LCD  : "LCDRoutines4"          'for controlling the LCD

PUB Go

LCD.INITIALIZE_LCD              'set up the LCD

repeat

LCD.POSITION (1,1)            'Go to 1st line 1st space

LCD.PRINT(STRING("Pot1="))    'Potentiometer position

LCD.PRINT_DEC(PotReading1)    'print pot value

LCD.SPACE(3)                  'erase over old data

LCD.POSITION (2,1)            'Go to 1st line 1st space

LCD.PRINT(STRING("Pot2="))    'Potentiometer position

LCD.PRINT_DEC(PotReading2)    'print pot value

LCD.SPACE(3)                  'erase over old data

LCD.POSITION (3,1)            'Go to 1st line 1st space

LCD.PRINT(STRING("Pot3="))    'Potentiometer position

LCD.PRINT_DEC(PotReading3)    'print pot value

LCD.SPACE(3)                  'erase over old data

LCD.POSITION (4,1)            'Go to 1st line 1st space

LCD.PRINT(STRING("Pot4="))    'Potentiometer position

LCD.PRINT_DEC(PotReading4)    'print pot value

LCD.SPACE(3)                  'erase over old data

Read3202_0                    'Read Pot routine

Read3202_1                    'Read Pot routine2

Read3202_2                    'Read Pot routine3

Read3202_3                    'Read Pot routine4

PUB FLASH (color)               'routine to flash an LED by color

outa[color] :=high          'line that actually sets the LED high

pause (200)                 'wait till counter reaches this value

outa[color] :=low           'line that actually sets the LED low

pause (200)                 'wait till counter reaches this value

'

PUB PAUSE(millisecs)            'As set up here it is 1.0 millisecconds

if millisecs>0

waitcnt((clkfreq/1_000)*millisecs +cnt)      'ms based on Osc freq

PUB GetPotVal

dira[PotLine]~~                'set potline as output

valutotal:=0                   'clear total

repeat  repval               'repeat

dira[PotLine]~~            'set potline as output

outa[PotLine]~~            'make it high so we can charge the capacitor

waitcnt(4000+cnt)          'wait for the capacitor to get charged

dira[PotLine]~             'make potline an input. line switches H>L

startCnt:=cnt              'read the counter at start of cycle and store

repeat                     'go into an endless loop

while ina[PotLine]~~       'keep doing it as long as the potline is high

EndCount := cnt            'read the counter at end of cycle and store

delay := ((EndCount-StartCnt)-1184)   'calculate time for line to go H>L

if delay>610_000           'max permitted delay

delay:=610_000           'clamp delay

PotValue:=(delay/2000)     'This reduces the value to 0-255 or 1 byte

valutotal:=valutotal+potvalue    'figures total

potvalue:=valutotal/repval 'figure average

potvalue <#=255

potvalue #>=0

result:=PotValue      'figure average

PUB GetPotVal2

dira[PotLine2]~~                'set potline as output

valutotal2:=0                   'clear total

repeat  repval2               'repeat

dira[PotLine2]~~            'set potline as output

outa[PotLine2]~~            'make it high so we can charge the capacitor

waitcnt(4000+cnt)           'wait for the capacitor to get charged

dira[PotLine2]~             'make potline an input. line switches H>L

startCnt2:=cnt              'read the counter at start of cycle and store

repeat                      'go into an endless loop

while ina[PotLine2]~~       'keep doing it as long as the potline is high

EndCount2 := cnt            'read the counter at end of cycle and store

delay2:= ((EndCount2-StartCnt2)-1184)   'calculate time for line to go H>L

if delay2>610_000             'max permitted delay

delay2:=610_000             'clamp delay

PotValue2:=(delay2/2300)      'This reduces the value to 0-255 or 1 byte

valutotal2:=valutotal2+potvalue2    'figures total

potvalue2:=valutotal2/repval2 'figure average

potvalue2 <#=255              'clamp at 255

potvalue2 #>=0                'clamp at 0

result:=Potvalue2             'use average

PUB Read3202_0

DIRA[chipSel]~~     'osc once to set up 3202

DIRA[chipDin]~~     'data set up to the chip

DIRA[chipDout]~     'data from the chip to the Propeller

DIRA[chipClk]~~     'oscillates to read in data

DataRed:=0             'Clear out old data

outa[chipSel]~~         'Chip select has to be high to start off

outa[chipSel]~          'Go low to start process

outa[chipClk]~          'Clock needs to be low to load data

outa[chipDin]~~         'must start with Din low to set up 3202

outa[chipClk]~~         'Clock high to read data in

outa[chipClk]~          'Low to load

outa[chipDin]~~         'High single mode

outa[chipClk]~~         'High to read

outa[chipClk]~          'Low to load

outa[chipDin]~          'low channel 0

outa[chipClk]~~         'High to read

outa[chipClk]~          'Low to load

outa[chipDin]~~         'msbf high = MSB first

outa[chipClk]~~         'High to read

outa[chipDin]~          'making line low for rest of cycle

outa[chipClk]~          'Low to load Read the null bit, not stored

outa[chipClk]~~         'High to read

repeat BitsRead          'Reads the data into DataRed in 12 steps

DataRed <<= 1         'Move data by shifting left 1 bit. Ready for next bit

outa[chipClk]~         'Low to load

DataRed:=DataRed+ina[chipDout]  'Xfer the data from pin chipDout

outa[chipClk]~~        'High to read

outa[chipSel]~~          'Put chip to sleep, for low power

PotReading1:=DataRed     'Finished data read for display

result:=dataRed

PUB Read3202_1

DIRA[chipSel]~~     'osc once to set up 3202

DIRA[chipDin]~~     'data set up to the chip

DIRA[chipDout]~     'data from the chip to the Propeller

DIRA[chipClk]~~     'oscillates to read in data

DataRed:=0              'Clear out old data

outa[chipSel]~~         'Chip select has to be high to start off

outa[chipSel]~          'Go low to start process

outa[chipClk]~          'Clock needs to be low to load data

outa[chipDin]~~         'must start with Din low to set up 3202

outa[chipClk]~~         'Clock high to read data in

outa[chipClk]~          'Low to load

outa[chipDin]~~         'High single mode

outa[chipClk]~~         'High to read

outa[chipClk]~          'Low to load

outa[chipDin]~~         'high channel 1

outa[chipClk]~~         'High to read

outa[chipClk]~          'Low to load

outa[chipDin]~~         'msbf high = MSB first

outa[chipClk]~~         'High to read

outa[chipDin]~          'making line low for rest of cycle

outa[chipClk]~          'Low to load Read the null bit, not stored

outa[chipClk]~~         'High to read

repeat BitsRead2         'Reads the data into DataRed in 12 steps

DataRed <<= 1          'Move data by shifting left 1 bit. Ready for next bit

outa[chipClk]~         'Low to load

DataRed:=DataRed+ina[chipDout]  'Xfer the data from pin chipDout

outa[chipClk]~~        'High to read

outa[chipSel]~~          'Put chip to sleep, for low power

PotReading2:=DataRed     'Finished data read for display

result:=dataRed

PUB Read3202_2

DIRA[chipSel2]~~     'osc once to set up 3202

DIRA[chipDin2]~~     'data set up to the chip

DIRA[chipDout2]~     'data from the chip to the Propeller

DIRA[chipClk2]~~     'oscillates to read in data

DataRed:=0              'Clear out old data

outa[chipSel2]~~         'Chip select has to be high to start off

outa[chipSel2]~          'Go low to start process

outa[chipClk2]~          'Clock needs to be low to load data

outa[chipDin2]~~         'must start with Din low to set up 3202

outa[chipClk2]~~         'Clock high to read data in

outa[chipClk2]~          'Low to load

outa[chipDin2]~~         'High single mode

outa[chipClk2]~~         'High to read

outa[chipClk2]~          'Low to load

outa[chipDin2]~~         'high channel 0

outa[chipClk2]~~         'High to read

outa[chipClk2]~          'Low to load

outa[chipDin2]~~         'msbf high = MSB first

outa[chipClk2]~~         'High to read

outa[chipDin2]~          'making line low for rest of cycle

outa[chipClk2]~          'Low to load Read the null bit, not stored

outa[chipClk2]~~         'High to read

repeat BitsRead3         'Reads the data into DataRed in 12 steps

DataRed <<= 1          'Move data by shifting left 1 bit. Ready for next bit

outa[chipClk2]~         'Low to load

DataRed:=DataRed+ina[chipDout2]  'Xfer the data from pin chipDout

outa[chipClk2]~~        'High to read

outa[chipSel2]~~          'Put chip to sleep, for low power

PotReading3:=DataRed     'Finished data read for display

result:=dataRed

PUB Read3202_3

DIRA[chipSel2]~~     'osc once to set up 3202

DIRA[chipDin2]~~     'data set up to the chip

DIRA[chipDout2]~     'data from the chip to the Propeller

DIRA[chipClk2]~~     'oscillates to read in data

DataRed:=0              'Clear out old data

outa[chipSel2]~~         'Chip select has to be high to start off

outa[chipSel2]~          'Go low to start process

outa[chipClk2]~          'Clock needs to be low to load data

outa[chipDin2]~~         'must start with Din low to set up 3202

outa[chipClk2]~~         'Clock high to read data in

outa[chipClk2]~          'Low to load

outa[chipDin2]~~         'High single mode

outa[chipClk2]~~         'High to read

outa[chipClk2]~          'Low to load

outa[chipDin2]~         'low channel 1

outa[chipClk2]~~         'High to read

outa[chipClk2]~          'Low to load

outa[chipDin2]~~         'msbf high = MSB first

outa[chipClk2]~~         'High to read

outa[chipDin2]~          'making line low for rest of cycle

outa[chipClk2]~          'Low to load Read the null bit, not stored

outa[chipClk2]~~         'High to read

repeat BitsRead4         'Reads the data into DataRed in 12 steps

DataRed <<= 1          'Move data by shifting left 1 bit. Ready for next bit

outa[chipClk2]~         'Low to load

DataRed:=DataRed+ina[chipDout2]  'Xfer the data from pin chipDout

outa[chipClk2]~~        'High to read

outa[chipSel2]~~          'Put chip to sleep, for low power

PotReading4:=DataRed     'Finished data read for display

result:=dataRed