' {$STAMP BS2}

' {$PBASIC 2.5}

' Program Name: Humidity Data Acquisition and Robot Movement Program

' Original Program Written By: The Parallax INC. Forum (forums.parallax.com)

' Revision Date: 02/21/2008

' Last Revision Made By: Mark Kibler (as suggested by Phil Kenney and Tracy Allen)

' To remove syntax errors

' File name "Rocket_Robot_Program_February_21.bs2

DEBUG CLS, CR

DEBUG "John Stark Regional High School, NH", CR, CR

DEBUG "NASA Student Launch Initiative Rocketry Team", CR, CR

DEBUG "Humidity Data Acquisition and Robot Movement Program", CR, CR

DEBUG      "______________________________________________________", CR, CR, CR

main2:

'--- Data ---

motormovementtime             VAR   Word

motormovementtime = 100

ShtData         PIN     1                       ' bi-directional data

Clock           PIN     0                       ' clock (for Sensirion)

TX              PIN     8               ' Transmit Data   --> 27937.4 (RXD)

RTS             PIN     9               ' Request To Send --> 27937.6 (CTS)

RX              PIN     10              ' Receive Data    <-- 27937.5 (TXD)

CTS             PIN     11              ' Clear To Send   <-- 27937.2 (RTS)

' -----[ Constants ]-------------------------------------------------------

Baud            CON     84              ' Serial Baud Rate 9600 bps (BS2)

NumSamples      CON     15*60                   ' Number Of Samples To Log (15 minutes)

ShtTemp         CON     %00011                  ' read temperature

ShtHumi         CON     %00101                  ' read humidity

ShtStatW        CON     %00110                  ' status register write

ShtStatR        CON     %00111                  ' status register read

ShtReset        CON     %11110                  ' soft reset (wait 11 ms after)

Ack             CON     0

NoAck           CON     1

No              CON     0

Yes             CON     1

DegSym          CON     186             ' degrees symbol for DEBUG

buffer          VAR     B0              ' Input Buffer (B0 - B15)

index           VAR     B18             ' Index Variable

ioByte1         VAR     B19             ' Input/Output Storage

counter         VAR     W8              ' Counter Variable

flag            VAR     B20.BIT0        ' Event Status Flag

ioByte2         VAR     B13             ' data from/to SHT1x

ackBit          VAR     B15.BIT0        ' ack/nak from/to SHT1x

toDelay         VAR     B14             ' timeout delay timer

timeOut         VAR     B15.BIT1        ' timeout status

soT             VAR     W0              ' temp counts from SHT1x

tC              VAR     W1              ' temp - celcius

tF              VAR     W2              ' temp - fahrenheit

soRH            VAR     W3              ' humidity counts from SHT1x

rhLin           VAR     W4              ' humidity; linearized

rhTrue          VAR     W5              ' humidity; temp compensated

status          VAR     B12             ' SHT1x status byte

'

'

' -----[ Initialization ]--------------------------------------------------

'

'

PAUSE 500                               ' 500 allows 1/2 second TO settle

HIGH TX                               ' Initialize Transmit Line

LOW RTS                               ' Take Vinculum Out Of Reset

PAUSE 500                               ' Allow 1/2 Second To Settle

DEBUG "1) Synchronize Circuitry -->"

GOSUB SHT_Connection_Reset              ' reset device connection

SEROUT TX\CTS, Baud, ["E", CR]        ' Sync Command Character

GOSUB Get_Data                        ' Get Response

PAUSE 1

DO

SEROUT TX\CTS, Baud, ["e", CR]        ' Sync Command Character

GOSUB Get_Data                        ' Get Response

PAUSE 1                               ' Quick Pause

LOOP UNTIL ioByte1 = $0D                ' Wait For Carriage Return

' -----[ Program Code ]----------------------------------------------------

Main1:

DEBUG "     *SYNCHRONIZED*", CR, CR

DEBUG "2) Start Short Command Mode -->"

SEROUT TX\CTS, Baud, ["SCS", CR]

GOSUB Get_Data

DEBUG "  *CONFIRMED*", CR, CR

DEBUG "3) DataLogger Initialization --> "

Check_Drive:

DO

SEROUT TX\CTS, Baud, [CR]

GOSUB Get_Data

IF buffer(0) = ">" THEN

EXIT

ELSEIF buffer(0) = "N" AND buffer(1) = "D" THEN

DEBUG "."

ELSEIF buffer(0) = "D" AND buffer(1) = "D" AND flag = 0 THEN

DEBUG "Connected!", CR, "Accessing..."

flag = 1

ELSE

DEBUG ". Initialization pause . "

PAUSE 5000        ' Mark added this PAUSE on February 21, 2008

GOSUB Get_Data       ' The pause seems to give the Datalogger and

ENDIF               ' flash drive time to initialize.

PAUSE 1

LOOP

DEBUG " *INITIALIZED*", CR, CR

DEBUG "4) Open Data Storage File -->"

' -------------------------------------------------------------------------

GOSUB Get_Data

SEROUT TX\CTS, Baud, [$09, $20, "datafile.txt", CR]

GOSUB Get_Data

' ----------------------------------------------------

DEBUG "    *FILE OPEN*", CR, CR, CR

DEBUG "Writing temperature (C) and humidity (%) data...", CR, CR, CR

FOR counter = 1 TO 3

GOSUB SHT_Measure_Temp

GOSUB SHT_Measure_Humidity

DEBUG "#",DEC counter," ",REP "-"\tC.BIT15,DEC ABS tC/10,".",DEC1 ABS tC,", ",DEC rHLin/10,".",DEC1 rHLin,CR,LF

SEROUT TX\CTS, Baud, [ $8,$20,0,0,0,14,CR,tC.BIT15*13+32,DEC3 ABS (tC/10),".", DEC1 ABS tC,",",DEC3 (rhLin/10),".",DEC1 rhLin,CR,LF,CR]

PAUSE 1                             ' Delay in Writing Data 1000 = 1 second, 500 = 1/2 second, etc.

GOSUB Get_Data                      ' Purge Receive Buffer

NEXT

DEBUG CR, "5) Closing File..."

DEBUG " *DATA SAVED TO FLASH DRIVE*", CR, CR, CR

DEBUG " *START ROBOT and DATA ACQUISITION sequence*", CR, CR

SEROUT TX\CTS, Baud, [$0A, $20, "datafile.txt", CR]

GOSUB Get_Data

GOSUB MAIN                            ' Loops back to the start of the main: ground movement sequence

' -----[ Subroutines ]-----------------------------------------------------

Get_Data:

index = 0                             ' Reset Index Pointer

DO                                    ' Receive Data

SERIN RX\RTS, Baud, 100, TimeoutExit, [ioByte1]

buffer(index) = ioByte1             ' Add Received Byte To Buffer

index = index + 1                   ' Increment Index Pointer

IF index > 14 THEN TimeoutExit      ' Check For Overflow

LOOP

TimeoutExit:

RETURN

'

' connection reset: 9 clock cyles with ShtData high, then start sequence

SHT_Connection_Reset:

SHIFTOUT ShtData, Clock, LSBFIRST, [$FFF\9]

'

' generates SHT1x "start" sequence

'          _____         _____

' ShtData       |_______|

'              ___     ___

' Clock    ___|   |___|   |___

SHT_Start:

INPUT ShtData                                 ' let pull-up take line high

LOW Clock

HIGH Clock

LOW ShtData

LOW Clock

HIGH Clock

INPUT ShtData

LOW Clock

RETURN

'

' measure temperature:

' -- celcius = soT * 0.01 - 40

' -- fahrenheit = soT * 0.018 - 40

SHT_Measure_Temp:

GOSUB SHT_Start                               ' alert device

ioByte2 = ShtTemp                             ' temperature command

GOSUB SHT_Write_Byte                          ' send command

GOSUB SHT_Wait                                ' wait until measurement done

ackBit = Ack                                  ' another read follows

GOSUB SHT_Read_Byte                           ' get MSB

soT.HIGHBYTE = ioByte2

ackBit = NoAck                                ' last read

GOSUB SHT_Read_Byte                           ' get LSB

soT.LOWBYTE = ioByte2

'

' Note: Conversion factors are multiplied by 10 to return the

' temperature values are in tenths of degrees

tC = soT / 10 - 400                           ' convert to tenths C

RETURN

' measure humidity

'

SHT_Measure_Humidity:

GOSUB SHT_Start                               ' alert device

ioByte2 = ShtHumi                             ' humidity command

GOSUB SHT_Write_Byte                          ' send command

GOSUB SHT_Wait                                ' wait until measurement done

ackBit = Ack                                  ' another read follows

GOSUB SHT_Read_Byte                           ' get MSB

soRH.HIGHBYTE = ioByte2

ackBit = NoAck                                ' last read

GOSUB SHT_Read_Byte                           ' get LSB

soRH.LOWBYTE = ioByte2

'

rhLin = (soRH ** 26542)

rhLin = rhLin - ((soRH ** 3468) * (soRH ** 3468) + 50 / 100)

rhLin = rhLin - 40

rhTrue = ((tC / 10 - 25) * (soRH ** 524 + 1) + (rhLin * 10)) + 5 / 10

RETURN

' sends "status"

'

SHT_Write_Status:

GOSUB SHT_Start                               ' alert device

ioByte2 = ShtStatW                            ' write to status reg command

GOSUB SHT_Write_Byte                          ' send command

ioByte2 = status

GOSUB SHT_Write_Byte

RETURN

' returns "status"

'

SHT_Read_Status:

GOSUB SHT_Start                               ' alert device

ioByte2 = ShtStatW                            ' write to status reg command

GOSUB SHT_Read_Byte                           ' send command

ackBit = NoAck                                ' only one byte to read

GOSUB SHT_Read_Byte

RETURN

'

' sends "ioByte"

' returns "ackBit"

SHT_Write_Byte:

SHIFTOUT ShtData, Clock, MSBFIRST, [ioByte2]  ' send byte

SHIFTIN  ShtData, Clock, LSBPRE, [ackBit\1]   ' get ack bit

RETURN

'

' returns "ioByte"

' sends "ackBit"

SHT_Read_Byte:

SHIFTIN  ShtData, Clock, MSBPRE, [ioByte2]    ' get byte

SHIFTOUT ShtData, Clock, LSBFIRST, [ackBit\1] ' send ack bit

INPUT ShtData                                 ' release data line

RETURN

'

' wait for device to finish measurement (pulls data line low)

' timeout after ~1/4 second

SHT_Wait:

INPUT ShtData                                 ' data line is input

FOR toDelay = 1 TO 100                        ' give ~1 second to finish

timeOut = INS.LOWBIT(ShtData)               ' scan data line

IF (timeOut = No) THEN SHT_Wait_Done        ' if low, we're done

PAUSE 1

NEXT

SHT_Wait_Done:

RETURN

'

' reset SHT1x with soft reset

SHT_Soft_Reset:

GOSUB SHT_Connection_Reset                    ' reset the connection

ioByte2 = ShtReset                            ' reset command

ackBit = NoAck                                ' only one byte to send

GOSUB SHT_Write_Byte                          ' send it

PAUSE 11                                      ' wait at least 11 ms

RETURN

main:

DEBUG CR, CR

PAUSE 1000

GOSUB forward

GOSUB backward

GOSUB turnclockwise

GOSUB forward2

GOSUB backward2

GOSUB turnCOUNTERclockwise2:

GOTO main

forward:

FOR motormovementtime = 0 TO 600

PULSOUT 15, 850                           ' move forward 1

PULSOUT 13, 650

PAUSE 20

NEXT

PAUSE 1000

backward:                                    ' move backward 1/3

FOR motormovementtime = 0 TO 120

PULSOUT 15, 650

PULSOUT 13, 850

PAUSE 20

NEXT

PAUSE 1000

turnclockwise:                               ' rotate clockwise

FOR motormovementtime = 0 TO 120

PULSOUT 15, 850

PULSOUT 13, 850

PAUSE 20

NEXT

PAUSE 1000

forward2:

FOR motormovementtime = 0 TO 600

PULSOUT 15, 850                           ' move forward 1

PULSOUT 13, 650

PAUSE 20

NEXT

PAUSE 1000

backward2:                                    ' move backward 1/3

FOR motormovementtime = 0 TO 120

PULSOUT 15, 650

PULSOUT 13, 850

PAUSE 20

NEXT

PAUSE 1000

turnCOUNTERclockwise2:                               ' rotate clockwise

FOR motormovementtime = 0 TO 120

PULSOUT 13, 650

PULSOUT 15, 650

PAUSE 20

NEXT

GOSUB main2: