## Slide 1: Return To The Moon
Beacon Navigation Feasibility Study
Luis Bill
Joshua Eliser
Jason Frisk
Amitha Mathew

## Slide 2: Outline
Background
Project Objectives
Lunar Environment
Navigation Beacons
Rover Design Concept
Conclusions

## Slide 3: Background
10 Week Project to:
  Establish Feasibility of a Beacon-Based Navigation System for an Autonomous Lunar Rover
  Demonstrate Beacon Navigation with an Outdoor, Mobile Robot

## Slide 4: Project Objectives
Beacon Feasibility
  Localization
  Coverage
  Practicality
Rover Navigation Feasibility
  Test Rover Mobility Using Remote Control
  Way Point Navigation with Beacon Derived Position
  plus Around Mapped Hazards
  plus Around Unknown Obstacles
  plus Dead Reckon Upon Beacon Failure

## Slide 5: Lunar Environment
Lunar Terrain Is Highly Variable
  Avoid or Navigate Around Known High Hazard Areas
  Develop High Mobility, Robust Rover
Negligible Atmosphere (trillionth of Earth’s)
  Rover and Beacons Need Protection from Micrometeorite Strikes
  Sonar Sensors Impractical
Lunar Magnetism Is Negligible
  Compasses can not be used
Solar Wind and Flares
  Electronics need to be shielded form high energy particles
Lunar Temperature Varies From
  Limit rover time of operation

## Slide 6: Navigation Beacons
Types
Trilateration – determine position based on distances from known beacons (e.g. GPS)
Triangulation – determine position based on angles to known beacons
  Omnidirectional: requires more power
  Rotating Transmitter-Receiver, Stationary Reflectors: usually Laser with retroreflectors
  Rotating Transmitter, Stationary Receivers: usually Laser with transponder receivers
Requirements
Omnidirectionality
High Visibility: easy to see against background
No Moving Parts: high maintainability

## Slide 7: Beacon Coverage
Lunar Beacon Coverage:
  How much area can a beacon cover on the moon?
  Horizon Distance Proportional to Square Root of Beacon Height
  Approximate Beacon Coverage: 11*height(m), km^2
  Beacon Placement
    High on a hill would be best.
  Minimum of 3 beacons for triangulation or trilateration.
  Placement of Beacons:
    Area of exploration desired
    Type of beacons
    Physical terrain affects number and placement of beacons

## Slide 8: Radio Beacons
Low noise background
Not affected by sunlit terrain
No moving parts
Omnidirectional
Proven technique, e.g. LORAN
Provide rover localization by trilateration

## Slide 9: Rover Design Concept
Robust, Outdoor Four Wheel Drive Rover
Accelerometer for Slope Measurement
Wheel Encoders and Gyroscope for Dead Reckoning
Radio Beacon Localization
Video Camera for Remote Visualization
LADAR for Obstacle Avoidance
Parallax
QuadRover

## Slide 10: Conclusions
All Terrain, Mobile Rover Practicality Proved on Moon and Mars
Radio Beacon-Based Navigation Is Practical on the Moon
Obstacle Detection/Avoidance Demonstrated in DARPA Competitions
Autonomous, Semi-Autonomous Rover Operation Is Possible with Terrain Maps

## Slide 11: Project Management Due Dates
YouTube Video
Parallax Forum
Continuous
Publicity
Power Point Presentation
Word Document
Project Workbook
29 JUL 2008
Final Presentation
Robotic Requirements Demo
29 JUL 2008
Prototype Demonstration
Power Point Presentation
1 JUL 2008
Design Presentation
Power Point Presentation
Word Document
19 JUN 2008
Feasibility Report
Deliverables
Due Date
Task