## Slide 1: Return To The Moon
Design Review
July 1, 2008
Luis Bill
Joshua Eliser
Jason Frisk
Amitha Mathew

## Slide 2: Outline
Background
Objectives
Design Approach
Functional Parts
Plan of Action
Budget
Schedule

## Slide 3: Background
Objective is autonomous lunar navigation
Feasibility Study suggests:
  Radio beacons for localization
  Laser system for obstacle avoidance
  All wheel drive buggy for mobility
JPL papers propose Fuzzy Control software architecture1-4
This project follows from these precepts

## Slide 4: Objectives
Navigate using a remote control system
  Test platform mobility
Beacon waypoint navigation
Beacon navigation with mapped hazards
Beacon navigation with mapped hazards and unknown obstacles
Dead reckoning to safe positions

## Slide 5: Design Approach
Remote control
  Parallax RC code and hardware
  Mobility testing
  Emergency cut-off function
Beacon navigation for rover localization
  Ultra Wideband radio system
Obstacle Detection / Avoidance
  SICK LADAR
Dead Reckoning
  Wheel Encoders (travel)
  Accelerometer (slope)
  Gyroscope (turning)

## Slide 6: Functional Parts Outline
System Components:
  Parallax QuadRover
  Parallax Propeller Microcontroller
  Time Domain UWB Radio
  SICK LADAR
  Encoders
  Accelerometer
  Additional Power Supply
  RC controls
Parallax QuadRover

## Slide 7: System Configuration

## Slide 8: Parallax QuadRover
QuadRover Features
  4WD chassis
    Skid-steer drive train
  Honda engine
    Gas powered, 4-stroke
    2.5 horse power
    0.8 gal fuel tank
    Hydraulic drive
  Implementation and uses
    Developed for research
    Mobility platform
    RC control capability
    Hobbies and entertainment

## Slide 9: Parallax QuadRover
Hydraulic Drive System
  Hydraulic pump
  Drives 2 independent motors
    Flow-cutoff valves
    Flow-reverse valves
Electrical System/Devices
  Emergency cutoff switch
  Onboard 12V battery
  Multi-core Microcontroller
  Servos
    Throttle
    Right brake
    Left brake
  Emergency cut-off switch
QuadRover Hydraulic System
QuadRover Electrical System

## Slide 10: Parallax Propeller Microcontroller
Microcontroller Features
  3.3V input voltage
  8 processors (cogs)
  32 bit architecture
  Clock speed up to 80 MHz
  32 general purpose I/O pins
  32KB RAM / 32KB ROM
  40mA per I/O pin max, 25mA recommended, 300mA chip
  Supports Assembly and Spin programming languages
Parallax Propeller Pinout

## Slide 11: Propeller Block Diagram

## Slide 12: Remote Control
RC Transmitter
  Specs:
    7 Channel
    Supply voltage: 9.6V
    Current drain: 170mA
    Frequency: 2.4GHz
  Controls brakes, throttle and hydraulic solenoids
RC Receiver
  Specs:
    Supply voltage: 5V
    Current drain: 80mA
    7 Channel
  Controls 3 servos:
    Left brake, Right brake, Throttle
  Programmable signal loss operation:
    Maintains position
    Default position

## Slide 13: Remote Control Objectives
RC Software
  Processes signals from RC receiver
  Controls Left/Right brake and Throttle
  Controls solenoid valves
Testing:
  How fast can the robot travel ?
  What terrain can the robot traverse ?
  How should the robot traverse a type of terrain ?
  How easily can it do a zero turn radius maneuver
  What is the range of the transmitter ?
Safety:
  RC controller can act as a kill switch

## Slide 14: Radio Beacons
Why radio?
  Relatively low power consumption
  Great area of coverage
  Omni-directional
  Better for mobile robotic use
    No moving parts
    Proven technology
    Moon is radio quiet
Trilateration Position Determination

## Slide 15: Ultra Wideband Radio
Time Domain PulsON 210 UWB Radios
  Operating frequency: 4.7 GHz
  Power: 7.5V, ~1A, 6.5 W
  Size: 4” x 6” x 2”
  Range of operation:
    Configurable
    Max 1-2 km
  UDP ethernet interface
Configuration:
  Range: 100 meters - Position accuracy: ~1 foot
  Four field radios - Update rate: ~8 Hz
  One rover radio
Radio Beacon

## Slide 16: Obstacle Avoidance
Purpose :
  Detect unknown obstacles
  Where is the object?
  How far away is the object?
  Rate of change of distance to object
  What is the object’s extent?

## Slide 17: SICK LADAR
Supply voltage: 24V
Max power: 30W
Operating temp: 0ºC to +50ºC
Serial comm: 9600 - 56k baud
Scan angle: 180º
Angular resolution: 0.5º
Resolution: 70mm out to 50m range
One scan every 80ms (12.5 Hz)
Laser Ranger

## Slide 18: Wheel Encoders
Slotted Switch Position Encoder
  Consist of emitting diode and NPN photo-transistor
  11 mm lead centers
  Non-contact switching
Input Diode
  Forward Current: 10mA
  Reverse Voltage: 3.0 V
Output Phototransistor
  Collector Current: 100uA
  Emitter-Collector Voltage: 0.4V
  Collector-Emitter Voltage: 5V
Photo-Interrupter
Slotted Switch

## Slide 19: Additional Power Supply
Features of LM2576 series (DC-DC Converter)
  7V – 40V input voltage
  LM2576T-12, -5, adj
    24V input; 12V output
    12V input; 5V and 3.3V outputs
  Guaranteed 3A output current
  Requires only 4 external components
  High efficiency
Advantages
  No heat sink required
  Simplifies the design
  Uses readily available standard inductors

## Slide 20: Power Supply Schematic

## Slide 21: Laptop Computer
A laptop will be used if the Propeller microcontroller is not powerful enough to handle our navigation and interface needs
Laptop Features:
  Allows for faster computation
  Easier to interface with the radios and LADAR
  Can be programmed in C or C++
  Data logging is much easier

## Slide 22: Microcontroller Interfaces

## Slide 23: Plan Of Action / Project Recap
Remote Control of Robot.
  Interface to RC system
  Test the robots locomotion limits
Interface robot to the radio beacon system
  Interface to Ultra Wideband radio system to get position data.
Waypoint navigation with no obstacles.
  Write software to determine how to make the robot move from waypoint A to waypoint B.
  No obstacles will be in the way
Waypoint navigation with known obstacles.
  Software will implement Fuzzy controls to compute how to traveling to a waypoint and avoid an obstacle.
Waypoint navigation with unknown obstacles.
  Interface to LADAR sensor to detect any unknown obstacles and avoid accordingly.

## Slide 24: Budgets
* - This is the price for one radio on the robot. The system uses 4 more for positioning.
Battery Totals: 7 Amp-Hours
- Worse case: 30 min (running laptop off battery)
- Nominal case: 3 hrs
Devices
Voltage
Current
Power
Cost
Quad Rover
--
--
--
$ 5,500
Propeller Board
3.3V
40mA
0.132W
--
Sick LADAR
24V
1.25A
30W
$3,250
Time Domain
7.5V
0.866A
6.5W
$3,000*
Laptop
19.5V
4.62A
90W
$650
Accelerometer
5V
5mA
0.025W
40
Total
6.781A
126.66W
$ 12,340

## Slide 25: Schedule
Task
Due Date
Deliverables
Feasibility Report
19 JUN
Power Point Presentation
Word Document
Design Presentation
01 JUL
Power Point Presentation
Prototype Demonstration
TBA
Robotic Requirements
Power Point Presentation
Final Presentation
29 JUL
Word Document
Project Workbook
Publicity
Continuous
YouTube Video
Parallax Forums

## Slide 26: Navigation Paper References
H. Seraji: “Traversability Index: A New Concept for Planetary Rovers”, Proceedings IEEE International Conference on Robotics & Automation”, pp. 2006 – 2013, 1999.
A. Howard, H. Seraji, E. Tunsel: “A Rule-Based Traversability Index for Mobile Robot Navigation”, Proceedings IEEE International Conference on Robotics & Automation”, pp. 3067 – 3071, 2001.
H. Seraji, A. Howard, E. Tunstel: “Safe Naviagation on Hazardous Terrain”, Proceedings IEEE International Conference on Robotics & Automation”, pp. 3084 – 3091, 2001.
H. Seraji: “Terrain-Based Robot Navigation Using Multi-Scale Traversability Indices”, 10th IEEE Interational Conference on Fuzzy Systems, pp. 1309 – 1314, 2001.