| Pin Number | Propeller Proto Board – 5Mhz | Propeller Demo Board – 5Mhz | Hydra Gamer Board – 10Mhz | PropRPM Board – 5Mhz |
| --- | --- | --- | --- | --- |
| P0 | available | available | LED for Debug | available |
| P1 | available | available | HYDRA Net | available |
| P2 | available | available | HYDRA Net | available |
| P3 | available | available | NES cntllr - CLK | available |
| P4 | available | available | NES cntllr – SH/LD | available |
| P5 | available | available | NES cntllr – A OUT | available |
| P6 | available | available | NES cntllr – B OUT | available |
| P7 | available | available | AUDIO Mono | available |
| P8 | available | MIKE | MOUSE A | available |
| P9 | available | MIKE | MOUSE A | available |
| P10 | available | AUDIO stereo | MOUSE B | available |
| P11 | available | AUDIO stereo | MOUSE B | available |
| P12 | available | NTSC/PAL video | KEYBOARD A | NTSC/PAL video |
| P13 | available | NTSC/PAL video | KEYBOARD A | NTSC/PAL video |
| P14 | available | NTSC/PAL video | KEYBOARD B | NTSC/PAL video |
| P15 | available | NTSC/PAL video | KEYBOARD B | NTSC/PAL video |
| P16 | VGA video | VGA video | VGA video / Card I/O | LED 0 |
| P17 | VGA video | VGA video | VGA video / Card I/O | LED 1 |
| P18 | VGA video | VGA video | VGA video / Card I/O | LED 2 |
| P19 | VGA video | VGA video | VGA video / Card I/O | LED 3 |
| P20 | VGA video | VGA video | VGA video / Card I/O | LED 4 |
| P21 | VGA video | VGA video | VGA video / Card I/O | LED 5 |
| P22 | VGA video | VGA video | VGA video / Card I/O | LED 6 |
| P23 | VGA video | VGA video | VGA video / Card I/O | LED 7 |
| P24 | MOUSE | MOUSE | NTSC/PAL video | LED 8 |
| P25 | MOUSE | MOUSE | NTSC/PAL video | LED 9 |
| P26 | KEYBOARD | KEYBOARD | NTSC/PAL video | available |
| P27 | KEYBOARD | KEYBOARD | NTSC/PAL video | available |
| P28 [system] | EEPROM clock | EEPROM clock | EEPROM clock | EEPROM clock |
| P29 [system] | EEPROM data | EEPROM data | EEPROM data | EEPROM data |
| P30 [system] | Primary Serial I/O Rx# | Primary Serial I/O Rx | Primary Serial I/O Rx | Primary Serial I/O Rx* |
| P31 [system] | Primary Serial I/O Tx# | Primary Serial I/O Tx | Primary Serial I/O Tx | Primary Serial I/O Tx* |

General Note: Comparison with the Spin Stamp NOT provided.  Power supplies vary in configuration.

Note #: Propeller Proto Board requires additional serial interface for SPIN programing. Access to all I/O pins, P0-P31.

Note *: PropRPM has an on-board RS-232 level shifter for programming and communications. Access to I/O pins P0-P27 and uses the 40pin DIP Propeller which can be easily replaced.