## Slide 1: Return To The Moon
Final Presentation
August 4, 2008
Luis Bill
Joshua Eliser
Jason Frisk
Amitha Mathew
Mentors
Dr. Yuri Shtessel
Dr. John Piccirillo

## Slide 2: Outline
Background
Objectives
Design Approach
Functional Parts
Propeller Microcontroller Interface
Final Plan of Action
Results
Questions

## Slide 3: Background
Objective is autonomous lunar navigation.
Feasibility Study suggests:
  Radio beacons for localization
  Laser system for obstacle avoidance
  All wheel drive rover for mobility
JPL papers propose Fuzzy Control software architecture.

## Slide 4: Objectives
Navigate using a remote control system.
  Test platform mobility, durability, and features.
Beacon waypoint navigation to different goal points in a virtual map.
Beacon navigation with known obstacles.
Beacon navigation with unknown obstacles.
Ability to dead reckon position.

## Slide 5: Design Approach
Remote Control
  Parallax R/C code and hardware
  Mobility testing
  Emergency cut-off function
Beacon navigation for rover localization
  Ultra Wideband radio system
Obstacle Detection/Avoidance
  SICK LADAR

## Slide 6: Functional Parts Outline
System Components:
  Parallax QuadRover
  Parallax Propeller Microcontroller
  Time Domain UWB Radio
  SICK LADAR
  Panic Button
  Battery Box
  Additional Power Supply
  RC System
  Software implementation
Parallax QuadRover
with additional equipment

## Slide 7: Functional Parts
Robot’s front view
Robot’s back view
Panic Button
PropNIC
Mobile Beacon
LADAR
Power Supply Board
Power Supply Box
Battery Box
Serial board

## Slide 8: Parallax QuadRover
QuadRover Features
  4WD chassis
    Skid-steer drive train
  Honda engine
    Gas powered, 4-stroke
      Power and energy
      density
      Durability
    2.5 horse power
    0.8 gal fuel tank
    Hydraulic drive

## Slide 9: QuadRover Drive & Electrical
Hydraulic Drive System
  Hydraulic pump
  Drives 2 independent motors
    Flow-cutoff valves
    Flow-reverse valves
Electrical System/Devices
  Emergency cutoff switch and panic button
  Three onboard 12V batteries
  Multi-core microcontroller
  Servos
    Throttle
    Right brake
    Left brake
  Power supply box
QuadRover Electrical System
QuadRover Hydraulic System

## Slide 10: Parallax Propeller
Microcontroller Features
  3.3V input voltage
  8 processors (cogs)
  32 bit architecture
  Clock speed up to 80 MHz
  32 general purpose I/O pins
  32KB RAM / 32KB ROM
  40mA per I/O pin max, 25mA recommended, 300mA chip
  Supports Assembly and Spin programming languages
Parallax Propeller Pinout

## Slide 11: Parallax Propeller Block Diagram

## Slide 12: Remote Control
RC Transmitter
  Specs:
    7 Channel
    Supply voltage: 9.6V
    Current drain: 170mA
    Frequency: 2.4GHz
  Controls brakes, throttle and hydraulic solenoids
  Kill control capability
RC Receiver
  Specs:
    Supply voltage: 5V
    Current drain: 80mA
    7 Channel
  Controls 3 servos:
    Left brake, right brake, throttle
  Programmable signal loss operation:
    Maintains position
    Default position

## Slide 13: Remote Control Objectives
RC Software
  Processes signals from RC receiver
  Controls left/right brake and throttle
  Controls solenoid valves
Testing:
  How fast should the robot go on the autonomous mode?
  What types of terrains can the robot navigate safely?
  What type of fuzzy logic control is appropriate for the robot’s navigation?
Safety:
  RC controller can function as a kill switch

## Slide 14: Radio Beacons
Why radio?
  Relatively low power consumption
  Great area of coverage
  Omni-directional
  Better for mobile robotic use
    No moving parts
    Proven technology
    Moon is radio quiet
Trilateration Position Determination

## Slide 15: Ultra Wideband Radio
Time Domain PulsON 210 UWB Radios
  Operating Frequency: 4.7 GHz
  Power: 7.5V, ~1A
  Power Consumption: 6.5 W
  Range of Operation:
    Configurable
    Max 1-2 km
  UDP Ethernet interface
Configuration:
  Range: 100 meters - Position accuracy: ~ 1 foot
  Four field radios - Update rate: ~ 8 Hz
  One rover radio
Radio Beacon

## Slide 16: Radio Beacon System
Static radio beacons
  Virtual map is composed
  of four radio beacons.
Mobile radio beacon
  Receives information from
  static beacons.
PropNIC
  ENC28J60
  SPI interface

## Slide 17: Obstacle Avoidance
Purpose :
  Detect unknown obstacles
  Where is the object?
  How far away is the object?
  Determine the rate of change of the distance to the object.
  Find the safest path for the robot to follow.

## Slide 18: SICK LADAR
Supply voltage: 24V
Max power: 30W
Operating temp: 0ºC to +50ºC
Serial com: 9600 - 56k baud
Scan angle: 180º
Angular resolution: 0.5º
2D Vision
Resolution: 70mm out to 50m range
One scan every 80ms (12.5 Hz)

## Slide 19: LADAR-Robot System
Position relative to the floor
  Distance of ~2ft from the floor.
Detects range of the closest object.
  The robot turns left/right or stops depending on the distance from an object.
Serial board interface.

## Slide 20: Battery Box
Battery Box includes
  6-pin Charging Connector
  4-pin Power Connector
  3-SPDT Relay Switch
  Two 12-volt batteries
    24V output
    12V output
  Fuses (8 Amperes)
12 Volt battery
Relay Switch
Fuses
Terminal Strips
6 Pin Charging Connector
4 Pin Power Connector

## Slide 21: Additional Power Supply
Features of LM2576 series (DC-DC Converter)
  7V – 40V input voltage
  LM2576T-12, -5, adj
    24V input; 12V output
    12V input; 5V and 3.3V outputs
  Guaranteed 3A output current
  Requires only 4 external components
  High efficiency
Advantages
  No heat sink required
  Simplifies the design
  Uses readily available standard inductors

## Slide 22: Power Supply Schematic

## Slide 23: Software Implementation
Software Flow Diagram and Cog Representation

## Slide 24: Propeller Interface

## Slide 25: Final Plan of Action
Interface robot to the radio beacon system
  Interface with UWB radio system to get position data.
Waypoint navigation with no obstacles.
  Write software to determine how to make the robot move to multiple waypoints in one virtual map.
  No obstacles in the way
Fuzzy Traversability Control
  JPL proposed algorithm
Waypoint navigation with unknown
obstacles.
  Interface to LADAR sensor to detect any
  unknown obstacles and avoid accordingly.

## Slide 26: Results
Autonomous waypoint navigation
  The robot can reach a determine goal position autonomously.
  The distance to be traveled is known by means of the radio beacons.
Simulated hazard avoidance
  Known/unknown object avoidance
  capability.
Localization of the robot
on the plane
  Position of the robot on the virtual map
  is known relative to the radio beacons.
Beacons implementation
  Beacon system navigation demonstrated to be a feasible intermediate solution while a Lunar Positioning System is under development.

## Slide 27: Future Recommendations
Robotic arm
  Improves robot’s capability
Overhaul certain sections of the robot’s chassis.
  Vibration problems
Implementation of dead reckoning.
  Usage for loss of beacon signal.
Add additional sensors
  Obstacle avoidance
Laptop interface
  Additional computing power
  Easier control of the robot

## Slide 28: References
Propeller QuadRover Robot and Honda Engine Manual: Reference to the different systems and components of the rover.
H. Seraji: “Terrain-Based Robot Navigation Using Multi-Scale Traversability Indices”, 10th IEEE International Conference on Fuzzy Systems, pp. 1309 – 1314, 2001.
H. Seraji: “Traversability Index: A New Concept for Planetary Rovers”, Proceedings IEEE International Conference on Robotics & Automation”, pp. 2006 – 2013, 1999.
A. Howard, H. Seraji, E. Tunsel: “A Rule-Based Traversability Index for Mobile Robot Navigation”, Proceedings IEEE International Conference on Robotics & Automation”, pp. 3067 – 3071, 2001.
H. Seraji, A. Howard, E. Tunstel: “Safe Navigation on Hazardous Terrain”, Proceedings IEEE International Conference on Robotics & Automation”, pp. 3084 – 3091, 2001.

## Slide 29: Questions & Answers