Getting started with Propforth assembler

This is not a PASM tutorial it is a HOW TO write PASM code for Propforth.

PASM code written for the Propforth ASM differs syntactically from code found in
the data section of a spin file. See below an example program Blinker.f , which blinks a LED from cog4 and displays a single letter of the alphabet from cog6 to the console each time the led on pin 16 is turned on.

Notice that the PASM source code at the top of the file is enclosed within curly brackets {}
Propforth uses {} to enclose comments. The source code is included in the file for review only.
The output generated by the asm is pasted to the blinker.f proper following the variables.

Looking at the PASM source code there are some notable differences.

All Forth code is written to a plain text file on a PC and is pasted to the console terminal. The first line always starts with fl. This is a call to the Forth loader.

The next line changes the base to hexadecimal from the default decimal base.

The following definitions occur in the Blinker file.

:asm Denotes start on assemble code (Note :asm is a single word)

c_'label' or v_'label' Denotes a word length constant

a_'lablel' Denotes a global label

__1 to __F Denotes local labels

_treg1 to treg7 Temporary storage registers assigned by the forth kernel

;asm Denotes the end on the asm code

Finally Forth words are delimited by spaces.
Labels should be on a new line and the only text on the line.
See PASM source code.

Just a note on the par register.

On cogreset the par register in the current forth cog points to the pad area. Each cog has its own pad area I have chosen an arbitrary par offset of hex 40 for this example.

{ Propforth ASM source Blinker.f source
        =============================

fl

hex
:asm
v_pin
10
v_delay
02625400
 v_char
61
a_tog
        mov _treg6 , par
        add _treg6 , # 40
        mov _treg2 , # 1
        shl _treg2 ,	v_pin
        mov dira , _treg2
        mov _treg3 , cnt
        add _treg3 , # 80
__1
        mov _treg4 , v_char
        mov _treg5 , # 1a
__2
        waitcnt _treg3 , v_delay
        muxnz outa , _treg2
        waitcnt _treg3 , v_delay
        muxz outa , _treg2
        wrlong _treg4 , _treg6
        add _treg4 , # 1
        djnz _treg5 , # __2
        jmp # __1

;asm

        End of Source Code
        ================

The above text within the {} brackets when pasted to the assembler will result in the following output generated and displayed to the console.

163 wconstant v_adr
152 asmlabel a_tog
151 wconstant v_char
150 wconstant v_delay
14F wconstant v_pin
lockdict variable def_014F 0164 l, 014F l,
00000010 l, 02625400 l, 00000061 l, A0BE1DF0 l, 80FE1C40 l, A0FE1401 l, 2CBE154F l, A0BFED0A l, A0BE17F1 l, 80FE1680 l,
A0BE1951 l, A0FE1A1A l, F8BE1750 l, 7CBFE90A l, F8BE1750 l, 78BFE90A l, 083E190E l, 80FE1801 l, E4FE1B5B l, 5C7C0159 l,
00000002 l,
freedict

The next step is to copy the above output from the console window and paste it to the Propforth Blinker.f text file.
This can be pasted directly under the first line, following the mandatory fl. I prefer to define variables first and paste the PASM output under the variables. See the Blinker file below.

/ Forth Code proper for Blinker.f
/ =======================
fl

hex

variable datx
variable rendezvous

/ Code generated by the Propforth Assemble

163 wconstant v_adr
152 asmlabel a_tog
151 wconstant v_char
150 wconstant v_delay
14F wconstant v_pin
lockdict variable def_014F 0164 l, 014F l,
00000010 l, 02625400 l, 00000061 l, A0BE1DF0 l, 80FE1C40 l, A0FE1401 l, 2CBE154F l, A0BFED0A l, A0BE17F1 l, 80FE1680 l,
A0BE1951 l, A0FE1A1A l, F8BE1750 l, 7CBFE90A l, F8BE1750 l, 78BFE90A l, 083E190E l, 80FE1801 l, E4FE1B5B l, 5C7C0159 l,
00000002 l,
freedict

 \ Forth Code
\
: lasm \ expects an address pointing to a structure in the following form
4+ dup L@ swap \ empty long, upper address of assembler routine
4+ swap over L@ \ lower address of assembler routine
dup coghere W! \ series of longs of assembler code
do
   4+ dup L@ cog,
loop
drop
;

: start_blink
  par COG@ 40 + rendezvous L! \ just pass the char address to rendezvous
  def_014F lasm a_tog ; \ The dreaded linker and a_tog the entry point

: disp dup datx L@ <> if dup datx L! emit else drop then ; \ only display new characters

: blink c" start_blink" 4 cogx \ start the driver in cog 4
  begin rendezvous L@ W@ disp 0 until ; \ send the output to disp

 \ End of Blinker.f
\ ==============

The assemble output lists the cog addresses which are needed to link the driver to the Forth code.

The first word (definition) is 'lasm' . It is Propforths linker (for want of a better word). It's beyond the scope of this
littte HOW TO explain lasm. Just add the lasm definition to the file for now following the asm code, if you plan to try Proforth ASM

What is important to note that the variable def_14f and the entry point a_tog @ 0153, produced by the assembler are required by lasm to start the blinker driver. Look at start_blink to see how this all fits together.

The definition 'disp' echo the character to the console

Blink is the main routine, it starts the blinker driver and calls disp to display the char to the console.

        Starting from scratch
        ================

To use PF ASM you will need to load the PF4.6 spin file and reboot Propforth.

From the supplementary folder paste fs.f to the Propforth terminal window and run saveforth.

Enter fsclr, then from the supplementary folder, paste asm.f to the Proforth terminal window.

Reboot and enter fsls

You should see that asm.f is now included in the eeprom file system.

To test the assembler, reboot Propforth then enter fsload asm.f

Propforth will compile the assembler and will return Cog6 OK

Now Paste the Propforth ASM source, inside {} to the terminal window

The assemble will proceed to assemble the asm source and all being well, will generate
the code which is then pasted to the blink.f proper.

A final note on cutting and pasting your code for the PF ASM. Make sure you cut from the fl line to
one clear line below the word ;asm, otherwise the assembler will not generate an output.

        End of the Blurb
        =============

        Reserved for FAQs
        ==============